## Slide 1: First Path AWV issue
Date: 2019-04-15
Authors:

## Slide 2: Abstract
This document discusses issues with first path AWV FTM procedure and proposes solutions.

## Slide 3: Intent of First Path AWV
Setting the trigger in FTM request that initiates the FTM burst to 2 indicates that all transmissions in the burst will use first path AWV.
Problem:
  The transmission of the first burst after the request is not immediate.
  The FTM exchanges in the burst are separated by “long” periods that may be used for data transmissions. These periods are used for calculations needed to for the TOA results and formatting of the messages.
  The transmission of data frames does not use the first path AWV – it uses the best path AWV.
  The FTM exchanges come to the initiator with no preparation or warning from the initiator.
    The initiator is not ready with antenna setting of the first path AWV when the FTM frame is received.
    Even when no first path AWV is used, the initiator may be receiving in omni-RX mode in between the exchanges and the exchange may come as a surprise.

## Slide 4: Solution #1 – disallow other transmissions in an FTM burst
Due to the time the RSTA needs for calculations, especially when AOA is involved, this will create a lot of wasted air time for the devices involved.
especially the ISTA can’t do anything else.

## Slide 5: Solution #2 – Use RTS/CTS or CTS-to-self
Before every FTM exchange (FTM frame and returning ACK) there is a transmission of CTS-to-self that includes a control trailer (CT). The CT includes a field that indicate that following this transmission there is a transmission using first path AWV.
In the PHY header of the FTM and the ACK PPDUs there is a field used to indicate that this PPDU is transmitted using first path. This bit in the ACK is an acknowledgment that the FTM was received using first path AWV in the RX
This way the time between exchanges may be used for data transmissions

## Slide 6: Solution #3
No change in protocol.
The data part of the FTM and ACK frames is transmitted using Best path AWV
A TRN field is appended to the PPDU, transmitted and received using First Path AWV.
T2 and T3 are measured on the TRN field as in secure TRNs.
A field in the PPDU header is used to indicate the use of FIRST path AWV in the TRN field

## Slide 7: Summary
 | Solution Type | Pros | Cons
1 | Don’t use the time between the FTM exchanges for data transmissions | No apparent changes in spec text | Very inefficient, especially when used in AOA and AOD. Against the spirit of the text
2 | Adding CTS-to-Self with CT before any exchange | Allows data transmission between exchanges. Robust | Requires additional PPDU transmission per exchange
3 | Perform measurement on first path AWV only on the TRN | No change in protocol, similar to secure TRNs. Works well even if first path has low SNR | Change in the way FTM measurements are made. Aligns with secure TRNs

## Slide 8: Recommendation
Use solution 3 – First path AWV on TRN field

## Slide 9: References