## Slide 1: Performance evaluation of Mid-amble
Date: 2019-05-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo choi |  |  |  | js.choi@lge.com
May 2019

## Slide 2: Introduction
In the previous meeting, following two methods were introduced and each presentation had shown that they can mitigate the Doppler impact and prevent the degradation of performance due to Doppler.
  Mid-amble [1]
  DACE [2]
But, LDPC, which had been decided to support, did not apply to both presentations. [1][2]
So, in this presentation, we further investigate performance with LDPC for mid-amble and DACE.

## Slide 3: Considerations (1/2)
Since 11bd PPDU format was not defined yet, the simulation was simply conducted using following PPDU.
  11ac OFDM numerology downclocked by 2 for 10MHz PPDU
  Reused 11ac PPDU format except VHT-SIG fields
Reuse the VHT-LTF symbol as Mid-amble
  Mid-amble consists of only one VHT-LTF symbol.
  Mid-amble is inserted per M symbols periodically
LDPC
  We reuse the LDPC parameters described in 19.3.11.7.2 (LDPC coding rates and codeword block lengths) for evaluation.
L-STF
L-STF
L-SIG
VHT-STF
DATA
VHT-LTF

## Slide 4: Considerations (2/2)
DACE [3]
  We have considered that DACE operates in LDPC codeword units to apply the LDPC.
    Here, one LDPC codeword can be constructed with multiple symbols.

## Slide 5: Simulation parameters
Bandwidth : 10MHz
OFDM numerology:
  11ac 20MHz OFDM numerology downclocked by 2
Number of data bits: 300 Bytes
Coding : LDPC
MCS level : 2/4/6
Car2Car Doppler channel model
  Rural LoS, Highway LoS, Highway NLoS
  No Impairment
Channel tracking
  DACE
  Mid-amble
    Uses VHT- LTF for 11ac

## Slide 6: Performance
Rural LoS channel
  In MCS2 case,
    Midamble and DACE have a similar performance.
  But, in high MCS cases such as MCS4/6, Midamble has a better performance than DACE
    Midamble has a 2~4dB gain.
  Regardless of the period of Midamble, it has a similar performance on each MCS case.
    Possible to minimize the overhead by adopting a long period of Midamble

## Slide 7: Performance
Highway Los channel
  It shows a similar trend with a performance of Rural LoS channel.
    In all MCS cases, Midamble has a better performance than DACE.
  And, in MCS6 case,
    It has shown that increasing MP has a performance degradation but still has a 2 dB gain than DACE.

## Slide 8: Performance
Highway NLoS channel
  The Midamble has a better performance than DACE
    MCS2 - 2dB gain
    MCS4 - 4dB gain
    MP8 and MP10 can provide the adequate performance up to 16QAM.
  In MCS6 case,
    DACE can not meet the 10% PER.
    Only MP4 can meet the 10% PER.
      A short period of Midamble is required.

## Slide 9: Discussion (1/2)
In all channel environments, the results showed that Midamble has performance gain.
  We confirmed the 2~ 4dB gain.
    Due to error propagation according to re-generation and re-estimation of LDPC codeword unit, DACE has degradation of performance.
  Except the challengeable channel condition like Highway NLoS, we can satisfy the target PER (10%) by using the long period of Midamble.
    In channel environments such as Highway NLoS, applying of appropriate MCS should be considered to provide a stable performance.
      Within suitable MCSs (e.g., up to 16QAM), either MP8 or MP10 can be used for 11bd transmission.

## Slide 10: Discussion (2/2)
DACE requires the high computation complexity and large delay because it performs a number of re-operations such as encoding, decoding, and channel estimation.
  Also, due to an operation based on LDPC codeword, it can occur additional delay according to size of LDPC codeword which consist of a number of OFDM symbols.
On the other hand, because the known symbol is used for the Midamble, it can simply estimate the channel with LS estimate algorithm without high complexity and large delay.
  In addition, applying the long period of Midamble can minimize efficiency loss as described in appendix.

## Slide 11: Conclusion
In this contribution, we evaluated the performance of Midamble and DACE with LDPC.
  In C2C channel, Midamble has shown a better performance than DACE.
  Also, Midamble has relatively low complexity and low delay compare to DACE.
    Long period of Midamble can minimize the efficiency loss.
  To minimize the signaling overhead in 11bd, one period of Midamble is preferred.

## Slide 12: SP1
Do you agree to add the followings into section 3 of 11bd SFD
  11bd PPDU shall include Midamble(s) in Data field.
    Midamble is composed by long training field, with design TBD
    Midamble is inserted in every M OFDM symbols
      M is TBD.

## Slide 13: SP 2
Do you agree to add the following into section 3 of 11bd SFD ?
  11bd only defines one midamble periodicity .
  Y/N/A

## Slide 14: Reference
[1] IEEE 802.11-19-0332/r2 , PHY design for 11bd
[2] IEEE 802.11-19-0310/r0, Considerations on NGV PHY design
[3] “DATA DECODING AIDED CHANNEL ESTIMATION TECHNIQUES FOR OFDM SYSTEMS IN VEHICULAR ENVIRONMENT”, Andrea Agnoletto, 2010

## Slide 15: Appendix

## Slide 16: Efficiency of Midamble
Equation for calculation (assumption of 300byte transmission)
  Efficiency = 1-( N_midamble_sym/ Total_N_sym)
    Where,
      Total_N_sym = N_data_sym + N_midamble_sym
      N_data_sym = number of OFDM data symbol according to MCS level
      N_midamble_sym = number of total midamble symbol according to period
  MP = 4
  MP = 8
  MP = 10
MCS level | N_data_sym | N_midamble_sym | Total_N_sym | Efficiency
2 | 47 | 11 | 58 | 81.03
4 | 24 | 5 | 29 | 82.76
6 | 12 | 2 | 14 | 85.71
MCS level | N_data_sym | N_midamble_sym | Total_N_sym | Efficiency
2 | 47 | 5 | 52 | 90.38
4 | 24 | 2 | 26 | 92.31
6 | 12 | 1 | 13 | 92.31
MCS level | N_data_sym | N_midamble_sym | Total_N_sym | Efficiency
2 | 47 | 4 | 51 | 92.16
4 | 24 | 2 | 26 | 92.31
6 | 12 | 1 | 13 | 92.31