## Slide 1: Multi-Band Opinion
Date: 2019-05-08
Authors:

## Slide 2: Introduction
The multi-band operation has been discussed during the EHT discussion[1~9]
We propose a Joint MAC + multiple concurrent PHY architecture for multi-band operation. As compare to multiple concurrent devices(e.g. 2.4GHz+5GHz devices) case, this proposed architecture can
  Reduce worst case latency
  Still be backward compatible to legacy devices

## Slide 3: Joint MAC Multiple Concurrent PHY
Assumption: multiple PHY can operate concurrently in different channel(band)
Each packet can TX/RX from one of the allowed channel(s)
  each packet can has different allowed channel(s)
Example of the key concept:
  A packet that is allowed to be transmitted in channel 1 or channel 2, and this packet is prepared in both queuing lists of channel 1 and channel 2
  If this packet is transmitted via one of the channel (e.g. channel 1), then remove this packet from the other queuing list (channel 2)

## Slide 4: Example (1/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
Simple TX example, no aggregation, non-QoS
Two PHYs, one is in channel 1, the other one is in channel 2
All packets are allowed to be transmitted by any PHY
The incoming packets are prepared in both queuing lists
...
...
...

## Slide 5: Example (2/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
If channel 1 acquires the TX opportunity, then packet A is transmitted via channel 1(shown in RED) and it is removed from channel 2 queuing list
If channel 2 acquires the TX opportunity, then packet B is transmitted via channel 2 and it is removed from channel 1 queuing list
...
...
...

## Slide 6: Example (3/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
If channel 1 is blocked temporarily for some reason, the packets can still be transmitted via channel 2
In this scenario, the traffic assigned in channel 1 might have worst case latency using current method
This proposal can reduce the worst case latency
...
...
...

## Slide 7: Example (4/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
E
Channel 2 queuing list
If packet C and D are allowed to be transmitted via channel 1 only, they will only be prepared in the channel 1 queuing list
The traffic to a legacy device is allowed in its operating channel only
...
...
...

## Slide 8: Conclusion
We propose a novel joint MAC and multiple concurrent PHY architecture and use a simple example to present this concept
Next step: more factors need to be considered, e.g. aggregation, QoS, security, re-transmission, …etc.

## Slide 9: References
[1] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[2] 802.11-18/1161r0 EHT Technology Candidate Discussions
[3] 802.11-18/1171r0 View on EHT Objectives and Technologies
[4] 802.11-18/1518r0 EHT Multi-Channel Operation
[5] 802.11-18/1525r1 EHT features for Multi-Band Operation
[6] 802.11-18/1908r0 Overview of Full Duplex over
Multi- Band (FD-MB) for EHT
[7] 802.11-19/108r1 Discussion on Multi-Band for EHT
[8] 802.11-19/367r0 Performance on Multi-band Operation
[9] 802.11-19/360r0 MAC Architectures for EHT Multi-band Operation