## Slide 1: Multi-Band Opinion
Date: 2019-05-09
Authors:

## Slide 2: Introduction
The multi-band operation has been discussed during the EHT discussion[1~9]
We propose a Joint MAC + multiple concurrent PHY architecture for multi-band operation. As compare to multiple concurrent devices(e.g. 2.4GHz+5GHz devices) case, this proposed architecture can
  Reduce worst case latency
  Still be backward compatible to legacy devices

## Slide 3: Our Thought of Multiple Links System
Ch1 and Ch2 are different channels that can be in the same or different bands, e.g. one is in 2.4GHz and the other is in 5GHz
The traffic is put into the queue and use all or part of the available channels to send
AP
STA
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
Joint MAC or Unified MAC

## Slide 4: Joint MAC Multiple Concurrent PHY
Assumption: multiple PHY can operate concurrently in different channel(band)
Each packet can TX/RX from one of the allowed channel(s)
  each packet can has different allowed channel(s)
Example of the key concept:
  A packet that is allowed to be transmitted in channel 1 or channel 2, and this packet is prepared in both queuing lists of channel 1 and channel 2
  If this packet is transmitted via one of the channel (e.g. channel 1), then remove this packet from the other queuing list (channel 2)

## Slide 5: Example (1/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
Simple TX example, no aggregation, non-QoS
Two PHYs, one is in channel 1, the other one is in channel 2
All packets are allowed to be transmitted by any PHY
The incoming packets are prepared in both queuing lists
...
...
...
Memory
Descriptors

## Slide 6: Example (2/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
If channel 1 acquires the TX opportunity, then packet A is transmitted via channel 1(shown in RED) and it is removed from channel 2 queuing list
If channel 2 acquires the TX opportunity, then packet B is transmitted via channel 2 and it is removed from channel 1 queuing list
...
...
...
Memory
Descriptors

## Slide 7: Example (3/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
C
D
E
Channel 2 queuing list
If channel 1 is blocked temporarily for some reason, the packets can still be transmitted via channel 2
In this scenario, the traffic assigned in channel 1 might have worst case latency using current method
This proposal can reduce the worst case latency
...
...
...
Memory
Descriptors

## Slide 8: Example (4/)
A
B
C
D
E
Incoming data
A
B
C
D
E
Channel 1 queuing list
A
B
E
Channel 2 queuing list
If packet C and D are allowed to be transmitted via channel 1 only, they will only be prepared in the channel 1 queuing list
The traffic to a legacy device is allowed in its operating channel only
...
...
...
Memory
Descriptors

## Slide 9: Conclusion
We propose a novel joint MAC and multiple concurrent PHY architecture and use a simple example to present this concept
Next step: more factors need to be considered, e.g. aggregation, QoS, security, re-transmission, …etc.

## Slide 10: References
[1] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[2] 802.11-18/1161r0 EHT Technology Candidate Discussions
[3] 802.11-18/1171r0 View on EHT Objectives and Technologies
[4] 802.11-18/1518r0 EHT Multi-Channel Operation
[5] 802.11-18/1525r1 EHT features for Multi-Band Operation
[6] 802.11-18/1908r0 Overview of Full Duplex over
Multi- Band (FD-MB) for EHT
[7] 802.11-19/108r1 Discussion on Multi-Band for EHT
[8] 802.11-19/367r0 Performance on Multi-band Operation
[9] 802.11-19/360r0 MAC Architectures for EHT Multi-band Operation

## Slide 11: Backup Slides

## Slide 12: Centralized Queuing List (1/)
Ch1 and Ch2 are different channels that can be in the same or different bands, e.g. one is in 2.4GHz and the other is in 5GHz
The traffic is put into the centralized queue and use all or part of the available channels to send
AP
STA
MAC
LMAC
MAC
LMAC
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
Joint MAC or Unified MAC

## Slide 13: Centralized Queuing
A
B
C
D
E
Incoming data
Packets A, B, E are allowed to be transmitted via both channels
Packet C and D are allowed to be transmitted via channel 1 only
...
...
Memory
Descriptors
A(1,2)
B(1,2)
C(1)
D(1)
E(1,2)
Centralized queuing list

## Slide 14: Centralized vs. Parallelized Queuing
A
B
C
D
E
Channel 1 queuing list
A
B
E
Channel 2 queuing list
Packets A, B, E are allowed to be transmitted via both channels
Packet C and D are allowed to be transmitted via channel 1 only
...
...
Dispatch
...
Descriptors
A(1,2)
B(1,2)
C(1)
D(1)
E(1,2)
Centralized queuing list
Removal module to remove the redundant queuing list after transmission