## Slide 1: Multi-link Operation Framework
Date: 2019-07-01
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Robert Stacey |  |  |  | 
Dan Bravo |  |  |  | 
Arik Klein |  |  |  | 
Carlos Cordeiro |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Multi-link operation has been discussed in [2-6] for the use cases of load balancing [2,4] and aggregation [3-6]
The presentation provides the follow up for multi-link operation

## Slide 3: Terminology Recap [2,4]
Extremely efficient multi-link operation calls for a new definition of multi-link logical entity with one or more affiliated STAs
  The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
  Multi-link AP logical entity: A multi-link logical entity, where each affiliated STA is an AP.
  Multi-link non-AP logical entity: A multi-link logical entity, where each STA is a non-AP STA.
This definition keeps within the current 802.11 architecture and definition of STA and link

## Slide 4: Terminology Recap [2]
Example 1 Example 2
Multi-link AP logical entity/Multi-link non-AP logical entity has an address to communicate to DSM, which may not be the address used on each WM

## Slide 5: Steering/load balancing Use Case under the Framework [2]
TBD Mechanism

## Slide 6: Aggregation Use case under the Framework [2]
TBD Mechanism

## Slide 7: Multi-link Setup
Traditionally, single link setup is achieved through the functionality of association.
  Executed over one link initiated by a non-AP STA with an AP
  Capability for one birdirectional link can be exchanged during the association
  The AP serves as the interface to the distribution system (DS) for the non-AP STA after successful association
For Multi-link setup, an “association” like multi-link setup signaling exchange is needed
  Executed over one link initiated by a multi-link non-AP logical entity with a multi-link AP logical entity
  Capability for one or more bidirectional links can be exchanged during the multi-link setup
  The multi-link AP logical entity serves as the interface to the distribution system (DS) for the multi-link non-AP logical entity after successful multi-link setup

## Slide 8: Illustration of Single Link Association
AP1 operating
on 2.4 GHz
Non-AP STA1
Association Request frame with capability of non-AP STA1
Association Response frame for with capability of AP1, configuration of link 1

## Slide 9: Illustration of Multi-link Setup
AP1 operating
on 2.4 GHz
Non-AP STA1
Request frame for multi-link setup with capability of non-AP STA1/2/3
Response frame for multi-link setup with capability of AP1/2/3, configuration of link 1/2/3

## Slide 10: Enable Link
After single link association, the link used for association singling exchange is enabled for class 2 and class 3 frame exchange (see Figure 11-16 [7])
For multi-link setup, due to the nature of multiple links, different simultaneous operation capability, power save consideration, there is a need to
  Define a mechanism to determine, during or after successful completion of multi-link setup, which bidirectional link(s) is(are) enabled for class 2 and class 3 frame exchange after multi-link setup
  A identification for each link may be needed, but details are TBD

## Slide 11: Multi-link Capability
Simultaneous operation across links provides gains but also corresponding hardware investment
We envision that the benefits multi-link operation can be enjoyed by a range of devices that support various capability of simultaneous operation across links
To achieve this goal,
  A multi-link logical entity can indicate capability to support exchanging frames simultaneously on a set of affiliated STAs

## Slide 12: Conclusion
We provide multi-link operation follow up to propose a unified framework that addresses the key use cases (load balancing and aggergation) and keeps within the current 802.11 architecture and definition
  Multi-link logical entity, Multi-link AP logical entity, and Multi-link non-AP logical entity are defined
We propose to define multi-link setup, which is analogous to single-link association
We propose to define multi-link capability indication, which enables multi-link operation for a wide range of devices

## Slide 13: Straw Poll #1 - Terminology
Do you support the following definition:
  Multi-link logical entity: A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
  Multi-link AP logical entity: A multi-link logical entity, where each STA within the multi-link logical entity is an AP.
  Multi-link non-AP logical entity: A multi-link logical entity, where each STA within the multi-link logical entity is a non-AP STA.
  NOTE –A Multi-link logical entity allows STAs within the multi-link logical entity to have the same MAC address
  NOTE – The exact name can be changed

## Slide 14: Straw Poll #2 – Multi-link Setup
Do you support the following:
  Define a multi-link setup signaling exchange executed over one link initiated by a multi-link non-AP logical entity with a multi-link AP logical entity as follows:
    Capability for one or more bidirectional links can be exchanged during the multi-link setup
    The multi-link AP logical entity serves as the interface to the distribution system (DS) for the multi-link non-AP logical entity after successful multi-link setup
  Define a mechanism to determine, during or after successful completion of multi-link setup, which bidirectional link(s) is(are) enabled for class 2 and class 3 frame exchange after multi-link setup
  NOTE - The link identification is TBD
  NOTE – Details for non-infrastructure mode of operation TBD

## Slide 15: Straw Poll #3 – Multi-link Capability
Do you support that a multi-link logical entity can indicate capability to support exchanging frames simultaneously on a set of affiliated STAs?

## Slide 16: Reference
[1] 11-18/1231r4 EHT draft proposed PAR
[2] 11-19/0822r0 Extremely Efficient Multi-band Operation
[3] 11-19/0731r0 Multi-link Operation
[4] 11-19/0823r0 Multi-Link Aggregation
[5] 11-19/0766r1 Enhanced Multi-band/Multi-channel Operation
[6] 11-19/0821r0 Multiple Band Operation Discussion
[7] Draft P802.11REVmd D2.2