## Slide 1: Performance Investigation on Multi-AP Transmission
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Sunwoong Yun |  |  |  | sunwoong.yun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
As one of the potential technologies for 11be, multi-AP coordination has been proposed in a bunch of contributions [1]-[11]
In this presentation, we investigate DL performance for various schemes including multi-AP as well as single-AP transmissions
The following two cases are considered and, in each case, the benefit of each scheme is verified
  Case 1: All distances between STAs and APs are the same
  Case 2: In each STA, distance from one AP is fixed but that from the other AP varies

## Slide 3: Case 1 (1/3)
We compare the following two schemes in DL MU MIMO
  Joint transmission (JTX)
    2 APs, each with 4 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    Dd = Di
  Single-AP transmission (STX)
    1 AP with 8 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    D = Dd = Di
Synchronization procedure
Data sharing
CSI sharing
CSI for all links

## Slide 4: Case 1 (2/3)
Simulation environments
  Band: 5GHz
  Bandwidth: 80MHz
  PPDU: HE PPDU with 4x+3.2us LTF and 3.2us GI
  Channel Coding: LDPC
  Channel model: Channel D, NLoS
  Feedback: (7,5) for compressed beamforming
  Channel estimation: least square
  Transmit power: 21dBm per AP
  Impairments: no CFO, no SFO, no TO, perfect sync between APs
  Pathloss model [12]
    PL(d) = 40.05 + 20*log10(fc/2.4) + 20*log10(min(d,10)) + (d>10) * 35*log10(d/10)

## Slide 5: Case 1 (3/3)
Performance
  Tput* : max. throughput per STA only considering the data part
    I.e., not consider MAC overhead and PHY preamble overhead
  JTX has a better performance than STX
    Note that we assume perfect synchronization between APs, and thus, to guarantee this performance, JTX needs a complex procedure for synchronization
    We need to further check on the performance considering various impairments that may degrade the performance of JTX
*Tput = maxMCS(Data_rate(MCS)*(1-PER(MCS,Distance)))

## Slide 6: Case 2 (1/4)
We compare the following three schemes
  JTX
  Coordinated beamforming (CBF)
  Non-coordinated transmission (non-CTX)
  In all schemes, we consider
    2 APs, each with 4 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    Dd < Di
Synchronization procedure
Data sharing
CSI sharing
CSI for desired and interference links
Associated STA’s data
CSI for a desired link
Associated STA’s data

## Slide 7: Case 2 (2/4)
Performance
  Simulation parameters are the same as in slide 4
<Dd = 10m>
<Dd = 20m>

## Slide 8: Case 2 (3/4)
Overall, JTX has a good performance
  As Di increases, throughput slightly decreases due to the received signal power reduction
  In the region with quite long Di, the received signal power from the link of Di may be negligible, and thus, JTX may become similar to a single AP transmission
  However, in most of the region, EHT can benefit from utilizing JTX
  For further study, we need to investigate how slight offsets (CFO, SFO, etc.) affect the performance of JTX

## Slide 9: Case 2 (4/4)
As for the non-data sharing cases, CBF has a nearly constant performance regardless of Di while the performance for non-CTX enhances as Di grows
  In the region with Dd ≈ Di (interference limited region / BSS edge), interference power is too high, and thus, interference nulling is essential
    In this region, CBF has a better performance than non-CTX but it doesn’t seem to approach JTX due to the dimension reduction by the nulling procedure
    Note that, to utilize CBF, antenna dimension should be guaranteed for interference nulling
    In terms of synchronization, CBF is less complex than JTX
  In the region with Dd << Di (noise limited region / BSS center), interference power is negligible, and thus, interference nulling is unnecessary
    In this region, non-CTX has a better performance than CBF and its performance even approaches that of JTX since, in this region, JTX is similar to a single AP transmission

## Slide 10: Conclusion
Overall, JTX provides performance gain compared to other schemes at the expense of complexity
In the interference limited region, CBF has a better performance than non-CTX
In the noise limited region, non-CTX offers a sufficient performance
As a next step, we need to further investigate the performance on JTX under various impairments

## Slide 11: References
[1] 802.11-18/1461r1 Discussions on the PHY features for EHT
[2] 802.11-18/1547r0 Technology Features for 802.11 EHT
[3] 802.11-18/1575r0 Further Study on Potential EHT Features
[4] 802.11-18/1116r0 Distributed MU-MIMO and HARQ Support for EHT
[5] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[6] 802.11-18/1161r0 EHT Technology Candidate Discussions
[7] 802.11-18/1439r0 Constrained Distributed MU-MIMO
[8] 802.11-18/1509r0 Discussions on Multi-AP Coordination
[9] 802.11-18/1510r1 AP Coordinated Beamforming for EHT
[10] 802.11-18/1533r0 View on EHT Candidate Features
[11] 802.11-18/1576r1 Considerations on AP Coordination
[12] 802.11-14/980r16 Simulation Scenarios

## Slide 12: Appendix
Additional Performance Results for Case 2
<Dd = 40m>