## Slide 1: Performance Investigation on Multi-AP Transmission
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
As one of the potential technologies for 11be, multi-AP coordination has been proposed in a bunch of contributions [1]-[11]
In this presentation, we investigate DL performance for various schemes including multi-AP as well as single-AP transmissions
The following two cases are considered and, in each case, the benefit of each scheme is verified
  Case 1: All distances between STAs and APs are the same
  Case 2: In each STA, distance from one AP is fixed but that from the other AP varies

## Slide 3: Case 1 (1/3)
We compare the following two schemes in DL MU MIMO
  Joint transmission (JTX)
    2 APs, each with 4 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    Dd = Di
  Single-AP transmission (STX)
    1 AP with 8 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    D = Dd = Di
Synchronization procedure
Data sharing
CSI sharing
CSI for all links

## Slide 4: Case 1 (2/3)
Simulation environments
  Band: 5GHz
  Bandwidth: 80MHz
  PPDU: HE PPDU with 4x+3.2us LTF and 3.2us GI
  Channel Coding: LDPC
  Channel model: Channel D, NLoS
  Feedback: (7,5) for compressed beamforming
  Channel estimation: least square
  Transmit power: 21dBm per AP
  Synchronization (residual CFO) in JTX: 0Hz for both APs (JTX w/ 0Hz) / +10Hz for AP 1 and -10Hz for AP 2 (JTX w/ 10Hz)
    [12] verified that predicting actual CFO within accuracy of 10Hz is feasible
  Pathloss model [13]
    PL(d) = 40.05 + 20*log10(fc/2.4) + 20*log10(min(d,10)) + (d>10) * 35*log10(d/10)

## Slide 5: Case 1 (3/3)
Performance
  Tput* : max. throughput per STA only considering the data part
    I.e., not consider MAC overhead and PHY preamble overhead
  JTX has a better performance than STX even under imperfect synchronization between APs
  JTX w/ 10Hz has a similar performance with JTX w/ 0Hz
    At a short distance region (high Tput region), JTX w/ 10Hz has a slightly worse performance since high MCSs (e.g., MCS 11) are more affected by the synchronization accuracy between APs
*Tput = maxMCS(Data_rate(MCS)*(1-PER(MCS,Distance)))

## Slide 6: Case 2 (1/4)
We compare the following three schemes
  JTX
  Coordinated beamforming (CBF)
  Non-coordinated transmission (non-CTX)
  In all schemes, we consider
    2 APs, each with 4 antennas
    2 STAs, each with 2 antennas
    2 SS per each STA
    Dd < Di
Synchronization procedure
Data sharing
CSI sharing
CSI for desired and interference links
Associated STA’s data
CSI for a desired link
Associated STA’s data

## Slide 7: Case 2 (2/4)
Performance
  Simulation parameters are the same as in slide 4
<Dd = 10m>
<Dd = 20m>

## Slide 8: Case 2 (3/4)
Overall, JTX has a good performance even with ±10Hz of a residual CFO at APs
  As Di increases, the received signal power reduces, and consequently, in the region with quite long Di, the received signal power from the link of Di may become negligible, and thus, JTX becomes similar to a single AP transmission
  However, we can see no throughput degradation in the region with Di shorter than 100m at least, and thus, in this region, EHT can benefit from utilizing JTX
  In addition to the residual CFO effect, we may need to further consider other impairment factors such as transmission timing and phase differences between APs to evaluate the JTX performance

## Slide 9: Case 2 (4/4)
As for the non-data sharing cases, CBF has a nearly constant performance except for a short Di region while the performance for non-CTX enhances as Di grows
  In the region with Dd ≈ Di (interference limited region), interference power is too high, and thus, interference nulling is essential
    In this region, CBF has a better performance than non-CTX but it doesn’t approach JTX
    Note that, to utilize CBF, antenna dimension should be guaranteed for interference nulling, and as a result, a sophisticated scheduling method is essential to a reliable performance
    In terms of hardware complexity, CBF doesn’t need a synchronization procedure, and thus, it may be less complex than JTX
  In the region with Dd << Di (noise limited region), interference power is negligible, and thus, interference nulling is unnecessary
    In this region, non-CTX has a better performance than CBF and its performance may approach that of JTX when Di becomes a quite large value

## Slide 10: Conclusion
JTX provides a better performance gain compared to other schemes at the expense of complexity for synchronization
  Various impairment factors for synchronization may need to be further considered
In the interference limited region, CBF has a better performance than non-CTX but its performance couldn’t reach that of JTX
  In order to find an efficient region for CBF, we may need to further consider various factors such as scheduling issues, hardware complexity as well as performance
In the noise limited region, non-CTX offers a good performance but it is hard to always guarantee a low interference level favorable to non-CTX especially in a dense environment
  To mitigate the interference, we can consider coordinated methods such as frequency/time allocation, SR, etc.

## Slide 11: References
[1] 802.11-18/1461r1 Discussions on the PHY features for EHT
[2] 802.11-18/1547r0 Technology Features for 802.11 EHT
[3] 802.11-18/1575r0 Further Study on Potential EHT Features
[4] 802.11-18/1116r0 Distributed MU-MIMO and HARQ Support for EHT
[5] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[6] 802.11-18/1161r0 EHT Technology Candidate Discussions
[7] 802.11-18/1439r0 Constrained Distributed MU-MIMO
[8] 802.11-18/1509r0 Discussions on Multi-AP Coordination
[9] 802.11-18/1510r1 AP Coordinated Beamforming for EHT
[10] 802.11-18/1533r0 View on EHT Candidate Features
[11] 802.11-18/1576r1 Considerations on AP Coordination
[12] 802.11-19/799r0 Comparison of Coordinated BF and Nulling with JT
[13] 802.11-14/980r16 Simulation Scenarios

## Slide 12: Appendix
Additional Performance Results for Case 2
<Dd = 40m>