## Slide 1: Considerations on feedback overhead
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Sunwoong Yun | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sunwoong.yun@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
  Support for 16 spatial streams has been discussed as a candidate feature for 802.11be.
If 802.11be agree to support 16 spatial streams, we need to consider large amount of sounding and feedback information because of the increase in total number of spatial streams.
At last F2F meeting, [1] introduced many kinds of feedback methods to reduce the overhead of channel acquisition.
In this contribution, we discuss more details about amount of feedback information.

## Slide 3: Explicit feedback beamforming
  In this contribution, we analyze the amount of feedback information of overall feedback method defined in existing 802.11 system.
  In explicit beamforming, in order for STA A to transmit a beamformed packet to STA B, STA B measures the channel matrices and sends STA A either the effective channel Heff, or the beamforming feedback matrix Vk, for STA A to determine a steering matrix.
    In CSI matrices feedback, each feedback matrix is encoded using 3 + 2 x Nb x Nr x Nc(Nb = 4, 5, 6 or 8)
    In non-compressed beamforming, each feedback matrix is encoded using 2 x Nb x Nr x Nc(Nb = 2, 4, 6 or 8)
    In compressed beamforming, each feedback matrix is compressed using Na x (b_phi+b_psi)/2

## Slide 4: The amount of feedback information
  If 11be support 16 spatial streams, the dimension of effective channel matrix and beamforming matrix can increase up to 16.
  As the dimension increases up to 16, the amount of feedback information also increases.
  In case of CSI matrices feedback and non-compressed beamforming feedback, the amount of feedback information mainly increases with increasing Nr x Nc
  In compressed beamforming, the amount of increasing feedback information is significantly lower than above two cases because of Na.
    Na (The number of angles used for beamforming matrix) is not proportional to Nr x Nc.

## Slide 5: The amount of feedback information
  In this slide, we calculate total number of feedback bits for CSI feedback, non-compressed beamforming feedback and compressed beamforming feedback.
  Assumption
    80MHz
    Grouping factor Ng = 4 (Nsd = 250), Ng = 16(Nsd = 64)
    Nb = 6 for CSI matrices feedback and non-compressed beamforming feedback
    For compressed beamforming feedback
      (B_phi, B_psi) = (6, 4) for SU, (7, 5) for MU
      Na for 9x9 ~ 16x16 are defined in appendix
    We compare total number of feedback bits in case of 8x8 matrix to in case of 16x16 matrix

## Slide 6: The amount of feedback information
  CSI feedback (3+2*Nb*Nr*Nc bits per subcarrier)
    8x8  (3 + 2*6*8*8) * Nsd(250) = 192,750 bits
    16x16 (3+2*6*16*16) * Nsd = 768,750 bits
  Non compressed feedback(3+2*Nb*Nr*Nc bits per subcarrier)
    8x8  (2*6*8*8) * Nsd = 192,000 bits
    16x16 (2*6*16*16) * Nsd = 768,000 bits
  Compressed feedback (Na*(b_phi+b_psi)/2 bits per subcarrier)
    8x8  (56 * (6+4)/2) * Nsd = 70,000 bits
    16x16 (240* (6+4)/2) * Nsd = 300,000 bits
  Since 11ac, 11ax exploit only compressed beamforming feedback method, in following slides, we focus on compressed beamforming and calculate TX time takes to transmit feedback frame.

## Slide 7: TX time calculation
  We calculate how much time takes to send feedback information in compressed beamforming feedback.
  Tx time calculation
     Legacy + RL_SIG + HE-SIGA + HE_STF + HE_LTF + FeedbackData
    TX time is mainly affected by MCS and Nss of feedback frame.
    Considering unreliable Wi-Fi channel characteristics, it may not be easy to assume that the feedback frame is transmitted in high MCS and NSS and it is necessary to select reliable parameter.
    TX time calculation results for 16x16 and 8x8 are as follow[usec]
16x16 | NSS = 1 | 2
MCS =0 | 8375.2 | 4220
1 | 4213.6 | 2139.2
2 | 2826.4 | 1445.6
3 | 2132.8 | 1092
4 | 1439.2 | 752.00
8x8 | NSS = 1 | 2
MCS =0 | 1983.20 | 1024.00
1 | 1017.60 | 534.400
2 | 691.200 | 371.200
3 | 528 | 289.600
4 | 364.800 | 208

## Slide 8: TX time calculation
  In MU case that will be practically considered in 16ss, total number of feedback bits can increase more.
  For example, if we consider 2 cases as below,
    AP with 16 antennas, (B_phi, B_psi) = (7, 5) for MU
    8 STAs (2 antennas per each STA)
      Each user has 16 x 2 beamforming matrix
      87,000 feedback bits per each user  Total : 696,000 bits
    4 STAs (4 antennas per each STA)
      Each user has 16 x 4 beamforming matrix
      162,000 feedback bits per each user  Total : 648,000 bits
    Total TX time for 8 STAs and 4 STAs are shown in the right table.
  Compared to SU case(300,000bits for 16 x16) , the number of MU feedback bits are more than twice and total TX time also increases almost twice.
16x2, 8 STAs | NSS = 1 | 2
MCS =0 | 16,121.6 | 8409.6
1 | 8358.4 | 4384.0
2 | 5747.2 | 3078.4
3 | 3249.6 | 2425.6
4 | 3027.2 | 1329.6
16x4, 4 STAs | NSS = 1 | 2
MCS =0 | 15168.0 | 7686.4
1 | 7660.8 | 3932.8
2 | 5158.4 | 2681.6
3 | 3907.2 | 2083.2
4 | 2656 | 1430.4

## Slide 9: Need for feedback overhead reduction
  In PAR document, many kinds of low latency applications are introduced such as virtual reality or augmented reality, gaming, remote office and cloud computing.
    Latency lower than 5ms for real-time gaming.
    In [2], latency for VR application should be less than 5~10ms.
    The increasing amount of feedback information may not meet low latency requirement.
  Multi-AP has been discussed as a candidate feature for 11be.
    For multi-AP coordination, need to acquire channel information between slave APs and STAs.
    In this procedure, the amount of feedback information may increase since a STA have to send feedback to each of the APs.
  For 11be’s use cases and candidate features, feedback overhead reduction is required.

## Slide 10: Candidate methods for overhead reduction
Differential feedback
    Feed back angle difference (Psi, phi) of Given’s rotation.
    Differential feedback method may reduce feedback overhead.
Unequal quantization
    In conventional method, Given’s angle is quantized evenly.
    Depending on the channel state, unequal quantization may be effective solution.
Codebook
    Widely used in cellular network.
    Performance analysis is needed compared to conventional method.

## Slide 11: Conclusion
In this contribution, we calculate the amount of feedback information and TX time assuming support up to 16 spatial streams.
    If feedback frame is transmitted with reasonable MCS and Nss for reliability, it takes much time to transmit feedback frame and may not meet low latency requirement of VR, AR.
Moreover, in case of multi-AP scenario, more feedback information is required.
Based on above reasons, we need to investigate feedback overhead reduction methods.

## Slide 12: References
[1] IEEE 802.11-19/0391r0 Feedback Overhead Reduction in 802.11be (Interdigital)
[2] IEEE 802.11.18/1954r2 EHT Use Case Discussion: VR Requirement Follow Up (Huawei)

## Slide 13: Appendix

## Slide 14: Na (The number of angles used for compressed beamforming feedback matrix)
Nc Nr | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
2 | 2 | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 | 4 | 6 | 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | 6 | 10 | 12 | 12 |  |  |  |  |  |  |  |  |  |  |  | 
5 | 8 | 14 | 18 | 20 | 20 |  |  |  |  |  |  |  |  |  |  | 
6 | 10 | 18 | 24 | 28 | 30 | 30 |  |  |  |  |  |  |  |  |  | 
7 | 12 | 22 | 30 | 36 | 40 | 42 | 42 |  |  |  |  |  |  |  |  | 
8 | 14 | 26 | 36 | 44 | 50 | 54 | 56 | 56 |  |  |  |  |  |  |  | 
9 | 16 | 30 | 42 | 52 | 60 | 66 | 70 | 72 | 72 |  |  |  |  |  |  | 
10 | 18 | 34 | 48 | 60 | 70 | 78 | 84 | 88 | 90 | 90 |  |  |  |  |  | 
11 | 20 | 38 | 54 | 68 | 80 | 90 | 98 | 104 | 108 | 110 | 110 |  |  |  |  | 
12 | 22 | 42 | 60 | 76 | 90 | 102 | 112 | 120 | 126 | 130 | 132 | 132 |  |  |  | 
13 | 24 | 46 | 66 | 84 | 100 | 114 | 126 | 136 | 144 | 150 | 154 | 156 | 156 |  |  | 
14 | 26 | 50 | 72 | 92 | 110 | 126 | 140 | 152 | 162 | 170 | 176 | 180 | 182 | 182 |  | 
15 | 28 | 54 | 78 | 100 | 120 | 138 | 154 | 168 | 180 | 190 | 198 | 204 | 208 | 210 | 210 | 
16 | 30 | 58 | 84 | 108 | 130 | 150 | 168 | 184 | 198 | 210 | 220 | 228 | 234 | 238 | 240 | 240