## Slide 1: Discussion on 6 GHz Band Support
Date: 2019-5-13
Authors:
Name | Company | Address | Phone | Email
Yusuke Tanaka | Sony Corporation |  |  | Yusuke.YT.Tanaka@sony.com
Sho Furuichi |  |  |  | Sho.Furuichi@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com
Ryuichi Hirata |  |  |  | Ryuichi.Hirata@sony.com
Naotaka Sato |  |  |  | naotaka.sato@ieee.org
Chen Sun |  |  |  | Chen.Sun@sony.com
William Carney |  |  |  | William.Carney@sony.com

## Slide 2: Introduction
6 GHz band (5,925 – 7,125 MHz (US) / 5,925 – 6,425 MHz (EU)) is now under regulatory discussion to opening up for Wireless Access System including Radio LAN (WAS/RLAN).
Availability of a large swath of spectrum (1,200 MHz bandwidth in US) will be of great benefit to IEEE P802.11be:
  Contiguous 320 MHz bandwidth possible
  Potential for Multi-Band Operation and Aggregation (e.g. 5 + 6 GHz)
To develop functionalities to use 6 GHz band will be necessary to achieve “a maximum throughput of at least 30 Gbps” that is a main scope of TGbe [1].

## Slide 3: Reality of 6 GHz Availability
There exist licensed incumbent systems.
  Fixed Systems (FS), Fixed Satellite Systems (FSS) (earth-to-space)
Wireless LAN will be required to operate on a secondary basis, therefore it must not cause harmful interference to those licensed incumbent systems.
  Incumbent protection requirements will likely be imposed by national regulatory authorities (not only FCC but also the others).
The requirements to protect licensed incumbent systems will impact the availability of the full 6 GHz band. That is, entire 6 GHz band will not necessarily be available to wireless LAN.

## Slide 4: The Proposed Rules as of May 2019
Notice of Proposed Rulemaking (NPRM) issued by FCC [2]:
  15.403 (b): Automated Frequency Coordination (AFC) is a system that automatically determines and provides lists of which frequencies are available for use by access points operating in the 5.925-6.425 GHz and 6.525-6.875 GHz bands.
  15.407 (d)(3): Operation in the 6.425-6.525 GHz and 6.875-7.125 GHz bands is limited to indoor locations.
  15.407 (k)(1): Access points operating in the 5.925-6.425 GHz and 6.525-6.875 GHz bands shall access an AFC system to determine the available frequencies at their geographic coordinates prior to transmitting. Access points may transmit only on frequencies indicated as being available by an AFC system.
U-NII-5
U-NII
-6
U-NII-7
U-NII-8
5,925
6,425
6,525
6,875
7,125
Freq [MHz]
500 MHz
100 MHz
350 MHz
250 MHz
Database required
Low power and indoor devices only

## Slide 5: Observations from the Proposed Rules
Only 29% of 6 GHz band is available without database access.
Contiguous 320 MHz is unavailable without database access.
Utilization of Non-contiguous 320 MHz operation is limited.
  A combination of 5 GHz band + U-NII-8 only (e.g. 160 MHz + 160 MHz).
  This will cause congestion in U-NII-8 band, that leads inefficient utilization of U-NII-8 band and non-contiguous 320 MHz operation.

## Slide 6: Consequences for the TGbe Spec Development
TGbe needs to consider and develop a specification to utilize the entirety of the 6 GHz band.
  This is a key requirement to achieve “a maximum throughput of at least 30 Gbps” that is a main scope of TGbe, and also realize “320MHz bandwidth and more efficient utilization of non-contiguous spectrum” that is a candidate technology of TGbe.
If not considered or defined in 11be:
  71% of 6 GHz band cannot be utilized.
  Contiguous 320 MHz operation cannot be supported in 11be.
  Non-contiguous 320 MHz operation will be inefficient.

## Slide 7: TGbe Potential Focus Areas for Complete 6 GHz Band Support
Develop database access (AFC) capability as one of 11be key functionalities.
Development or enhancement of Interface (SAP), Primitive and Entity necessary for database access.
Frame exchange to indicate available channels, maximum allowable transmission power, etc. which are authorized by database.
  Up to the final rules.

## Slide 8: Proposed Way Forward
Reuse of defined functionalities in IEEE 802.11af (WLAN for TVWS, a part of IEEE 802.11-2016).
  11af = 11n/ac PHY/MAC + Operation under GDB
  11be = new PHY/MAC + Amendment of Operation under GDB
Merits of this approach
  TGbe can develop both 1) the new PHY/MAC and 2) operation under 6 GHz database access in parallel.
  Parallel development of PHY/MAC specification and database amendment accommodates the current regulatory uncertainties and may be faster than creating new database specification from scratch.
  TGbe can continue developing PHY/MAC even if some regulatory authorities do not adopt database access for 6 GHz use.

## Slide 9: Conclusion
To develop functionalities for 6 GHz band will be a key requirement to achieve “maximum throughput of at least 30 Gbps” that is a main scope of TGbe [1].
TGbe should consider database access as one of these 11be functionalities so that it can globally achieve 30 Gbps where permitted.
TGbe should consider:
  Interface (SAP), Primitive, Entity
  Frame exchange to available channels, maximum allowable transmission power, etc.
  Reuse and enhancement of “Operation under GDB” defined for 11af

## Slide 10: Reference
[1] 11-18-1231-01-0eht-eht-draft-proposed-par
[2] FCC 18-147, “Notice of Proposed Rulemaking”, ET Docket No. 18-295 Unlicensed Use of the 6 GHz Band, October 24, 2018

## Slide 11: Straw Poll 1a & 1b
SP1a: Do you think that 11be should support the entirety of the 6 GHz bands presently under rulemaking?
  Yes
  No
  Need more information
SP1b: Do you think that 11be will need to provide AFC/database functionalities for operation in 6 GHz?
  Yes
  No
  Need more information

## Slide 12: Straw Poll 2
Do you think that “operation under GDB” defined in subclause 11.44 of IEEE 802.11-2016 is a potential baseline reference for the development of a database access specification in 6 GHz for TGbe?
  Yes
  No
  Need more information