## Slide 1: Expected Total System Architecture
Date: 2019-05-13
Authors:

## Slide 2: Abstract
This presentation describes an expected total system architecture including higher layer for eBCS DL use cases.

## Slide 3: Purpose
To get consensus of the group to consider each function of eBCS.

## Slide 4: Devices
Servers: Distribute contents by IP multicast.
APs: eBCS APs that transmit eBCS frames.
STAs: eBCS STAs that receive eBCS frames and provide contents to users.
Server
AP
AP
STA
AP
AP
AP
Server
Server
STA
STA
STA
STA

## Slide 5: Contents
Each contents is a stream of packets
  Live streaming
  A set of files (contents that is changed low frequency)
    Serialized and divided into a stream of packets
Each contents has its own identifier
Live Streaming
File 1
File 2
File 3
Set of Files
Serialize
Divide
Packets

## Slide 6: Server
Distribute contents by IP multicast.
If a content is a set of files, the server repeats to transmit the set of packets that are generated by the previously described method.
A server may provide redundancy such as inter-packet LDPC.
A server may distribute multiple contents.
A server should advertise contents information such as contents identifier.

## Slide 7: eBCS AP
An eBCS AP receives contents stream and transmits them by eBCS protocol.
An eBCS AP may receives multiple contents streams from single or multiple servers and transmits them.
An eBCS AP should advertise contents information such as contents identifier.
AP
Multicast Frames
eBCS Frames
Multicast Frames
Multicast Frames
Server
Server
Server

## Slide 8: eBCS STA
An eBCS STA receives eBCS frames and reconstruct contents from the frames.
An eBCS STA may show contents to user(s).
An eBCS STA should provide a function that the user can select the contents to be shown.
An eBCS STA may receives the same contents from multiple eBCS APs.
An eBCS STA may receives multiple contents from single/multiple eBCS APs.

## Slide 9: Comments & Questions