## Slide 1: Ranging Performance in 11bd
Date: 2019-05-06
      May 2019

## Slide 2: Introduction
TGaz developed a ranging protocol [1]
  Reuse 11ac/ax channel sounding frame i.e. null data packet (NDP)
  Utilize round trip time (RTT) for range estimation
  Higher bandwidth and multiple antennas provide high accuracy
  Mainly for indoor scenarios
Vehicular ranging/positioning is a promising use case for 11bd
  Especially when there is no/limited GPS coverage
  ~Meter accuracy is required
This submission investigates the ranging performance for 11bd
  Assume NDP based channel sounding
  Car-to-Car (C2C) channel model (10MHz and 20MHz bandwidths)
      May 2019

## Slide 3: 11az Ranging Sequence
11az supports non-trigger based (NTB) and trigger based (TB) ranging sequences
  NTB for responding STA (RSTA) to a single initiating STA (ISTA) ranging
  TB for RSTA to multiple ISTAs ranging
An example of NTB ranging sequence is shown below
NDP
Announcement
SIFS
ISTA
RSTA
SIFS
SIFS
UL NDP
DL NDP
Location
Measurement report
      May 2019

## Slide 4: RTT Calculation
Time stamps of UL NDP and DL NDP
After ISTA receives Location Measurement Report (LMR), RTT is derived as
RTT = t4 – t1 – (t3 – t2)
Range is calculated as
R = RTT*c/2, where c is the speed of light
RSTA
ISTA
UL NDP
DL NDP
t1 (ToD)
t2 (ToA)
t3 (ToD)
t4 (ToA)
NDPA
LMR (t2, t3)
      May 2019

## Slide 5: Ranging in 11bd
Two vehicles can use RTT-based method to estimate range
  Exchange DL and UL PPDUs
  Channel estimation based on UL/DL PPDU
  ToA estimation based on frequency domain channel estimation
  Use ToA and ToD for RTT calculation
11bd supports 20MHz bandwidth PPDU
  Higher ToA estimation accuracy than 10MHz bandwidth
      May 2019

## Slide 6: Two Channel Models
  C2C channel model is friendly to ToA estimation
  Small number of multipath taps
  First tap is separated from the other taps by dozens of nanoseconds or hundred nanoseconds
  Interference from the other taps is small
TGnF channel model is unfriendly to ToA estimation
  Large number of multipath taps
  Multipaths come in cluster
  First tap follows by other taps
  Interference from other taps is large
      May 2019

## Slide 7: C2C Channel Model
  Following C2C models are proposed for 11bd [2]:
Table 1: Rural LOS Parameters
Table 2: Urban Approaching LOS Parameters
      May 2019

## Slide 8: C2C Channel Model (cont’d)
Table 4: Highway LOS Parameters
Table 5: Highway NLOS Parameters
Table 3: Urban Crossing NLOS Parameters
      May 2019

## Slide 9: TGnF Channel Model
 | Tap1 | Tap2 | Tap3 | Tap4 | Tap5 | Tap6 | Tap7 | Tap8 | Tap9
Power | -3.4 | -3.7 | -4.0 | -4.2 | 0 | -0.9 | -1.7 | -2.6 | -1.5
Delay | 0 | 10 | 20 | 30 | 50 | 80 | 110 | 140 | 180
Tap10 | Tap11 | Tap12 | Tap13 | Tap14 | Tap15 | Tap16 | Tap17 | Tap18 | Units
-3.0 | -4.2 | -5.8 | -5.2 | -7.9 | -9.5 | -13.0 | -16.3 | -21.2 | dB
230 | 280 | 330 | 400 | 490 | 600 | 730 | 800 | 1050 | ns
TGnF model is defined for large space environments(indoor and outdoor). [3]
      May 2019

## Slide 10: Simulation
Simulation parameters
  Single Tx/Rx chain
  20MHz bandwidths, 128 tones (with 6 DC and edge tones)
  Interpolation for DC tone
  No RF impairment
  Select Table 2: Urban Approaching LOS Parameters for evaluation
  Pure Doppler method is utilized for modelling Doppler [4]
  MUSIC algorithm for ToA estimation [5, 6]
  Evaluate ToA error over 10000 channel realizations
  Compare performance under different channel models
      May 2019

## Slide 11: Results for 10MHz C2C
      May 2019

## Slide 12: Results for 20MHz C2C
      May 2019

## Slide 13: Results for 20MHz TGnF
      May 2019

## Slide 14: Remarks
  Ranging accuracies are 10x different between the two channel models
  The accuracy is affected by the spacing between channel taps
  Active channel taps within the transceiver sampling time i.e. 50 or 100 ns interfere with each other in the ranging estimation
C2C model has widely spaced taps e.g. >80 ns apart while TGnF has tightly clustered taps
V2V measurements [7] demonstrated the clustered arrival of multipaths
      May 2019

## Slide 15: Conclusions
Ranging performance for 11bd is investigated using 10 and 20 MHz bandwidths
The ranging accuracy is sensitive to channel model. Namely, the results are 10x different between the two channel models
  Sub-meter accuracy is achievable under C2C model
  Accuracy under TGnF model i.e. > 10 meters error
  For ranging evaluations, channel model with clustered multipath such as TGnF should be considered
      May 2019

## Slide 16: Reference
[1] IEEE 802.11az Draft 1.0
[2] IEEE 802.11-18/0858 C2C Channel Model Overview
[3] IEEE 802.11-03/0940 TGn Channel Models
[4] IEEE 802.11-19/0017 Simulation of NGV Channel Models
[5] R. O. Schmidt, “Multiple Emitter Location and Signal Parameter Estimation”, IEEE Trans. Antennas Propagat., vol. AP34, no. 3, pp. 276-280, Mar. 1986
[6] X. Li and K. Pahlavan, “Super-Resolution ToA Estimation With Diversity for Indoor Geolocation”, IEEE Trans. Wireless Comm., vol. 3, no. 1, pp. 224-234, Jan. 2004
[7] IEEE 802.11-19/0034 Considerations on Vehicular Channel Models
      May 2019