## Slide 1: HARQ Framing
Date: 2019-07-14
Authors:
Name | Affiliation | Address | Email
Imran Latif | Quantenna Communications | 1704 Automation Parkway, 95131, San Jose, CA, USA | ilatif@quantenna.com
Sigurd Schelstraete |  |  | sschelstraete@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com
Jul, 2019

## Slide 2: Background
Hybrid-ARQ is one of the candidate features for TGbe
How and at what layer HARQ will be supported needs to be better understood
There are intertwined aspects of the PHY and MAC which need to be understood better for HARQ support
Therefore, in this presentation we discuss granularity at which HARQ can be supported and what changes would be necessary at the PHY and MAC layer
Jul, 2019

## Slide 3: HARQ Support
HARQ granularity, theoretically, it can be supported at
  A-MPDU level
  MPDU level
  Codeword level
HARQ “Feedback” about the status of data decoding from RX to TX is extremely important and it should be supported on
  MPDU level (currently supported through MPDU BA feedback)
  Codeword level
ARQ support: in current release (11ax) MPDU retransmissions are supported but these retransmissions are not fit for HARQ type of combining at the RX (elaborated in next few slides)
Jul, 2019

## Slide 4: HARQ at A-MPDU Level
If and when the whole A-MPDU is to be retransmitted, MAC prepares the A-MPDU to be retransmitted
However, retransmitted A-MPDU usually has changes as compared to the original transmission because of:
  Arbitrary numbers of delimiters (DL) among the MPDUs
  Each MPDU Header’s flipped retry bit
  Different Cipher Text
  Different CRC bits
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
MPDU Header
Ext-IV
Cipher Text
MIC
CRC
DL (Delimiter)
Pre-FEC Padding
Jul, 2019

## Slide 5: HARQ at A-MPDU Level
These changes in A-MPDU results in different payload at PHY
AT PHY there is no knowledge of MPDUs and this payload is transformed into codewords (CW) for transmission
However, the CWs generated for retransmission will definitely be different than the CWs corresponding to the original transmission
Thus, due to these few different bits in the MAC payload combining of LLRs at the PHY layer on the RX will not be possible
Thus, not only HARQ at A-MPDU level is extremely in-efficient in terms of resource usage, without changes, it is not even possible to combine the retransmitted A-MPDU with previous A-MPDU
What changes are to made for making it work?
  Retransmit the same A-MPDU as from the original transmission?
    Needs changes at MAC – not desirable
Jul, 2019

## Slide 6: HARQ at MPDU Level
Next we discuss the HARQ at MPDU level
As is evident from A-MPDU case that MPDU level retransmissions would also not work in their current form in the standard
Consider the following example of an A-MPDU which has 4 MPDUs
  Suppose MPDU-2 was not decoded correctly and needs to be retransmitted
MPDU BA based feedback informs the TX that MPDU-2 is not decoded
First of all it can be observed that the failed MPDU can span multiple CWs (partially and completely).
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
Jul, 2019

## Slide 7: HARQ at MPDU Level
Failed MPDU at the RX has two partial CWs and two complete codewords
At the TX side this failed MPDU will be mapped onto different CWs and each CW will have different FEC padding
This causes the misalignment in the failed and retransmitted MPDU’s CWs
Failed MPDU
…
CW-4
CW-5
Failed MPDU
…
CW-1
CW-2
CW-3
At the RX
At the Tx for Retransmission
Due to this misalignment, codeword combining at physical layer is not possible
Other than misalignment issue, the failed MPDU will have following bits different in the next transmission,
  Retry bit
  Cipher text
  CRC bits
Therefore, due to the different bits at the input of the FEC encoder, the coded bits in the CWs would also be different
Thus these CWs cannot be combined at LLR level at the RX side
Jul, 2019

## Slide 8: HARQ at MPDU Level
Though HARQ support at MPDU level is desired, however, due to the reasons mentioned previously, it is not possible in the current form of the 802.11 standard
Due to the different payload (even few bits) in each MPDU, the contents of the CWs will change, thus no combining
Furthermore, due to the misalignment in the MPDU to CW mapping between first transmission and the retransmissions, it is still not possible to combine LLRs for MPDU level HARQ
Since there is no knowledge of MPDUs at the PHY so even PHY level retransmission (without packing of MAC) is not possible
Even if SAME MPDU is to be sent over medium, due to the possible misalignment in the CWs, partial CW combining won’t be possible at the RX
Jul, 2019

## Slide 9: HARQ at CW Level
As seen so far, that MAC level packing is problematic for HARQ
HARQ from pure PHY seems the way forward
However, in current form there is no support of PHY level retransmission as well
Lets consider the CW level retransmission for HARQ and see what kind of changes would be required in 11be
Jul, 2019

## Slide 10: HARQ at CW Level
Codeword level HARQ requires that RX at the PHY should know that it has received an erroneous codeword so that it can use this knowledge for combining of the retransmitted CWs
However, PHY at the RX does not have any CRC, but it can use LDPC Parity Check to see if it needs to store this codeword or not.
Additionally, the MAC layer can inform the PHY by checking CRC about the status of MPDUs and PHY can associate failed CWs to MPDUs
RX then needs to send back the feedback about failed CWs to the TX
Tx would needs to store the original payload at PHY level and it will need to retransmit only the codewords which are asked for in the feedback
To do this, we present two solutions in this contribution
Jul, 2019

## Slide 11: Solution 1: 2-tier HARQ
Let’s take the same example as before, MPDU – 2 decoding failed
In this case the RX sets up a HARQ session between TX and RX by asking for CW-3 to CW-6 in the retransmission
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
RX does that by sending a CW level feedback to the TX
A prior is that TX needs to store the CWs at the PHY level
On reception of the CW level feedback, TX packs only the CW-3 to 6 in a dedicated retransmission packet and sends this to the RX
RX receives these CWs and combines them with previous codewords and forwards the (if all correctly) decoded bitstream to the MAC
The MAC performs the CRC check and terminates the HARQ session by sending MPDU level feedback to the TX
CW-4
CW-5
CW-6
CW-3
Retransmission
Jul, 2019

## Slide 12: Solution 1: 2-tier HARQ
In this case the HARQ session remains active for as long as the RX decides to keep it active
To terminate the session the RX sends back the legacy MPDU block acknowledgement
This whole process is shown below
TX
RX
Time
Original PPDU Tx
PHY CW NACK (1st NACK)
PHY CW Retrans PPDU (1st retry)
PHY CW NACK (n_th NACK)
PHY CW Retrans PPDU (n_th retry)
…
ACK/BA (MPDUL level acknowledgement)
Codeword NACK & Retransmit
Jul, 2019
Notes: Transmitter is expected to receive either Codeword NACK or MPDU level ACK/BA.
  If it received MAC ACK/BA, then it concludes both HARQ and MPDU level acknowledgment process.
  If it received Codeword NACK, then it should pack the codewords requested in the Codeword NACK into one or more ACTION_NO_ACK frames to send to the receiver
The receiver and the transmitter can exchange multiple rounds of Codeword NACK and retransmitting procedure
The Receiver finally sends out ACK/BA to conclude both the HARQ Codeword and MPDU level acknowledgment

## Slide 13: Solution 1: 2-tier HARQ
Receiver initiates an HARQ session for each transmission until it is either successful or reaches maximum HARQ retransmissions (not discussed here)
This requires the HARQ session to be finished before a new transmission can be started on the medium
Though this is simple and straight forward to implement (with minimum changes in transmitter and receiver side)
  It can be very in-efficient as the medium stays busy for longer time
  No other transmission can be combined with the retransmission
Jul, 2019

## Slide 14: Solution 2: Efficient 2-tier HARQ
Lets take the same example as before, MPDU 2 failed and it is encompassing CW 3 – 6
The bitstream at the output of the decoder is presented to the MAC for parsing.
This includes identifying subframe delimiters and verifying the CRCs of any subframes that are found in this way.
This allows the MAC to determine that MPDUs 1, 3 and 4 were received correctly.
At the same time, the PHY can identify the locations of the codewords that were not decoded correctly (invalid parity).
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
Jul, 2019

## Slide 15: Solution 2: Efficient 2-tier HARQ
The information from MAC (MPDU) and PHY (codewords) can now be combined into a single ACK that acknowledges reception of MPDU 1, 3 and 4 and requests retransmission of codewords 3 to 6
Such a dual feedback is more efficient than creating an HARQ session and multiple compression schemes can be applied on codeword level feedback (The compression schemes are not discussed here)
TX
RX
Time
Original PPDU Tx
MPDU+CW Feedback
2-tier Feedback
MPDU BA bit mask
Codeword level Feedback
Jul, 2019

## Slide 16: Solution 2: Efficient 2-tier HARQ
On receiving the dual feedback from RX , the TX gets the knowledge that it has to prepend codewords 3-6 with the new A-MPDU packet
The MAC prepares the full AMPDU with new MPDUs (5 – 7 in the example below)
MAC sends the AMPDU to PHY
PHY prepends CW 3-6 to AMPDU
Then the combined transmission happens as shown below
PHY level Retransmission
MPDU-5
MPDU-6
MPDU-7
…
…
CW-4
CW-5
CW-6
CW-12
CW-13
CW-14
CW-15
CW-16
CW-17
CW-18
CW-19
CW-3
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
Jul, 2019

## Slide 17: Solution 2: Efficient 2-tier HARQ
However, the boundary between the retransmitted codewords and the new payload needs to be signaled to the PHY
To convey this information, we propose to add a new SIG field in the PHY which shall provide minimum information required to RX for combining the required CWs
On reception of retransmitted data, the PHY combines the retransmitted codewords with the bit positions known to be in error in the previous payload
L-STF
L-LTF
L-SIG
…
HARQ-SIG
DATA
Legacy Preamble
HARQ Control Information
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
CW-4
CW-5
CW-6
CW-3
+
Jul, 2019

## Slide 18: Solution 2: Efficient 2-tier HARQ
RX only combines the previously stored CWs and tries to decode the full payload
Assume that with the retransmission the decoding was successful for previously failed MPDU, i.e., codewords 3 to 6 and new payload
Then the decoded bit stream is again presented to the MAC for parsing
The MAC now determines that in addition to the MPDUs 1, 3 and 4, also MPDU 2 is correctly received.
At the same time, RX MAC will also parse the new payload containing MPDUs 5 to 7.
  If we assume all of these are correct, the receiver can send a “traditional” ACK for all MPDUs
  If some MPDUS and CW are not decoded correctly, then RX can send again 2-tier feedback and TX can combine the failed CWs with new transmission containing fresh payload as well
Jul, 2019

## Slide 19: Solution 2: Efficient 2-tier HARQ
This approach is spectrally efficient and does not need to setup any HARQ session
Its independent to HARQ scheme
  It can support both CC and IR HARQ (single bit signaling, details not discussed here)
It can pack retransmissions with new data
Due to the introduction of SIG field (which can be pre-coded) it can also support MU operations (OFDMA and/or MU MIMO)
Changes required for 11be as compared to 11ax:
  TX side PHY layer payload to be stored
  New HARQ SIG field (design can be optimized)
  RX side:
    parity check operation for CWs
    2-tier feedback support
Jul, 2019

## Slide 20: Summary
We have discussed the Framing for HARQ
We have shown HARQ can be implemented on various layers
We presented issues with some of these implementations and possible solutions to those problems
We showed that CW level HARQ is a natural fit for HARQ in 11be
We presented two CW level HARQ solutions
  A simple approach of codeword NACK and retransmission will work, but it is less efficient
  For efficiency and high performance, efficient 2-tier HARQ seems suitable
Jul, 2019
Notes: MAC level protp