## Slide 1: 3GPP RAN1 status on NR-Unlicensed
Date: 2019-05-16
Authors:
Name | Affiliations | Address | Phone | email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari | Broadcom |  |  | shubhodeep.adhikari@broadcom.com

## Slide 2: Abstract
This presentation provides updates from the latest 3GPP RAN1 meetings (RAN1#96b and RAN1#97) on the standardization of NR-Unlicensed, with a focus on fair coexistence with 802.11.

## Slide 3: Outline
The presentation discusses status of the following topics:
Reply to LS from IEEE 802.11 on the use of no/short LBT
LBT for transmission of DL control messages
LBT for UCI-only PUSCH transmissions
LBT for DL transmissions containing only UL grants
LBT for a 16us gap after a DL transmission and before a UL transmission in a gNB-acquired COT
Supported sub-slot PDSCH durations
CW adaptation mechanisms
Multi-carrier channel access schemes
Common preamble between NR-U and Wi-Fi in 5 GHz and 6 GHz.

## Slide 4: Reply to LS from IEEE 802.11 on the use of no/short LBT
The LS from IEEE 802.11 to 3GPP RAN1 had raised concerns on NR-U employing the following:
Transmission of DRS by the gNB up to 5% of the time when the total duration of such transmissions is up to 1 ms
Transmissions by UEs for Random Access, HARQ-ACK, Scheduling Request, Channel State Information, etc.
The response contained in R1-1905860 says the following (the original proposal supported by many companies had omitted the highlighted details which now can be used as the topic for further LS exchanges):
NR-U uses short LBT to transmit DRS alone or multiplexed with non-unicast data (e.g. OSI, paging, RAR) if the DRS length is up to 1ms and the DRS is transmitted no more than 5% of the time. NR-U DRS may have different signals/channels than LAA DRS.
Other proposals to use short LBT for transmissions other than the types of DRS transmissions mentioned above were not approved by RAN1, although it is expected that transmission with short LBT might be allowed for some NR-U carriers in a similar way that it is allowed for LTE-LAA with type B channel access procedure for transmissions on multiple carriers.
Regarding the request for 3GPP RAN1 to consider supporting the proposal in ETSI BRAN to ban the use of no LBT and restrict the use of short LBT (to about 1%), the RAN1 view is that the clause 4.2.7.3.3 in EN 301 893 is used by LTE-LAA, even though a short LBT is additionally applied. There is no consensus on supporting the proposal to ban the use of no LBT and restrict the use of short LBT (to about 1%).

## Slide 5: LBT for transmission of DL control messages
Agreed:
DRS alone or multiplexed with non-unicast data (e.g. OSI, paging, RAR)
  When the DRS duty cycle ≤1/20, and the total duration is up to 1 ms: 25 µs Cat 2 LBT is used (as in LAA)
    The maximum DRS transmission window duration is 5 ms. The maximum number of candidate SSB positions within a DRS transmission window, Y, is selected as Y = 10 for 15 kHz SCS and Y = 20 for 30 kHz SCS.
    The number of starting points for DRS transmissions with the 5 ms window that can use a Cat. 2 LBT is to be discussed further as part of channel access discussions.
  When DRS duty cycle is > 1/20, or total duration > 1 ms: Cat4 with any channel access priority class value can be used
DRS multiplexed with unicast data
  Channel access priority class is selected according to the multiplexed data

## Slide 6: LBT for UCI-only PUSCH transmissions
Agreed:
For a UCI-only transmission on PUSCH in a channel occupancy initiated by the UE, Cat4 with lowest channel access priority class value can be used by the UE

## Slide 7: LBT for DL transmissions containing only UL grants
Proposed by Ericsson (R1-1907454):
When a gNB transmission includes only control signals/channels/information without any user plane data, the priority class value for accessing the channel is up to gNB.
The proposal affects the channel access mechanism indirectly used by the UEs which will share the COT initiated by the gNB while sending the grants. It is based on an incorrect statement “In LAA, the choice of LBT priority class for grant-only transmissions, i.e. PDCCH only, is up to eNB” noted in the above contribution.
In LAA, it has been ensured that for grant-only transmissions, the priority class is based on the data that is expected to be transmitted. The only agreement was “UL grant only transmission by eNB based on Rel-13 Cat-4 LBT priority class is supported” which is valid along with another agreement: “When the UE performs 25 microsecond LBT on an LAA SCell,
  There is no additional restriction at the UE (other than the multiplexing rules defined in RAN2) on the type of the traffic that can be carried in the scheduled subframes.
  eNB shall not schedule the UE more subframes than the minimum necessary to transmit all the traffic corresponding to the same LBT priority class or lower (i.e., with a lower number in the LBT priority class table) than the LBT priority class used by the eNB based on the DL traffic and the latest BSR and received UL traffic from the UE.
  The eNB is responsible for making sure that the mapping between QCI and LBT priority class is consistent with section 5.7.1 in TS 36.300.
      The eNB is expected to take the QCI with the lowest priority in the logical channel group into account when defining the LBT priority class for a logical channel group”
Broadcom proposes the same mechanism as in LAA for grant-only transmissions.

## Slide 8: LBT for a 16us gap after a DL transmission and before a UL transmission in a gNB-initiated COT
Agreed:
For LBT by a UE prior to transmission of a UL burst within a gNB-initiated channel occupancy as an LBE device, for gap durations shorter than 25 microseconds, Cat 2 LBT can be indicated (FFS: explicit and/or implicit) to the UE if the gap is 16 microseconds (allowing for implementation tolerances)
Select one of the following alternatives for Cat2 LBT in a 16 us gap.
  Alt 1: The 16us measurement period is split into two slots with the first slot having a duration 7us and second slot having a duration of 9us.
    Energy measurement is done in the 9us slot with the measurement including averaging for at least 4 us in any portion of the slot. LBT is said to be successful if the measured energy is lower than the ED threshold.
  Alt 2: The 16us measurement period is split into two slots with the first slot having a duration 7us and second slot having a duration of 9us.
    Energy measurement is done in both the 7us and 9us slot with the measurement including averaging for at least 4 us in any portion of each slot. LBT is said to be successful if the measured energy is lower than the ED threshold in both slots.
  Alt 3: Energy measurement is done in any portion of the 16 us duration including averaging for at least 4 us. LBT is said to be successful if the measured energy is lower than the ED threshold.
Alt 2 is Broadcom's proposal and it aligns most closely in performance to what is done in 11ax

## Slide 9: Supported sub-slot PDSCH durations
Agreed:
Durations from 2 to 13 symbols are supported
Capability signaling will be defined for UEs to indicate which specific subset of durations are supported by the UE
This helps to significantly reduce transmission of reservation signals by NR-U.

## Slide 10: CW adaptation mechanisms
Proposal that has been developed in an offline of the ongoing RAN1#97 meeting
The following alternatives have been identified for a definition of reference slot for CWS adjustment
  Alt 1: reference slot for CWS update for PDSCH/PUSCH is defined as
    the n first slots of the most recent transmission on the LBT subband made by gNB or UE, for which at least some HARQ-ACK feedback is expected to be available
    FFS: value of n
  Alt 2: reference slot for CWS update for PDSCH/PUSCH is defined as
    the n first slots of the most recent transmission on the LBT subband made by gNB or UE
    FFS: value of n
Alt 2 is Broadcom proposal to align the behavior with the ETSI BRAN regulations

## Slide 11: Multi-carrier channel access schemes
Agreed:
Multi-carrier channel access schemes that are applicable to multiple carriers with a single LBT sub-band per carrier that is the same as the carrier bandwidth are also applicable to multiple LBT sub-bands within a carrier when such carriers are used either as a single wideband carrier or as part of carrier aggregation of a set of carriers.

## Slide 12: Common preamble between NR-U and Wi-Fi
Both RAN1 WG and TSG-RAN have extensively discussed coexistence aspects, but did not find consensus for adopting a preamble for NR-U. As a consequence, and in accordance with the workplan outlined in the NR-U Work Item //add link//, RAN1 WG will not address proposals any further on adopting a preamble for NR-U.
- Nevertheless, TSG-RAN is open for further discussions on a common preamble for 6GHz at its next meeting (3-6 June), and will check whether member company views have shifted towards a consensus.