## Slide 1: Comparison of Digital Signature with TESLA
Date: 2019-06-11
Authors:

## Slide 2: Abstract
This presentation describes a performance comparison of Digital Signature with TESLA related to a proposal for eBCS frame authentication (11-19/451).

## Slide 3: Introduction
In May meeting, there was a question why TESLA was required.
Although I have explained that the processing time of Digital Signature is too long for low end (low computational power) devices, quantitative evaluation was lacked.
So this presentation shows a quantitative evaluation of Digital Signature and TESLA.

## Slide 4: Assumed Algorithm
Digital Signature
  RSA 2048 bit
    Fastest verification algorithm
TESLA
  HMAC-SHA256
  HMAC-SHA3-256

## Slide 5: Authenticator Size
Digital Signature requires 256 octets to authenticate.
TESLA requires 32 octets to authenticate in both HMAC-SHA256 and HMAC-SHA3-256.
If the size of each payload is 1,500 bytes, the ratio of the authenticator to the payload is following.
  Digital Signature: 17%
  TESLA: 2%
The size of the authenticator affects frame size and airtime occupation.

## Slide 6: Processing Time
 | RSA 2048 Sign | RSA 2048 Verify | HMAC-SHA256 (ratio to RSA 2408 Verify) | HMAC-SHA3-256 (ratio to RSA 2408 Verify)
Intel Core i7-5557U 3.1GHz (Ubuntu) | 1,680 us | 70 us | 5 us (7.1%) | 8 us (11%)
ARM1176JZF-S 1GHz (Raspbian, Raspberri Pi Zero W) | 122,045 us | 3,602 us | 219 us (6.1%) | 395 us (11%)
ARM Cortex-A7 1.1GHz (Android) | 94,073 us | 2,460 us | (172 us) expected | (271 us) expected

## Slide 7: Conclusion
TESLA requires 32 octets authenticator compared with 256 octets Digital Signature.
Digital Signature verification requires 14 times the processing time of TESLA HMAC-SHA256.
Digital Signature verification requires 9 times the processing time of TESLA HMAC-SHA3-256.
Combination of Digital Signature and TESLA is better than Digital Signature only frame authentication mechanism.

## Slide 8: Comments & Questions