## Slide 1: SIG-A Changes for Ranging NDP
Date: 2019-06-12
Authors:

## Slide 2: Problem in SIG-A with Ranging NDP
Repetition of HE-LTFs
  Pre-11az STAs will decode LSIG length
  Compare with NSTS in SIG-A
  Interpret extra HE-LTFs as Data field
  Will also affect 11ax based sniffers
Desirable to have 11az Wave 1 devices with minimal PHY changes
  Will potentially ignore NDPs with repeated HE-LTFs
  Re-use current P-matrix for decoding
  Not easy to link PHY processing to parameters received in NDP-A

## Slide 3: Match Existing P-Matrix
Use current P-matrix for decoding
  Secure LTF needs multiple channel estimates for detecting attacker
  Non-secure only wants averaged results to reduce noise
Treat repetition as partial “bigger P-matrix”
  P-matrix removal implicitly calculates average
  Lower memory needs
  Avoid new implementation
Example is N_STS=2, N_REP=2
  Use first two columns of 4x4 P-matrix
  If apply full 4x4 P-matrix, two “zero channels”

## Slide 4: Solution
Modify SIG-A NSTS
  Include repetitions of non-secure HE-LTFs in SIG-A NSTS
  Non-secure HE-LTFs can be limited to 8 to fit SIG-A NSTS subfield
    Typically used for 1x1 and 2x2 STAs to improve SNR
    If repetition is a 2-power, fits P matrix
  Simply change interpretation
    Instead of thinking of a N_STS=2 with LTF_REP=2 of two 2x2 P-matrices stacked
    Interpret as first two columns of 4x4 P-matrix
    N_STS=4 with zero power on 3rd and 4th stream
    Still “correct” use of NSTS subfield by 11ax standard

## Slide 5: Additional Enhancements
Most subfields in HE SIG-A not used in HE NDPs
  Could reuse some subfields to explicitly encode
    True N_STS
    LTF_REP
  HESIGA1
    MCS: B3:B6 (4bits)
    DCM: B7
  HESIGA2
    Coding: B7
    LDPC extra symbol: B8
    STBC: B9
    Pre-FEC Padding Factor: B11-B12 (2bits)
    PE Disambiguity: B13
    Doppler: B15

## Slide 6: Allowed Combinations of N_STS and LTF_REP
Possible cases:
  N_STS=1, Base P-matrix=1
    LTF_REP=1/2/4/6/8
    Final P-matrix=1/2/4/6/8
  N_STS=2, base P-matrix=2,
    LTF_REP=1/2/3/4
    Final P-matrix=2/4/6/8
  N_STS=3/4, base P-matrix=4
    LTF_REP=1/2
    Final P-matrix=4/8
P-matrix sizes 2/4/6/8
  N_STS=5/6, base P-matrix=6
    LTF_REP=1
    Final P-matrix=6
  N_STS=7/8, base P-matrix=8,
    LTF_REP=1
    Final P-matrix=8

## Slide 7: Strawpoll I
Do you support to limit the possible combinations of N_STS and LTF_REP in non-secure HE Ranging NPDs to the ones listed on slide 5?
Yes: No: Abstain:

## Slide 8: Strawpoll II
Do you support to change the NSTS encoding in HE SIG-A for HE Ranging NPDs, to include all non-secure HE-LTFs, including repeated HE-LTFs?
For example: a N_STS=2 and N_REP=2 would encode the NSTS subfield as if there were 4 spatial streams.
Yes: No: Abstain:

## Slide 9: Strawpoll III
Do you support to reuse some of the HE-SIG-A field in HE Ranging NDPs to encode the true N_STS and N_REP?
For example, use MCS, DCM, coding subfields.
Yes: No: Abstain: