## Slide 1: HARQ with A-MPDU in 11be
Date: 2019-07-10
Authors:

## Slide 2: Background
Various contributions on Hybrid Automatic Repeat Request (HARQ) have been presented in previous meetings [1-7]
In this contribution, we want to discuss some issues related to supporting HARQ in 802.11, in particular to the misalignment that can occur between an A-MPDU and the LDPC codewords
We then present some potential solutions for this misalignment issue, and discuss their pros and cons

## Slide 3: Existing Procedure
The 802.11 specs (and hence respective implementations) assume the following:
    The PHY receives a PSDU from the MAC layer and is not aware of the MPDU boundaries, their length, delimiters, etc.
    The FEC (LDPC) operates on blocks of information bits, regardless of MPDU boundaries
    A Block ACK (BA) indicates which MPDUs (within the A-MPDU) were decoded correctly, so retransmission occurs only for incorrectly decoded MPDUs

## Slide 4: A-MPDU and LDPC: Retransmissions
Assuming an A-MPDU was transmitted and some of the MPDUs were incorrectly decoded, the transmitter will have to retransmit only those MPDUs that failed
For example, in the figure, an A-MPDU containing 5 MPDUs (2000 bits each) is transmitted using coding rate 1/2, where the 2nd and 3rd MPDUs failed and need to be retransmitted
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
MPDU Boundary
FEC Boundary
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822

## Slide 5: A-MPDU and LDPC: Retransmissions
A retransmission of the failed MPDUs will include different coded bits due to a different setting of the scrambler + FEC, as shown here, so the LLRs cannot be combined
This is a major problem – reusing the existing (retransmission) mechanism, the LLRs respective to retransmitted coded bits cannot simply be combined with old LLRs, as there is no alignment between old and new codewords
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Retransmitted
Retransmitted
MPDU of size 2000 bits
FEC block
Different info bits at input to FEC, hence different coded bits at output
Padding 20 bits
FEC #1
Info: 804
Coded: 1612
FEC #2
Info: 804
Coded: 1613
FEC #3
Info: 804
Coded: 1613
FEC #4
Info: 804
Coded: 1613
FEC #5
Info: 804
Coded: 1613

## Slide 6: A-MPDU and LDPC: Impact on HARQ
The example in the previous two slides shows how the misalignment of the MPDUs and the LDPC codewords poses a problem for HARQ
  Furthermore, changing MCS between transmission and retransmissions is limited to the same coding rate, so that the same LDPC matrices are used
In the next slides, we look at several potential solutions to this misalignment issue
Our underlying assumption/motivation: we would like to maintain – where possible - the existing Block ACK mechanism as well as the existing LDPC design, so that there are minimal changes to existing designs and the protocol

## Slide 7: Potential Solution #1
The simplest solution is to retransmit the entire A-MPDU, regardless of which MPDU(s) failed
This is similar to LTE, where the entire Transport Block (TB) is retransmitted upon a failure
However, such a solution will typically lead to very high inefficiency
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822
Retransmitted
Retransmitted
Retransmitted
Retransmitted
Retransmitted

## Slide 8: Potential Solution #2
  In case of retransmission, transmit all bits/QAMs respective to FEC blocks that ‘contain’ failed MPDUs
  At the Rx, combine LLRs and discard of bits not part of MPDUs 2 and 3
  There is overhead due to ‘tail’ codewords (though for large MPDUs overhead can be small)
  In addition, PHY Tx needs to either maintain coded bits/QAMs in memory, or compute where to apply FEC encoder
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
MPDU of size 2000 bits
FEC block
Retransmitted
Retransmitted

## Slide 9: Potential Solution #3
  Pad an MPDU(s) to form an HARQ ‘Block’; LDPC is being applied within each HARQ ‘Block’ independent of other HARQ ‘Blocks’
  The size of such a ‘Block’ can be negotiated or pre-defined
  This solution is relatively simple
  However, it may incur overhead (padding towards HARQ ‘Block’ size)
  In addition, if small MPDUs are concatenated within a ‘Block’, a retransmission may contain MPDUs which didn’t fail
MPDU
FEC block
MPDU #1
Padding
Multiple LDPC codewords
HARQ Block #1
HARQ Block
MPDU #2
Padding
HARQ Block #2
Multiple LDPC codewords
MPDU #3
Padding
HARQ Block #3
Multiple LDPC codewords
failed
MPDU #2
padding
HARQ Block #2
Multiple LDPC codewords
MPDU #4
Retransmitted

## Slide 10: Conclusions
In order to support HARQ in 802.11be, one issue that needs to be solved is the (mis)alignment between LDPC codewords and MPDUs
We presented here several solutions for supporting HARQ while maintaining the existing LDPC and Block-ACK designs
More work is required in order to analyze all design implications and potentially consider other alternatives

## Slide 11: References
11-18-1587: HARQ for EHT, Sep. 2018
11-18-1955: HARQ for EHT – Further Information, Nov. 2018
11-18-1963: Discussion on HARQ for EHT, Nov. 2018
11-19-1992: HARQ Feasibility, Jan. 2019
11-19-2029: HARQ in EHT, Jan. 2019
11-19-1979: HARQ performance analysis, Jan. 2019
11-19-780: Consideration on HARQ, May 2019