## Slide 1: Medium Access with 20MHz BW
Date: 2019-07-01
Authors:

## Slide 2: Recap: >10MHz Operation in NGV Channels
11bd allows 20MHz transmission in two 10MHz channels that legacy 11p STAs and 11bd 10MHz STAs exist.
  The medium access procedure should be defined to allow such operation.
>20MHz operation in 2.4/5/6GHz bands
  One 20MHz primary channel is defined, other 20MHz channels of the BSS operating channel are secondary 20MHz channels
  The backoff and NAV operation are based on:
    The Duration detected in the PPDU that covers the primary 20MHz channel.
    The PHY CCA detection in the primary 20MHz channel.
  The busy/idle detection in 20MHz channels other than the primary 20MHz channel is based on idle/busy checking within PIFS before the transmission.

## Slide 3: Method 1: Primary 10MHz channel + Secondary 10MHz Channel
When the backoff in primary channel becomes 0 and the idle/busy checking in secondary 10MHz channel indicates idle within PIFS before the 20MHz transmission, the 20MHz PPDU can be transmitted.
  If 10MHz secondary channel is busy and the backoff counter becomes 0, 10MHz PPDU can be transmitted in primary 10MHz channel.
With this method, the transmission in secondary 10MHz channel may be ignored by 20MHz 11bd STA because of short CCA detection time, higher CCA level.
Primary 10MHz channel
secondary 10MHz channel
CCA idle with PIFS

## Slide 4: Method 2: NAV and CCA in Secondary 10MHz channel
A 20MHz STA does backoff and PHY CCA in primary 10MHz channel per the current 10MHz operation.
A 20MHz STA keeps monitoring the secondary 10MHz channel and updates its NAV when a PPDU covers the secondary 10MHz channel.
When the NAV timer of the secondary 10MHz channel doesn’t have non-zero value and PHY CCA per -82dbm indicates medium idle, the secondary channel can be used with the primary 10MHz channel (i.e. when the primary channel backoff timer becomes 0).
Primary 10MHz channel
secondary 10MHz channel
NAV timer in secondary channel has zero value and PHY CCA in secondary channel indicates idle medium.

## Slide 5: Method 3: Two Backoff Procedures
Each 10MHz channel has its own backoff procedure (method with two primary channels).
  When the backoff procedure in one 10MHz channel becomes 0 and another 10MHz channel is idle per NAV check and PHY CCA check, a STA can transmit 20MHz PPDU.
    The fairness between 20z STA and 10MHz STA should be guaranteed.
NAV timer in secondary channel has zero value and PHY CCA in secondary channel indicates idle medium.
Backoff timer becomes 0
Continue the backoff timer counting down.
Start the new backoff procedure.