## Slide 1: Multi-Link Operation: Dynamic TID Transfer
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-09-17

## Slide 2: Overview
Multi-link operation (MLO) has been discussed in the past with the focus on packet-level aggregation [1]
In this document, we discuss how the unified (MLO) framework can support dynamic transfer of a TID between links

## Slide 3: TID Link Switch
MLO framework would need to have the ability to seamlessly move a TID from one link to another link based on a certain condition
  E.g., transferring a TID from a link on 2.4GHz to a link on 5GHz without requiring reassociation
A TID may be transferred for reasons such as load balancing or congestion
  E.g., 2.4GHz link is congested or becomes unavailable
Different from packet-level aggregation where both links are utilized for aggregation
Packet-level agg
TID Link Switch

## Slide 4: Example of unified MLO framework to support pkt-level / TID Link switching
Packet-level Aggregation
Dynamic TID Link Switch

## Slide 5: Summary
The contribution introduces a high-level design to support dynamic TID transfer between links with MLO framework

## Slide 6: Straw Poll 1
Do you support that the 802.11be amendment shall define mechanism(s) for multi-link operation that enables the following:
  An operational mode for concurrently exchanging frames on more than one link for one or more TID(s)
  An operational mode for restricting outstanding MPDUs of one or more TID(s) to be on one link at a time
  Y: 60
  N: 7
  A: 34

## Slide 7: Motion
Move to add the following to the 802.11be SFD:
  define mechanism(s) for multi-link operation that enables the following:
    An operational mode for concurrently exchanging frames on more than one link for one or more TID(s)
    An operational mode for restricting exchanging frames of one or more TID(s) to be on one link at a time
  Mover: Abhishek Patil
  Second:
  Y:
  N:
  A:

## Slide 8: Straw Poll 2
Do you support that the 802.11be amendment shall define mechanism(s) for multi-link operation that enables the following:
  Dynamically change the mapping of MPDUs of one or more TID(s) from one set of links to another set of links
  Y:
  N:
  A:

## Slide 9: Reference
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai Huang - Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek Patil - Qualcomm)
[3]: 11-19-0821 multiple band discussion (Liwen Chu - Marvell)
[4]: 11-19-0979 Multi-link Operation Follow-up (Yongho Seok - Mediatek)