## Slide 1: High-level EHT Preamble Structure
Date: 2019-07-14
Authors:

## Slide 2: Introduction
Until 11ax, different preamble formats are introduced in each generation.
State-of-art STA’s preamble detection state machine is getting more and more complicated.
In this contribution, we discuss the EHT preamble design criteria and high-level structure.

## Slide 3: Existing PPDU Formats
HT-GF: Third symbol QBPSK detection can classify.
HT-MM: LENGTH%3 == 0 + SIG1 QBPSK (+ SIG2 QBPSK) can classify
VHT: LENGTH%3 == 0 + SIGA1 BPSK + SIGA2 QBPSK
HE SU/MU: LENGTH%3 ~= 0 + RLSIG + SIGA1 BPSK + SIGA2 BPSK
HE ER SU: LENGTH%3 ~= 0 + RLSIG + SIGA1 BPSK + SIGA2 QBPSK
L-STF
L-LTF
L-SIG
RLSIG
HE-SIGA2
HE-SIGA, HE-SIGB, HE-STF, HE-LTF, HE-DATA
HE-SIGA1
L-STF
L-LTF
L-SIG
L-DATA
L-STF
L-LTF
L-SIG
HTSIG1
HT-STF
HT-LTFs
HT-DATA
11a
HT-MM
HTSIG2
HT-GF-STF
HT-LTF1
HTSIG1
HT-DATA
HTLTF2~NLTF
HTSIG2
HT-GF
L-STF
L-LTF
L-SIG
VHTSIGA1
VHTSTF
VHTLTFs
VHT-DATA
VHT
VHTSIGA2
VHTSIGB
L-STF
L-LTF
L-SIG
RLSIG
HE-SIGA2
HE-SIGB, HE-STF, HE-LTF, HE-DATA
HE SU/MU
HE-SIGA1
HE_ER
QBPSK
BPSK

## Slide 4: Design Criteria
EHT preamble shall provide backward compatibility and coexistence with legacy PPDUs.
PPDU format signaling is no more complex than 11ax.
  Every generation keeps adding more patterns to distinguish from legacy PPDU formats.
  The auto-detection complexity and latency keeps increasing.
  EHT preamble design needs to limit the complexity.
Supports interoperability with future generations.
  EHT and future devices may be able understand the preamble for better interoperability and coexistence, on top of simple LENGTH definition.

## Slide 5: EHT Preamble Structure
Coexistence:
  Duplicated legacy preamble (LSTF+LLTF+LSIG) is appended
RLSIG:
  may keep for range extension and PPDU format signaling
EHT SIGs:
  Contains static bits signaling information for interop. with future generations.
  And PPDU-dependent decoding related information bits.
L-STF
L-LTF
L-SIG
RLSIG
L-STF
L-LTF
L-SIG
RLSIG
EHT SIGs
L-STF
L-LTF
L-SIG
RLSIG
…
…
;;;
…

## Slide 6: Static Bits in EHT SIGs
The bits useful for EHT and future generations devices to interop.
  For example, PPDU/PHY format bits (reserve multiple bits for future use), BSS color and etc..
  Fixed bit location and definition for EHT and beyond devices to understand.
Structure:
  The static bits needs to be defined on 20MHz bandwidth, similar to HE-SIGA.
  Duplicated over entire PPDU bandwidth.
  Resilient to preamble puncturing.

## Slide 7: Summary
Discussed about design criteria for EHT preamble.
  Backward compatible and future-proof.
Pre-appended legacy preamble for backward compatible.
Static bits in EHT-SIG for future interoperability.