## Slide 1: Coexistence Mechanisms
Date: 2019-07-17
Authors:

## Slide 2: Coexistence Mechanisms
The key elements for coexistence are
  A calibrated sensing mechanism
    Listen for transmissions from other nodes
  A listen-before-talk (LBT) protocol
    A protocol to process the sensing results prior to transmission
  Maximum channel occupancy time (MCOT) limits
    Limits on transmit duration when transmitting
  Adjacent channel protection
    Requirements on protection of adjacent channels when transmitting

## Slide 3: Sensing Threshold
IEEE 802.11a/n/ac use two thresholds, one for own technology, higher for other technologies
IEEE 802.11ax uses more than two thresholds depending on spatial reuse option
  Preambles are used to differentiate between own and other technology/network and choose a different threshold for them
3GPP technologies use a single threshold for all technologies

## Slide 4: Sensing Threshold
IEEE 802.11ax devices defer to IEEE 802.11a/n/ac and ax (own network) devices at -82 dBm
802.11a/n/ac/ax_own_nwk
802.11ax
-62 dBm
-82 dBm

## Slide 5: Sensing Threshold
IEEE 802.11ax devices defer to IEEE 802.11ax (other network) devices at threshold greater than -82 dBm (spatial reuse)
802.11ax
other_nwk
802.11ax
-82 dBm
-62 dBm

## Slide 6: Sensing Threshold
IEEE 802.11ax devices defer to other technology devices at threshold -62 dBm
Other technology
802.11ax
-82 dBm
-62 dBm

## Slide 7: Sensing Threshold
Sensing threshold determines the level of spatial reuse by determining the level at which a node defers to another node
  Trade-off between reuse (proportional to channel access opportunities) and SINR
The appropriate level of the sensing threshold to maximize system performance depends on
  Deployment density
  Radio environment (Indoor residential, Indoor office, Outdoor urban, Outdoor suburban, …)
The appropriate level of the sensing threshold should NOT depend on the characteristics of neighboring nodes
  Own or other network
  Own or other technology

## Slide 8: Sensing Threshold for 6 GHz
A solution that satisfies the clear need for adaptation of sensing thresholds in the real world without violation of regulations is needed
Co-existing networks, even when using the same technology will not be aware of the thresholds used by each network
A single common maximum energy detection threshold between all nodes and technologies is the only solution that is viable and future proof (addressed further in companion document)
Additional sensing mechanisms for sharing within a network can be independently used as long as these mechanisms comply with the single common maximum energy detection threshold across all technologies. Examples:
  A network operating without scheduling can use preambles for sharing (e.g., IEEE 802.11a/n/ac/ax)
  A managed network can use scheduled operation for sharing (e.g., LTE, NR, IEEE 802.11ax)

## Slide 9: Adjacent Channel Protection
Adjacent channel leakage ratio is an important requirement for good coexistence of nodes operating in adjacent channels
3GPP standards require ~9 dB (35 dB vs. 26.3 dB) additional protection compared to IEEE 802.11
Carrier 1
Carrier 2
Power spectral
density

## Slide 10: Adjacent Channel Protection with Wideband Carriers
IEEE 802.11 defines spectral emissions mask for transmissions on parts of wideband carriers (e.g. 80 MHz)
Spectral emission masks for Wi-Fi preamble puncturing where N is the number of contiguous punctured 20 MHz channels
Transmit spectral emission mask from the latest version of the ETSI BRAN Harmonized standard EN 301 893 v2.1.1

## Slide 11: Adjacent Channel Protection with Wideband Carriers
The ETSI spectral mask requirements are not met for various cases
  Can cause harmful interference to already deployed LTE-LAA systems designed to meet ETSI masks
Comparison of the overall spectral emission masks for the [1 1 0 1] channel puncturing pattern
Comparison of the overall spectral emission masks for the [1 0 0 1] channel puncturing pattern