## Slide 1
Authors:
Multi-Link Architecture and Requirement Discussion
Date: 2019-07-14
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses a potential EHT multi-link communication to support low latency, high reliability and high throughput applications.

## Slide 3: Background
Potential Applications
  EHT PAR lists some major use cases for the specification enhancements
    Extreme high throughput
      4K or 8K video transmission, virtual reality or augmented reality, remote office and cloud computing etc..
    High reliability transmission application
      manufactory automation, IoT services, etc..
    Low latency transmission application
      gaming, machine control, virtual reality or augmented reality, etc..

## Slide 4: Background
Potential Features
  EHT PAR lists some main features under the discussion for support indoor and outdoor operation in the 2.4 GHz, 5 GHz and 6 GHz frequency bands.
    320MHz bandwidth and more efficient utilization of non-contiguous spectrum,
    Multi-band/multi-channel aggregation and operation,
    Multi-AP Coordination (e.g. coordinated and joint transmission),
    etc.
  The multi-channel and/or multi-AP operation may be considered together under the multi-link communication
    Multi-channel/band operation - when the multi-link communication are with the same AP.
    Multi-AP operation - when the multi-link communications are with different APs.

## Slide 5: Background
802.11 Protocol Reference Architecture
  Basic reference model
  Multi-band reference model
    MSDUs with same TID cannot be transmitted across channels or bands
(A) ISO/IEC basic reference model
(B) Reference model for a multi-band capable device

## Slide 6: Background
802.11 Protocol Reference Architecture
  Reference model for support multiple MAC sublayers
(C) Reference model for supporting multiple MAC sublayers

## Slide 7: Multi-Link Architecture Considerations
Multi-Link Framework Requirements
  Dynamic selecting and switching an operating link to address the use cases of reducing access latency for fast connection, balancing loads, etc..
  Concurrent transmit or receive packets over multiple links to address the use cases of improving transmission reliability and increasing peak-throughput.
  Utilizing multi-link efficiently for power saving especially for stations

## Slide 8: Multi-Link Reference Modal (1)
ML Multi-BSS Model
  A ML AP forms multiple BSS, each has its own link and operates independently.
  A ML STA associates with one or more BSS of the ML AP and communicates with the ML AP through each BSS.
  More backward-compatible to legacy reference architecture, and reuse of most existing MAC
  It may need multiple associations and is difficult for coordination of ML operations by the upper layer.
CH1
CH2
Upper Layer
802.11 PHY1
MLME
802.11 PHY2
ML STA
802.11 MAC1
802.11 MAC2
802.11 PHY2
802.11 MAC2
CH3
PME
Upper Layer
802.11 PHY1
MLME
ML AP
802.11 PHY2
802.11 PHY3
802.11 MAC1-L
802.11 MAC2-L
802.11 MAC3-L
PME

## Slide 9: Multi-Link Reference Modal (2)
ML Single-BSS Model
  A ML AP forms a single BSS (i.e. BSSID) over multiple links
  A ML STA associates to this BSS of ML AP, but can communicate through different links.
  Single association and easy to control/coordinate the ML operation by MAC
  Some modification of reference architecture may be needed.
CH1
CH2
802.11 MAC-U
802.11 PHY1
MLME
802.11 PHY2
ML STA
802.11 MAC1-L
802.11 MAC2-L
802.11 PHY2
802.11 MAC2-L
CH3
PME
802.11 MAC-U
802.11 PHY1
MLME
ML AP
802.11 PHY2
802.11 PHY3
802.11 MAC1-L
802.11 MAC2-L
802.11 MAC3-L
PME

## Slide 10: MAC Protocol Stack Partition
Upper MAC vs Lower MAC
 | TX |  | RX | 
MAC-U | A-MSDU Aggregation |  | A-MSDU De-aggregation | 
 | PS Defer Queue |  | (null) | 
 | Sequence Number Assignment |  | (null) | 
 | MSDU Integrity Protection (optional) |  | MSDU Integrity Protection (optional) | 
 | Fragmentation |  | Defragmentation | 
 | Packet Number Assignment |  | Replay Detection (optional) | 
 | (null) |  | Block Ack Buffering and Reordering | 
 | MPDU Encryption and Integrity Protection |  | MPDU Decryption and Integrity Check | 
 | (null) |  | Duplicate Removal | 
 | (null) |  | BA (delayed) | 
MAC-L | TX1 | TX2 | RX1 | RX2
 | (null) | (null) | HARQ-ACK/NACK, ACK, BA | HARQ-ACK/NACK, ACK, BA
 | (null) | (null) | Address Filtering | Address Filtering
 | MPDU Header + CRC Creation | MPDU Header + CRC Creation | MPDU Header + CRC Validation | MPDU Header + CRC Validation
 | MPDU Aggregation | MPDU Aggregation | MPDU De-aggregation | MPDU De-aggregation

## Slide 11: Multi-Link Requirement Discussion
Multi-Link Operation Options
  Selective communication
    Transmit or receive a PPDU over one link
  Joint communication
    Concurrently transmit or receive the same PPDU over two or more links
  Simplex communication
    Concurrently transmit or receive different PPDUs over two or more links
  Duplex communication
    Concurrently transmit and receive different PPDUs over two or more links
  Multi-Link Operation Setup
  ML STA and ML AP may need to exchange the ML capability during the association.
  Multi-Link Transmission
  Current MAC SAP only supports Service Class (SC): QoSAck and QoSNoAck
  It may need new SC : Low Latency, High Reliability and High Throughput

## Slide 12: Multi-Link Requirement Discussion
Support Low Latency Applications
  A STA performs EDCA on multiple channels to find the earliest available link(s) and transmits the low latency data packet over this link.
CH2
CH1
CH3
The earliest available channel in the idle
CH Busy
CH Busy
CH Busy
Transmits a PPDU over CH3

## Slide 13: Multi-Link Requirement Discussion
Support High Reliability Applications
  A STA performs EDCA on multiple channels to find two or more available link and transmits high reliable data packets jointly over those links.
CH2
CH1
CH3
Two available channels at the same time
CH Busy
CH Busy
CH Busy
transmit the same PPDU over CH3
transmit the same PPDU over CH1

## Slide 14: Multi-Link Requirement Discussion
Support High Throughput Applications
  A STA performs EDCA on multiple channels to find multiple available links and transmits high throughput data packets in simplex or duplex.
CH2
CH1
CH3
Transmit a PPDU over CH1
The first available channel
The third available channel
CH Busy
CH Busy
CH Busy
The second available channel
Transmit a PPDU over CH3
Transmit a PPDU over CH2

## Slide 15: Summary
In this contribution, we discussed
  Multi-Link reference modes and a potential MAC protocol model
  Multi-Link framework requirements
  Different Multi-Link operation options and how to use them to support different application use cases

## Slide 16: Straw Poll 1
Do you support the single BSS (i.e. BSSID) over multi link operation?
    YES/NO/ABS

## Slide 17: Straw Poll 2
Do you support ML STA and ML AP exchange their multi link capabilities during the association?
    YES/NO/ABS

## Slide 18: Straw Poll 3
Do you support following options in Multi-Link Operation?
  Selective communication
    Transmit or receive one PPDU over one link at one time
YES/NO/ABS
  Joint communication
    Concurrently transmit or receive the same PPDU over two or more links
    YES/NO/ABS
  Simplex communication
    Concurrently transmit or receive different PPDUs over two or more links
    YES/NO/ABS

## Slide 19: References
11-18-1231-04-0eht-eht-draft-proposed-par
11-18-1233-04-0eht-eht-draft-proposed-csd

## Slide 20
Thank you!