## Slide 1: Sounding procedure in AP collaboration
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu |  | F3-6A, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Guogang Huang |  |  |  | 
Dandan Liang |  |  |  | 

## Slide 2: Background
In 11ax (and before), sounding procedure is done within a BSS.
In 11be, with AP coordination, channel state information across BSSs are needed. Hence, sounding procedures with multiple APs and multiple STAs need to be designed.

## Slide 3: Background
Assume there are two BSSs, AP1 and AP 2 are two BFers. STA1 is associated with AP1, STA2 is associated with AP2. STA1 and STA2 are two BFees.
AP1 also acts as the master AP. AP2 acts as the slave AP.

## Slide 4: Sounding Procedure - NDPA
The master AP (AP1) will first send EHT NDPA, followed by NDP. The NDPA will indicate:
  The APs that are involved in the sounding procedure.
  The sounding parameters per each AP-STA pair.
  A shared AID space is preferred for STAs involved in AP coordination..

## Slide 5: Sounding Procedure – NDPs
After the first NDP sent by the master AP, the other slaves AP will send NDP sequentially following the sequence specified in the EHT NDPA .
  Each slave AP can also transmits its own NDPA
  Each slave AP can adjust CFO and timing offset based on the NDPA sent by the master AP before transmitting NDP
  Multiple APs may send joint NDPA frames and NDPs multiplexed in freq./spatial domain.

## Slide 6: Sounding Procedure - Collecting CSI
After the NDPs, the master AP will send BFRP trigger frames to solicit beamforming report (BFR) from each STA. There are several options:
  Opt1: each AP collects its own CSI, i.e., AP1 collects CSI (AP1STA1, AP1STA2), AP2 collects CSI (AP2STA1, AP2STA2).
    Pro: for transmission like CoBF, co-OFDMA, no need to exchange CSI between APs.
    Con: AP needs to collect CSI from non-associated STAs.

## Slide 7: Sounding Procedure - Collecting CSI
  Opt2: each AP collects CSI only from its associated STA(s), i.e., AP1 collects CSI (AP1STA1, AP2STA1), AP2 collects CSI (AP1STA2, AP2, STA2).
    Pro: CSI is exchanged within each BSS
    Con: needs to exchange CSI through wired/wireless transmission

## Slide 8: Sounding Procedure - Collecting CSI
  Opt3: master AP collects CSI for all the APs.
    Pro: simplified triggering procedure.
    Con: needs to exchange CSI through wired/wireless transmission.

## Slide 9: Sounding Procedure –transfer/return frame
For Opt1 and Opt2, after one AP collects all the CSIs, the AP will further indicate the second AP to collect its CSI, e.g., through transfer frame.
Furthermore, when the last AP finishes collecting all the CSIs, the AP will indicate the master AP, it has finished collection through return frame.
No need of transfer/return frame for Opt 3.

## Slide 10: Sounding Procedure – BF report
For the BF report, for Opt2 and Opt3, the BF report contains CSI of multiple APs:
  Opt A: separate EHT MIMO control and related CSI information
  Opt B: unified EHT MIMO control and separate CSI information
For Opt1, the BF report still contains CSI of a single AP.
Order | Opt A
0 | Category
1 | EHT Action
2 | EHT MIMO control for AP1
3…5 | CSI/CQI/etc. for AP1
6 | EHT MIMO control for AP2
7…9 | CSI/CQI/etc. for AP2
Order | Opt B
0 | Category
1 | EHT Action
2 | EHT MIMO control for all APs
3…5 | CSI/CQI/etc. for AP1
6…8 | CSI/CQI/etc. for AP2
 | …

## Slide 11: Wrap up
Sounding procedure for AP coordination is discussed in this presentation.
  Explicit sounding procedure is discussed here. Implicit sounding procedure can be separately discussed.
Different options of collecting CSIs are analyzed:
  Opt1: each AP collects its own CSI, i.e., AP1 collects CSI (AP1STA1, AP1STA2), AP2 collects CSI (AP2STA1, AP2STA2).
    Pro: for transmission like CoBF, co-OFDMA, no need to exchange CSI between APs.
    Con: AP needs to collect CSI from non-associated STAs.
  Opt2: each AP collects CSI only from its associated STA(s), i.e., AP1 collects CSI (AP1STA1, AP2STA1), AP2 collects CSI (AP1STA2, AP2, STA2).
    Pro: CSI is exchanged within each BSS
    Con: needs to exchange CSI through wired/wireless transmission
  Opt3: master AP collects CSI for all the APs.
    Pro: simplified triggering procedure.
    Con: needs to exchange CSI through wired/wireless transmission.