## Slide 1: Preamble design and auto-detection for 11bd
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo choi |  |  |  | js.choi@lge.com
July 2019

## Slide 2: Introduction
In the previous presentation[1], we have introduced the two methods for packet classification to detect the 11bd PPDU.
  Auto-detection based on constellation mapping
  Auto-detection based on repetition checking
In this contribution, we investigate the performance according to the auto-detection method and suggest the preamble design for the 11bd frame.

## Slide 3: Recap : Preamble and Packet classification
Two options for preamble were discussed[1].
  Option 1 : Q-BPSK constellation mapping is applied to one OFDM symbol after L-SIG symbol.
    Auto-detection based on constellation mapping is used for classification of option 1.
  Option 2 : The repeated L-SIG symbol is located after L-SIG symbol.
    Auto-detection based on repetition checking is used for classification of option 2.
L-SIG
Q-BPSK
L-STF
L-LTF
L-SIG
L-SIG
L-STF
L-LTF

## Slide 4: Repetition detection
It performed the repetition detection in frequency domain
  The multiple ways of repetition detection in frequency domain can be considered.
  Herein, we consider the one way which is simple and gets reliable detection performance.
    As described in [2], we check the Hamming distance of coded bits for L-SIG and L-SIG next symbol.
    Then, by performing of L-SIG content check after repetition detection, it can reduce L-SIG false positive probability.
      Parity, Rate = 3Mbps, LENGTH == 3x
    This method already have been applied for repetition detection of 11ax PPDU.

## Slide 5: Performance (1/3)
Rural LoS
  P-miss of repetition is lower than error rate of L-SIG.
  On the other hand, we can verify that P-miss of QBPSK is very high and even higher than PER of L-SIG.
  Also, we can check that repetition of L-SIG has very low false detection probability in this simulation result.

## Slide 6: Performance (2/3)
Highway LoS

## Slide 7: Performance (3/3)
Highway NLoS

## Slide 8: Error rate of L-SIG
We can also improve the L-SIG field error rate.
  By repetition of L-SIG, we can get the gain more than 2dB.
  Since it improves the performance of L-SIG, range extension can be expected.

## Slide 9: NGV-SIG
It was decided to include the NGV-SIG field in 11bd PPDU in the previous meeting.
And, NGV-SIG field includes the control information related to 11bd transmission and performs the same role as VHT-SIGA in 11ac.
  For example, NGV-SIG field can include information such as BW, mid-amble, MCS, etc.
  Like this, since it includes the common control information of 11bd PPDU, it is required the better reliability than data fields.
    To provide reliability, robust modulation(i.e., BPSK) should be applied
      Other schemes for higher reliability is open.
Thus, to give this kind of information in advance, it is desirable that NGV-SIG is located before starting of NGV-portion.

## Slide 10: Proposed 11bd frame format
Use L-SIG repetition for 11bd packet detection, i.e.,
  Locating the 8us symbol repeating the L-SIG content right after L-SIG symbol in 11bd PPDU
    Rate field in L-SIG shall be set to the value of 3 Mb/s.
  Modulating the repeated L-SIG( RL-SIG) symbol with BPSK and rate ½ BCC.
  The next symbol (NGV-SIG) after RL-SIG is also BPSK.
L-SIG
RL-SIG
L-STF
L-LTF
NGV-STF
NGV-SIG
·····
NGV-LTF
Legacy preamble
BPSK, ½BCC
BPSK, ½BCC
BPSK, ½BCC
11bd preamble
Will be discussed in other contributions

## Slide 11: Conclusion
We investigated the miss and false detection probability according to auto-detection methods considering for 11bd PPDU format.
  L-SIG repetition showed reliable miss detection and false detection error probabilities in various V2V channels.
  Since it can improve the L-SIG performance, range extension can be expected.
It is appropriate to place NGV-SIG before the staring of NGV-portion(ex., NGV-STF) for the early reliable indication of control information included in NGV-SIG.
  To guarantee reliability, NGV-SIG should be modulated with BPSK

## Slide 12: Reference
[1] IEEE 802.11-19/0739r3, PPDU format for 11bd
[2] IEEE802.11-15/0579r2, 802.11ax Preamble Design and Auto-detection

## Slide 13: SP1
Do you agree that in 11bd PPDU, a 8us symbol having the same L-SIG content is located right after L-SIG symbol?
  Y/N/A

## Slide 14: SP2
Do you agree that the rate field in L-SIG shall be set to the value of 3Mbps ?
  Y/N/A

## Slide 15: SP3
Do you agree that NGV-SIG symbol(s) is located right after the RL-SIG symbol in 11bd PPDU?
  Y/N/A

## Slide 16: SP4
Do you agree that the OFDM symbols for both RL-SIG and NGV-SIG shall use BPSK modulation?
  Y/N/A