## Slide 1: Consideration on HARQ Unit
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
There have been lots of contributions dealing with the HARQ feature on 11be [1-16]
  Most contributions are focusing on figuring out how much the performance with HARQ can be improved in various conditions
  Some contributions are beginning to consider HARQ framing/structural issues [7, 15, 16]
In this contribution, we’d like to discuss an issue related to HARQ, particularly (re)transmission HARQ unit
We introduce two candidates for the HARQ unit and investigate their tx/rx procedure from the perspective of PHY and MAC side

## Slide 3: HARQ unit
HARQ unit definition
  An HARQ unit represents an error-check unit for HARQ retransmission
There are two candidates for HARQ unit
  PHY-level unit (E.g., LDPC codeword(s), A new PHY-level unit)
  MAC-level unit (E.g., MPDU(s))
Assumptions on this contribution
  HARQ units
    We considers an LDPC codeword as a PHY-level unit and an MPDU as a MAC-level unit from here
  Error check method
    Ack/Nack check is assumed to be performed by an LDPC checksum if the LDPC codeword is the PHY-level unit and is performed by the CRC check if the MPDU is the MAC-level unit
  In case when HARQ retransmission occurs, the size of HARQ units does not vary

## Slide 4: 1) PHY-level unit: General procedures
It is determined whether or not the HARQ unit has been successfully transmitted at the PHY side (Ack/Nack decision)
HARQ transmission and HARQ error check is performed on a per-codeword(s) basis
HARQ feedback mechanism and a new HARQ feedback frame structure should be defined
Tx
MAC
Tx
PHY
Rx
PHY
Rx
MAC
HARQ
F/B
A-MPDU
PHY HDR
Data
Data
PHY HDR
A bunch of the HARQ units
HARQ Combining
HARQ
F/B
Delivering to Rx MAC
BlockAck
BAR
After HARQ feedback with all ack context, any MAC acknowledgement may be transmitted (beyond scope of this contribution)

## Slide 5: 1) PHY-level unit: Overhead/buffer issues
Signaling overhead
  Some signaling overhead (E.g., numbering units, distinguishing firstly transmitted and retransmitted units) on a PHY header may be required
  If some procedures are negotiated between Tx and Rx, this signaling overhead may be reduced
    E.g., a new data is not allowed to be contained in the retransmitted PPDU
    or, the order of the HARQ units in following PPDUs cannot be switched
    or, the nack-ed HARQ units can be transmitted over two or more times
Feedback overhead
  A new HARQ feedback frame structure should be defined
  A method to indicate which units are required to be retransmitted is needed (Similar to the BlockAck Bitmap field in BlockAck frame)
  If there are lots of units in a PPDU, HARQ feedback should contain lots of information
    Hence, for reducing this feedback size, it is possible to define the HARQ unit with multiple codewords
MAC padding overhead
  There is no MAC padding overhead issue
Buffer issues
  The HARQ units should be buffered in both the Tx and Rx PHY layers

## Slide 6: 1) PHY-level unit: Compatibility issues
Interaction with existing ARQ
  Since there can be HARQ retransmissions between PHYs, Tx and Rx MACs may wait for a long time while their ARQ procedures cannot be supported for HARQ
    To solve this, it can be possible to define fixed number of max retransmission or define MAC timeout
  Ack policy needs to be revised
    If there are HARQ retransmissions when the Ack policy indicates Normal Ack or Implicit BAR, Tx MAC may think the MPDU just sent is failed
  A relationship between PHY HARQ feedback and MAC (Block)Ack also can be considered
    PHY HARQ feedback can replace MAC BlockAck when all HARQ units are successfully received

## Slide 7: 2) MAC-level unit: General procedures
HARQ Ack/Nack is determined by MAC layer using CRC in each MPDU
HARQ error checking is performed on an MPDU basis
Existing BlockAck can be used as the HARQ feedback
MAC padding can be adopted to align the border of MPDU and codeword
  Using additional MAC padding, MPDU and codeword can be aligned so that retransmission procedure can be relatively simple; however, it can cause additional overhead
  Without additional MAC padding, mapping information between MPDU and codeword can cause additional overhead
Tx
MAC
Tx
PHY
Rx
PHY
Rx
MAC
A-MPDU
BlockAck
A-MPDU
BlockAck
Data
PHY HDR
Data
PHY HDR
HARQ Combining
A bunch of HARQ units

## Slide 8: 2) MAC-level unit: Overhead/buffer issues
Signaling overhead
  Mapping information between MPDUs and LDPC codewords need to be contained in PHY header (See Appendix)
    With additional MAC padding, only codeword number information is needed to map a certain MPDU to codewords
    Without additional MAC padding, additional indication is needed since a codeword can be related to two or more MPDUs and vice versa
  This signaling overhead can be large overhead since PHY header has the lowest MCS
Feedback overhead
  Existing BlockAck frame can be exploited as the HARQ feedback
MAC padding overhead
  With MAC padding, it incurs padding overhead for each MPDU
Buffer issues
  The HARQ units should be buffered in the Rx PHY layers
    The HARQ units should also be buffered on Tx PHY when the MAC padding is not adopted
* We briefly estimated the size of overhead in Appendix B.

## Slide 9: 2) MAC-level unit: Compatibility issues
Interaction with existing ARQ
  The existing ARQ procedure will rarely change
  MAC-level retransmission is more compatible than PHY-level retransmission
  Some indications from Rx MAC to Rx PHY may be needed to control buffered data
    Rx MAC should let Rx PHY know which codewords will be retransmitted after responding BlockAck frame
    When all MPDUs are successfully received by Rx MAC, Rx MAC will transmit BlockAck with all-ack context, and then will let Rx PHY flush buffered codewords out

## Slide 10: Comparison between the PHY-level and MAC-level HARQ unit
From signaling and potential padding overhead aspect, PHY-level unit is preferred while we may need to design a new feedback and consider how to co-operate with the existing ARQ protocol
 | 1. PHY-level unit | 2. MAC-level unit
Signaling overhead | Low | High It may cause severe overhead since PHY header has the lowest MCS
HARQ feedback overhead | (Potentially) High It can be reduced by defining multiple codewords as the HARQ unit MAC acknowledgement is likely to be replaced by HARQ feedback | Low Existing BlockAck frame can be exploited
MAC padding overhead | Low | High Depending on the MAC padding, the amount of overhead varies
Compatibility with existing ARQ | Current ARQ may need to be revised to operate HARQ with ARQ | Relatively compatible with the existing ARQ

## Slide 11: Summary
In order to adopt HARQ into 11be, the HARQ unit and HARQ procedure need to be defined
We presented two candidates for HARQ unit; PHY-level unit and MAC-level unit
  When using PHY-level unit, we need to design a new HARQ feedback which may require large overhead
    However, it can be reduced if the feedback transmits with higher rate
  In case of MAC-level unit, signaling overhead to map MPDUs with codewords and additional MAC padding overhead will be large overhead
We think that using PHY-level unit as an HARQ unit is appropriate since the drawback of using PHY-level unit can be relatively easily resolved

## Slide 12: Straw Poll
Which option do you prefer as a unit for HARQ?
  Option 1: A PHY-level unit (E.g., LDPC codeword(s))
  Option 2: A MAC-level unit (E.g., MPDU(s))

## Slide 13: References
[1] 18/1116r0, “Distributed MU-MIMO and HARQ Support for EHT”
[2] 18/1587r1, “HARQ for EHT”
[3] 18/1955r0, “HARQ for EHT – Further Information”
[4] 18/1963r1, “Discussion on HARQ for EHT”
[5] 18/1979r1, “HARQ performance analysis”
[6] 18/1992r1, “HARQ Feasibility for EHT”
[7] 18/2029r1, “HARQ in EHT”
[8] 18/2031r0, “HARQ Gain Studies”
[9] 19/0070r0, “HARQ in Collision-Free and Collision-Dominated Environments”
[10] 19/0390r0, “Effect of Preamble Decoding on HARQ in 802.11be”
[11] 19/0780r0, “Consideration on HARQ”
[12] 19/0791r1, “Effect of Preamble Decoding on HARQ in 802.11be”
[13] 19/0792r1, “Comparisons of HARQ transmission schemes for 11be”
[14] 19/0798r0, “HARQ Simulation Results”
[15] 19/0873r0, “HARQ Framing”
[16] 19/1038r0, “HARQ with A-MPDU in 11be”

## Slide 14: Appendix A: PPDU format example - MPDU as an HARQ unit without padding to align
Codeword
#1
Data
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5
PHY
HDR
Mapping information:
MPDU#1 – CW#1, #2
MPDU#2 – CW#2, #3
MPDU#3 – CW#4, #5
MPDU
#1
MPDU
#2
MPDU
#3

## Slide 15: Appendix A: PPDU format example - MPDU as an HARQ unit with padding to align
Data
PHY
HDR
Mapping information:
(2, 1, 2)
MPDU
#1
MPDU
#2
MPDU
#3
Padding
Codeword
#1
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5

## Slide 16: Appendix B: Overhead estimation
 | Signaling overhead | HARQ feedback overhead | MAC padding overhead
1. A codeword as an HARQ unit | Low | Required HARQ feedback information size: (16383*8/1944)*64 bits = 4352 bits | None
2. MPDU as an HARQ unit without padding to align | Required size for indexing starting number field per one PPDU: log24288 bits = 13 bits Required size for indicating the number of codewords for each MPDU = log2(16383*8/1944) bits = 7 bits Required size for mapping per one PPDU: 64 * (13 + 7) bits = 160 Bytes | Use existing BlockAck frame | None
3. MPDU as an HARQ unit with padding to align | Information of mapping the number of codewords into the MPDU is needed Required size for mapping per one PPDU: 64 * 7 bits = 56 Bytes | Use existing BlockAck frame | Distribution of MPDU size: Uniform Expected padding overhead size per one PPDU: (1944/2)*64 bits ≈ 8 KBytes
A new data cannot be transmitted until one packet transmission finishes.
Retransmitted HARQ units are ordered as they transmitted just before.
Codeword length = 1944 bit
Max MPDU size = 2^14 -1 = 16383 bytes
Max number of codewords in one MPDU = (16383*8/1944) = 67
The number of MPDUs per one PPDU = 64
Max number of codewords in one PPDU = 67*64 = 4288