## Slide 1: Channel coding issue in HARQ
Date: 2019-07-16
Authors:
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jinmin1230.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Recap on [1-16]
So far, even if the amount of gain is different, [1-16] show the benefit and throughput gain of HARQ
  And, various issues (e.g. HARQ method(CC/IR), link adaptation, collision issue, error check unit, HW complexity, HARQ-SIG design, etc) are discussed
To strengthen the merit of HARQ, we simulate HARQ performance with both BCC and LDPC in short packet case

## Slide 3: LDPC in short packet
In general, parity check matrix is designed to have a best performance when there is no punctured bits in a codeword block.
However, in practical system, since the size of information bit is variable, puncturing/repetition almost always occurs. Moreover, if there are many punctured bits, the performance can be degraded.
  In BCC case, there is no restriction about information size if we consider reasonable information size which is enough longer than trellis length
Furthermore, short packet causes the retransmission overhead increase due to large PHY preamble portion of short packet
So, we’d like to verify HARQ performance in short packet case

## Slide 4: The number of punctured bits
In spec., the number of punctured bits is computed by following equation
    The BW, number of information bits, MCS and Nss are the factors to calculate the number of punctured bits
  When we assume reasonable packet length(>100bytes, e.g. VoIP, Appendix 1), The table below shows the maximum puncturing case per MCS
MCS(20MHz, Nss=1) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Information size(bytes) | 247B | 247B | 238B | 162B | 248B | 329B | 373B | 417B
The number of punctured bits per CW | 296bits | 278bits | 138bits | 268bits | 126bits | 173bits | 128bits | 84bits
Ratio % (Punctured bits/parity bits) | 30.5% | 28.6% | 28.4% | 27.6% | 25.9% | 26.7% | 26.3% | 25.9%

## Slide 5: Performance in short packet (ARQ)
Simulation parameter
  802.11ax, 20 MHz, TGnD channel
  SISO, BCC/LDPC, MCS 0~7
  Optimal MCS selection
  Packet length (see previous page)
  PHY&MAC overhead are considered
LDPC shows 1~3dB better performance than BCC even in the maximum puncturing case
− BCC
− LDPC

## Slide 6: LDPC IR method in HARQ
To evaluate the performance of HARQ in short packet, we consider LDPC IR method below to transmit new redundancy version (This is just example, other methods are possible)
  1st step: Encoding with one level lower coderate than designated code rate (code rate set : [1/2, 2/3, 3/4, 5/6])
  2nd step: Puncturing parity bits to make same code rate as designated code rate
  3rd step: For retransmission, different puncturing pattern is used
  ※ This example assumes self-decodable packet in any (re)transmissions. So, it doesn’t require the increase in LDPC CW processing rate.
Information bits
Information bits
Parity bits
R=2/3
Parity bits
Parity bits
Information bits
HARQ
Actual encoding R=1/2
Parity bits
Information bits
Discard punctured bits
Re-transmission
Effective R=2/3
effective R=2/3
(Designated R=2/3)
ARQ
(Designated R=2/3)
Initial transmission
Transmission
Discard punctured bits

## Slide 7: Performance in short packet (HARQ)
Simulation parameter
  BCC IR[11, 13] / LDPC IR
  Packet length (see the appendix)
  Optimal MCS selection
  Up to 2 transmissions
  PHY&MAC overhead are considered
As in the case of ARQ, LDPC shows better performance than BCC even in the maximum puncturing case
And, even considering PHY&MAC overhead, HARQ shows better performance and smoother curve than ARQ
  The gap can be increased if we consider realistic link adaptation
− BCC
− LDPC

## Slide 8: Conclusions
Even considering PHY&MAC overhead in short packet case, HARQ shows better performance and smoother curve than ARQ
In our results, LDPC always shows better performance than BCC even in the maximum puncturing case
  If we consider more sophisticated IR method in LDPC, the gap will be increased
  We may need to reconsider whether we keep BCC in 11be if we adapt HARQ in 11be

## Slide 9: Straw poll/motion #1
Do you agree to add the following text into SFD?
  TGbe shall support HARQ for data frame transmission
    Other frames(control, management) is TBD

## Slide 10: Straw poll/motion #2
Do you agree to add the following text into SFD?
  TGbe shall support LDPC as the mandatory coding scheme for HARQ transmission.

## Slide 11: References
[1] 18/1116r0, “Distributed MU-MIMO and HARQ Support for EHT”
[2] 18/1547r0, “Technology Features for 802.11 EHT”
[3] 18/1549r0, “Recommended Direction for EHT”
[4] 18/1587r1, “HARQ for EHT”
[5] 18/1955r0, “HARQ for EHT – Further Information”
[6] 18/1963r1, “Discussion on HARQ for EHT”
[7] 18/1979r1, “HARQ performance analysis”
[8] 18/1992r1, “HARQ Feasibility for EHT”
[9] 18/2029r1, “HARQ in EHT”
[10] 18/2031r0, “HARQ Gain Studies”
[11] 19/0070r0, “HARQ in Collision-Free and Collision-Dominated Environments”
[12] 19/0390r0, “Effect of Preamble Decoding on HARQ in 802.11be”
[13] 19/0780r0 “Consideration on HARQ”
[14] 19/0792r0, “Comparisons of HARQ transmission schemes for 11be”
[15] 19/0798r0, “HARQ Simulation Results”
[16] 19/0873r0, “HARQ Framing”
[17] 19/1038r0, “HARQ with A-MPDU in 11be”

## Slide 12: Appendix 1
Example of VoIP packet size
  In IEEE 802.16m Evaluation Methodology Document(IEEE 802.16m-08/004r5)
    Instead of 802.16e Header and CRC, we assume 802.11 Header and CRC (34bytes) and AMR without Header compression IPv4 active(73 bytes)
      In this case, total VoIP packet size is 107byts

## Slide 13: Appendix 2
The maximum puncturing case in HARQ
  Since we encode with one level lower code rate except MCS 0, 1 and 3, the number of punctured bits is different from ARQ
    MCS 0, 1 and 3 have ½ code rate which is lowest one.
MCS(20MHz, Nss=1) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Information size(bytes) | 247B | 247B | 331B | 162B | 331B | 256B | 351B | 390B
The number of punctured bits per CW | 296bits | 278bits | 352bits | 268bits | 352bits | 614bits | 336bits | 278bits
Ratio % (Punctured bits/parity bits) | 30.5% | 28.6% | 54.3% | 27.6% | 54.3% | 63.2% | 51.9% | 57.2%