## Slide 1: Channel coding issue in HARQ
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jinmin1230.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Recap on [1-17]
So far, even if the amount of gain is different, [1-17] show the benefits and throughput gain of HARQ
  And, various issues (e.g. HARQ method(CC/IR/punctured CC), HARQ unit, collision issue, HW complexity, HARQ-SIG/feedback design, etc.) are discussed
Based on our simulation results in this contribution, we want to make it more clear that HARQ will bring benefits to Wi-Fi system

## Slide 3: LDPC IR method in HARQ
First of all, to evaluate the performance of HARQ, we consider LDPC IR method below to transmit additional parity bits (This is just example, other methods are possible)
  1st step: Encoding with one level lower coderate than designated code rate (code rate set : [1/2, 2/3, 3/4, 5/6])
  2nd step: Puncturing parity bits to make same code rate as designated code rate
  3rd step: For retransmission, different puncturing pattern is used
  ※ This example assumes self-decodable packet in any (re)transmissions. So, it doesn’t require the increase in LDPC CW processing rate.
Information bits
Information bits
Parity bits
R=2/3
Parity bits
Parity bits
Information bits
HARQ
Actual encoding R=1/2
Parity bits
Information bits
Discard punctured bits
Re-transmission
Transmitted R=2/3
Transmitted R=2/3
(Designated R=2/3)
ARQ
(Designated R=2/3)
Initial transmission
Transmission
Discard punctured bits
If combining, effective R=1/2

## Slide 4: Simulation Assumptions
Simulation assumptions
  802.11ax, 80 MHz, Regular GI, 4x HE-LTF, TGnD channel
  MIMO(2x2), LDPC, MCS 0~7
    Optimal MCS
    Sub-optimal MCS selection
      Select highest MCS with <10% PER based on long-term measurement
    Packet length=1000bytes, single MPDU per PPDU
  Up to 2 (re)transmissions
  Same channel realization is applied across all (re)transmissions
    If we consider different channel, HARQ can bring a more gain due to time diversity.
  No impairments, ideal channel estimation, ideal ACK/NACK feedback

## Slide 5: Simulation Results: PER performance
Observation points:
  IR scheme shows better performance than CC and ARQ.
    Especially for non-½ MCSs, additional parity bits increase the gain effectively. (e.g. MCS=2, 4, 5, 6 and 7)
  And, the PER curve per MCS in IR is evenly distributed than others.
    It means that link adaptation can be managed efficiently.
ARQ
HARQ (CC)
HARQ (IR)

## Slide 6: Simulation Results: Goodput performance
Observation points:
  In low SNR region, HARQ shows better performance than ARQ
    The IR shows better performance even in high SNR region
  The IR scheme enables sophisticated link adaptation without additional MCS definition due to smoother curve
    It is caused by evenly distributed PER curve
Optimal MCS selection
Sub-optimal MCS selection

## Slide 7: Introduction of HARQ into Wi-Fi
Although we assume self-decodable packet, only up to 2 (re)transmission and initial version of LDPC IR method, HARQ shows better performance than ARQ
  It is clear that if we consider partial IR, further enhanced IR scheme and optimal retransmission number(e.g. up to 3 or 4), the gain from HARQ can be increasing.
So, we think TGbe shall support HARQ for data frame
  Other frames(control, management) is TBD
Also, since the IR scheme shows better performance than other methods, we should consider IR scheme in HARQ

## Slide 8: Channel coding issue
From 802.11a, Wi-Fi system has kept the BCC because it has a merit in short packet case and has low HW complexity
  In general, parity check matrix in LDPC is designed to have a best performance when there are no punctured bits
  However, in short packet case, many parity bits are punctured in order not to increase PPDU length compared to BCC case. This may cause performance degradation
Furthermore, high PHY preamble ratio in short packet case increases the retransmission overhead
So, we’d like to investigate HARQ performance in short packet case

## Slide 9: The number of punctured bits
In spec., the number of punctured bits is computed by following equation
    The BW, number of information bits, MCS and Nss are the factors to calculate the number of punctured bits
  When we assume reasonable packet length(>100bytes, e.g. VoIP, Appendix 1), The table below shows the maximum puncturing case per MCS
MCS(20MHz, Nss=1) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Information size(bytes) | 247B | 247B | 238B | 162B | 248B | 329B | 373B | 417B
The number of punctured bits per CW | 296bits | 278bits | 138bits | 268bits | 126bits | 173bits | 128bits | 84bits
Ratio % (Punctured bits/parity bits) | 30.5% | 28.6% | 28.4% | 27.6% | 25.9% | 26.7% | 26.3% | 25.9%

## Slide 10: Performance in short packet (ARQ)
Simulation parameter
  802.11ax, 20 MHz, TGnD channel
  SISO, BCC/LDPC, MCS 0~7
  Optimal MCS selection
  Packet length (see previous page)
LDPC shows 1~3dB better performance than BCC even in maximum puncturing case
− BCC
− LDPC

## Slide 11: Performance in short packet (HARQ)
Simulation parameter
  BCC IR[11, 13] / LDPC IR
  Packet length (see the appendix)
  Optimal MCS selection
  Up to 2 (re)transmissions
  PHY&MAC overhead are considered
    PHY Preamble, IFS, backoff, ACK duration
Even considering PHY&MAC overhead, HARQ shows better performance and smoother curve than ARQ
  The gap can be increased if we consider realistic link adaptation
− BCC
− LDPC

## Slide 12: Conclusions
We show HARQ performance and verify that HARQ brings benefits to Wi-Fi system even in sub-optimal scenario
  The more sophisticated HARQ scheme can increase the gain.
Even in short packet case, HARQ shows better performance and smoother curve than ARQ considering PHY&MAC overhead
  In our results, LDPC always shows better performance than BCC even in maximum puncturing case
  Considering current chip manufacturing skill, HW complexity is no longer a problem
  So, we may need to reconsider whether we keep BCC in 11be if we adapt HARQ in 11be

## Slide 13: Straw poll/motion #1
Do you agree to add the following text into SFD?
  TGbe shall support HARQ for data frame transmission
    Other frames(control, management) is TBD

## Slide 14: Straw poll/motion #2
Do you agree to add the following text into SFD?
  TGbe shall support LDPC as the mandatory coding scheme for HARQ transmission.

## Slide 15: Straw poll/motion #3
Do you agree to add the following text into SFD?
  TGbe shall support IR(incremental redundancy) scheme which includes to transmit additional parity bits for HARQ retransmission.

## Slide 16: References
[1] 18/1116r0, “Distributed MU-MIMO and HARQ Support for EHT”
[2] 18/1547r0, “Technology Features for 802.11 EHT”
[3] 18/1549r0, “Recommended Direction for EHT”
[4] 18/1587r1, “HARQ for EHT”
[5] 18/1955r0, “HARQ for EHT – Further Information”
[6] 18/1963r1, “Discussion on HARQ for EHT”
[7] 18/1979r1, “HARQ performance analysis”
[8] 18/1992r1, “HARQ Feasibility for EHT”
[9] 18/2029r1, “HARQ in EHT”
[10] 18/2031r0, “HARQ Gain Studies”
[11] 19/0070r0, “HARQ in Collision-Free and Collision-Dominated Environments”
[12] 19/0390r0, “Effect of Preamble Decoding on HARQ in 802.11be”
[13] 19/0780r0 “Consideration on HARQ”
[14] 19/0792r0, “Comparisons of HARQ transmission schemes for 11be”
[15] 19/0798r0, “HARQ Simulation Results”
[16] 19/0873r0, “HARQ Framing”
[17] 19/1038r0, “HARQ with A-MPDU in 11be”

## Slide 17: Appendix 1
Example of VoIP packet size
  In IEEE 802.16m Evaluation Methodology Document(IEEE 802.16m-08/004r5)
    Instead of 802.16e Header and CRC, we assume 802.11 Header and CRC (34bytes) and AMR without Header compression IPv4 active(73 bytes)
      In this case, total VoIP packet size is 107byts

## Slide 18: Appendix 2
The maximum puncturing case in HARQ
  Since we encode with one level lower code rate except MCS 0, 1 and 3, the number of punctured bits is different from ARQ
    MCS 0, 1 and 3 have ½ code rate which is lowest one.
MCS(20MHz, Nss=1) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Information size(bytes) | 247B | 247B | 331B | 162B | 331B | 256B | 351B | 390B
The number of punctured bits per CW | 296bits | 278bits | 352bits | 268bits | 352bits | 614bits | 336bits | 278bits
Ratio % (Punctured bits/parity bits) | 30.5% | 28.6% | 54.3% | 27.6% | 54.3% | 63.2% | 51.9% | 57.2%