## Slide 1: 20MHz Channel Usage Options
Date: 2019-07-14
Authors:
Onn Haran, Autotalks

## Slide 2: Assumptions
1. 20MHz channel can enable high-bandwidth use-cases, such as cooperative perception
2. Both 10MHz sub-channels are carrying safety data
  Same high level of protection is needed for both
  Having said that, the channels composing the 20MHz channels, are rarely used today
  3. Concurrent transmission in two adjacent channels create mutual interference, shortening communication range of both channels

## Slide 3: Stating the obvious: Service should use a single predetermined sub-channel
Service breaks if both 10MHz sub-channels are used
Busy (st A)
Busy
10MHz TX (st B)
Transmission of station A isn’t received by station B and vice-versa. Station B can’t determine which station transmits while reception is ongoing. A common service to station A and B would be broken if station B would use different sub-channel than station A

## Slide 4: Options for 20MHz Channel Usage
No usage of 10MHz sub-channels
Predetermined 10MHz sub-channel may be used
Busy
Busy
20MHz TX
Busy
Busy
10MHz TX
20MHz channel transmission is deferred when either of the 10MHz sub-channels is busy
Receiving only 20MHz channel
Transmission uses predetermined 10MHz sub-channel when other sub-channel is busy
Receiving either 20MHz or predetermined 10MHz sub-channel
Predetermined

## Slide 5: Adjacent Channel Interference
No usage of 10MHz sub-channels
Predetermined 10MHz sub-channel may be used
Busy
20MHz TX
Busy
10MHz TX
No adjacent channel interference
Strong adjacent channel interference

## Slide 6: Protection of Second Sub-Channel
No usage of 10MHz sub-channels
Predetermined 10MHz sub-channel may be used
Busy
20MHz TX
Busy
10MHz TX
NAVs of both sub-channels are detected and respected
NAV is ignored while sub-channel is transmitting, settling on lower protection of guard-interval correlation
Busy
20MHz TX
Busy
RX
NAV should be respected while sub-channel is received

## Slide 7: Link Utilization
No usage of 10MHz sub-channels
Predetermined 10MHz sub-channel may be used
Busy
20MHz TX
Busy
10MHz TX
Sparsely used sub-channels: high utilization for both
20MHz TX
20MHz TX
Busy
20MHz TX
Busy
10MHz TX
20MHz TX
20MHz TX
Busy
Busy
Heavily used other sub-channel: advantage to 10MHz channel usage
Busy
20MHz TX
Busy
Busy
20MHz TX
Busy
Heavily used predetermined sub-channel: low utilization for both

## Slide 8: Implementation Complexity
No usage of 10MHz sub-channels
Predetermined 10MHz sub-channel may be used
20MHz receiver
10MHz NAV receiver of either sub-channel
No concurrent reception
Single receiver, toggling between 20MHz reception and NAV reception in either 10MHz sub-channels
Single radio (always tuned to 20MHz channel)
Concurrent reception (for NAV during sub-channel reception)
NAV receiver is almost as complicated as full receiver
Dual radio is needed to maintain receiver sensitivity and adjacent channel rejection
Simplified solution would have been possible with compromised protection of other sub-channel
L-STF detector
L-STF detector
RX/TX front end
10/20MHz receiver
L-STF detector
L-STF detector
RX/TX front end
10MHz NAV receiver
RX front end

## Slide 9: Comparison Summary
 | No usage of 10MHz sub-channels | 10MHz sub-channels may be used
Transmission operation | 20MHz transmission when both sub-channels are idle | Using predetermined 10MHz sub-channel when other sub-channel is busy
Protection of 10MHz sub-channels | Good. Both are protected | Mostly good. The other sub-channel is less protected after 10MHz transmission
Adjacent channel | No interference from other sub-channel | Mutual interference to other sub-channel
Implementation complexity / cost | Medium. Single receiver and single radio path | Double. Dual receiver and dual radio path
Link utilization | Medium-low. Not coping with heavily used sub-channels | Medium. Can cope with heavily used other sub-channel. Can’t cope with busy predetermined sub-channel
Summary | Using 10MHz sub-channel doubles complexity and creates adjacent channel interference for better coping with heavy load in non predetermined sub-channel | 

## Slide 10: Not to Decide is to Decide
In theory, both options can be allowed
In practice, implementation is different
  Implementation would have to support the more complicated option: using 10MHz sub-channel

## Slide 11: Straw Poll #1
Do you agree to add the following text into Section 3 of SFD?
During receive, 802.11bd 20MHz shall detect both 10MHz sub-channels NAV
Y:
N:
A:
July 2019
Onn Haran, Autotalks

## Slide 12: Straw Poll #2
Which of 20MHz operation methods is preferred?
1. No usage of 10MHz sub-channels:
2. Predetermined 10MHz sub-channel may be used:
3. None of the above:
Abstain:
July 2019
Onn Haran, Autotalks

## Slide 13: Straw Poll #3a
Do you agree to add the following text into Section 3 of SFD?
802.11bd 20MHz channel shall not use 10MHz sub-channels
Y:
N:
A:
July 2019
Onn Haran, Autotalks

## Slide 14: Straw Poll #3b
Do you agree to add the following text into Section 3 of SFD?
802.11bd 20MHz channel may use predetermined 10MHz sub-channel
Y:
N:
A:
July 2019
Onn Haran, Autotalks