## Slide 1: Mechanisms for Reliable V2X operation
Date: 2019-07-14
Authors:
Onn Haran, Autotalks

## Slide 2: V2X Communication Should be Reliable
  Communication should be trusted to control vehicle
  Delivery guarantee is not available for unacknowledged Broadcast messages
  MAC acknowledgement provides the foundation for delivery guarantee
  Aligned with 3GPP progress for supporting future V2X use-cases
  Baseline for media-agnostic upper layers

## Slide 3: Broadcast Acknowledgement
  Broadcast Ack message reports the successfully received MAC addresses
  Broadcast Ack message is transmitted periodically at the basic message rate (100mS)

## Slide 4: Reaction to Broadcast Acknowledgement
  Vehicle learns whether it was received by another vehicle within target range
  Vehicle searches Broadcast Ack content for its own MAC address
  Vehicle knows locations of other vehicles from their prior transmissions
  Target range could be adjusted according to environment (channel load, urban, etc…)
  Vehicle should send a new message if previous transmission failed
  Retransmission should be avoided to maintain data freshness requirements

## Slide 5: Channel Load Consideration
  Broadcast Ack transmission should not overload channel
  It is unnecessary that all vehicles in a dense environment would share their feedback
  Two options are presented to reducing number of transmission
  1. Some vehicles are transmitting all the time: Each vehicle selects if it transmits
  2. All vehicles are transmitting occasionally: Each vehicle selects it transmission periodicity
Channel load | Option A: Probability of vehicle transmission | Option B: Periodicity of vehicle transmission
<10% | 100% | 1
<25% | 50% | 4
Otherwise | 10% | 10

## Slide 6: Broadcast Acknowledge Operation Sparse environment
Broadcast Ack:
Green car not listed
Prior transmission wasn’t received by purple vehicle (within target range)
All vehicles transmit Broadcast Ack every 100mS
Safety message transmission
Safety message transmission (triggered after failure of previous message)
Broadcast Ack:
Green car listed

## Slide 7: Broadcast Acknowledge Operation Dense environment
Some of the vehicles transmitted Broadcast Ack in last cycle
Broadcast Ack: Green car not listed
Prior transmission wasn’t received by purple vehicle
Safety message transmission
Broadcast Ack: Green car listed
Safety message transmission (triggered after failure of previous message)

## Slide 8: Broadcast Ack Transmission
Broadcast Ack transmission
Logging of received MAC addresses with valid CRC
Periodic transmission of the log
Start log
Stop log
Packet for transmission
UTC
Functionality is shown for the sake of complexity estimation
Operation may be performed either in MAC layer or in upper layer
MAC address of RX packet with valid CRC

## Slide 9: Broadcast Ack Reception
Broadcast Ack reception
Checking presence of self MAC address in Broadcast Ack content
Checking if time of last transmitted packet is within log period
Received Broadcast Ack
Received MAC address
Self MAC address found / not found
Last TX packet is within reported period
Functionality is shown for the sake of complexity estimation
Operation may be performed either in MAC layer or in upper layer
UTC of last transmitted packet

## Slide 10: Upper Layer New Packet Generation Decision
Functionality is shown for the sake of complexity estimation. Performed in upper layer
Did self vehicle transmit in last 100mS and not planning to transmit in next 100mS?
Is self MAC address missing from Broadcast ACK of vehicle within target range?
Prepare new packet for transmission
Yes
No
Yes
Transmission isn’t needed
No

## Slide 11: Broadcast Ack can be Encoded as new BlockAck variant
  Reserved values can be utilized

## Slide 12: Possible Broadcast Ack Format
  Log UTC start and stop times
    Used to determine relevancy of Ack to last transmitted message
  UTC can be represented as [0…9999]mS aligned with GNSS timing
  MAC addresses of successfully received messages
  Compressed (e.g. 16bits) for minimizing channel load
Compressed RX MAC address #1
2
Octets
Compressed RX MAC address #2
2
Compressed RX MAC address #N
2
. . . . . . . . . . . . . . .
Log UTC start
12-16 bits
Log UTC stop
12-16 bits

## Slide 13: Straw Poll #1
Should 802.11bd define feedback of received MAC addresses decoded in a BlockAck variant?
Y:
N:
A:
July 2019
Onn Haran, Autotalks

## Slide 14: Straw Poll #2
Assuming 802.11bd includes Broadcast Ack, what should be specification scope?
Broadcast ACK format definition:
Broadcast ACK format and transmit and receive operation:
None of the above:
Abstain:
July 2019
Onn Haran, Autotalks

## Slide 15: Straw Poll #3
Assuming 802.11bd includes Broadcast Ack transmission, would you agree to the following message format?
Y:
N:
A:
July 2019
Onn Haran, Autotalks
Compressed RX MAC address #1
2
Octets
Compressed RX MAC address #2
2
Compressed RX MAC address #N
2
. . . . . . . . . . . . . . .
Log UTC start
12-16 bits
Log UTC stop
12-16 bits

## Slide 16: Straw Poll #4
Assuming 802.11bd includes Broadcast Ack transmission, what would be the preferred congestion control mitigation?
Self-selection of transmitting vehicles:
Adjustment of transmission periodicity:
None of the above:
Abstain:
July 2019
Onn Haran, Autotalks

## Slide 17: References
  [1] Reliable V2X operation, Onn Haran 802.11-19-0717/r1
July 2019
Onn Haran, Autotalks