## Slide 1: Multiple Link Operation Capability Announcement
Date: 2019-07-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: Multi Link Operation
A multi-link logical entity can include multiple links.
The capability to use multiple links by a multi-link logical entity should be announced.
  Whether a multi-link logical entity can do transmission while reception in more than one link.
Common Function
Link1 MAC/PHY
Link2 MAC/PHY

## Slide 3: Restriction of Multiple Link Operation
A multi-link logical entity supports only one link at any time.
A multi-link logical entity supports more than one link at any time:
  A multi-link logical entity that supports multiple links at any time can announce the following capabilities for each pair of links:
    Support the transmission on a link concurrently with reception on another link
    Doesn’t support the transmission on a link concurrently with reception on another link
The announced capability is decided by the frequency distance between two links (e.g. | the center frequency of link1 – the center frequency of link2 | ) and the interference canceling capability between two links.
Common Function
AP1 MAC/PHY in link1
Link 1
Link 2
A-MPDU from STAx1 to AP1
A-MPDU from AP2
AP2 MAC/PHY in link2
Multi-link logical AP entity

## Slide 4: Link Operation Capability Announcement
A multi link logical entity may include more than two links
The multi-link operation capability about transmission while reception is defined every two links.
Common Function
MAC/PHY in link1
MAC/PHY in link3
MAC/PHY in link2
Multi-link logical entity

## Slide 5: Capability Announcement and Channel Switch
A multi-link AP entity may do channel switch in one link during the BSS operation.
If after the channel switch operation, the frequency distance between two links becomes smaller, a multi-link AP/STA entity assumes that the peer multi-link AP/STA entity can’t do transmission while reception within these two links.
If after the channel switch operation, the frequency distance between two links becomes larger, a multi-link AP/STA entity assumes that a peer multi-link AP/STA entity can do transmission while reception within these two links if the peer multi-link AP/STA entity can do transmission while reception before the channel switch.