## Slide 1: Multiple Link Operation Capability Announcement
Date: 2019-07-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: Multi Link Operation
A multi-link logical entity can include multiple links.
The capability to use multiple links by a multi-link logical entity should be announced.
  Whether a multi-link logical entity can do transmission while reception in more than one link.
Common Function
Link1 MAC/PHY
Link2 MAC/PHY

## Slide 3: Restriction of Multiple Link Operation
A multi-link logical entity supports only one link at any time.
A multi-link logical entity supports more than one link at any time:
  A multi-link logical entity that supports multiple links at any time can announce the following capabilities for each pair of links:
    To support transmission on one link concurrent with reception on the other link
      Support can be advertised only if the 2 links are on different channels
    To support transmission on one link concurrent with transmission on the other link
    To support reception on one link concurrent with reception on the other link
The announced capability is decided by the frequency distance between two links (e.g. | the center frequency of link1 – the center frequency of link2 | ) and the interference canceling capability between two links.
Common Function
AP1 MAC/PHY in link1
Link 1
Link 2
A-MPDU from STAx1 to AP1
A-MPDU from AP2
AP2 MAC/PHY in link2
Multi-link logical AP entity

## Slide 4: Capability Announcement and Channel Switch
A multi-link AP entity may do channel switch in one link during the BSS operation.
If after the channel switch operation, the frequency distance between two links becomes smaller, a multi-link AP/STA entity assumes that the peer multi-link AP/STA entity can’t do transmission while reception within these two links.
If after the channel switch operation, the frequency distance between two links becomes larger, a multi-link AP/STA entity assumes that a peer multi-link AP/STA entity can do transmission while reception within these two links if the peer multi-link AP/STA entity can do transmission while reception before the channel switch.

## Slide 5: Straw Poll 1
Do you support that
  A multi-link logical entity supports only one link at any time.
  A multi-link logical entity supports more than one link at any time:
    A multi-link logical entity that supports multiple links at any time can announce the following capabilities for each pair of links:
      To support transmission on one link concurrent with reception on the other link
        Support can be advertised only if the 2 links are on different channels
      To support transmission on one link concurrent with transmission on the other link
      To support reception on one link concurrent with reception on the other link