## Slide 1: Discussion on HARQ
Date: 2019-07-15
Authors:

## Slide 2: Introduction
Hybrid ARQ (HARQ) exploits a retransmission and combination mechanism
  Receiver stores erroneously received packets
  Receiver combines the retransmitted signal with the stored signal
The following topics are considered
  Retransmission scheduling
  Control information for HARQ procedures
  HARQ unit
  ACK/NACK

## Slide 3: Retransmission
We consider the following two retransmission strategies
  Contention based retransmission
  Back to back retransmission
    New transmission and retransmission in same TXOP

## Slide 4: Contention Based Retransmission
Perform contention before retransmission
  No changes to current IEEE 802.11 retransmission except combining transmissions
  Issues:
    Large number of HARQ processes are needed, e.g. HARQ process/memory per TID and per STA

## Slide 5: Scheduled Retransmission
Reserve TXOP including HARQ retransmission
  Smaller amount of memory is required.
  Fast retransmission is possible
  Issues:
    Number of HARQ retransmissions is limited to TXOP limit
    Can be inefficient when number of retransmissions is less than expected.

## Slide 6: Control Information
Two potential ways to carry HARQ control information
  PLCP header
  New MAC control frame
HARQ control information
  Transmitter and receiver ID
  HARQ parameters
  Feedback related information (if needed)
  HARQ process ID (if needed)

## Slide 7: HARQ Unit
HARQ Unit: unit for retransmission
  Size of HARQ Unit can be varying to optimize resource utilization, overhead, etc.
  Option 1: HARQ unit contains one or more MPDU(s)
    ACK/NACK for each MPDU [or HARQ unit]
    Pros: no CRC needed per HARQ unit, reuse BA for feedback
    Cons: padding overhead

## Slide 8: HARQ Unit (Cont.)
HARQ Unit: unit for retransmission
  Option 2: HARQ unit is not aligned with MPDU boundary
    ACK/NACK for each or group of HARQ unit(s)
    Pros: minimize padding overhead by using dynamic fragmentation
    Cons: need to store partially decoded MPDU that staggers over two HARQ units
  Note that, we may consider fragmentation to eliminate padding issue for option 1 or partially decoded MPDU that staggers over two HARQ units for option 2.

## Slide 9: ACK/NACK Channel
Two potential ways to carry HARQ ACK/NACK information
MAC BA: minimal design effort
New PHY feedback: optimize overhead, e.g. omitting transmitter and receiver ID

## Slide 10: Summary
Discussed about
  Retransmission scheduling
  HARQ control information and its exchange
  HARQ Unit for retransmission
  ACK/NACK channel