## Slide 1
Consideration on Multi-link Operation
Date: 2019-07-15
Authors:

## Slide 2: Introduction
According to PAR[1], the two main objectives of 802.11be are:
  Enhanced high peak throughput
  Reduced latency and jitter
The multi-link operation is suggested as a key candidate feature in EHT to achieve the objectives [2], [3]
For efficient multi-link operation, technical issues including the following ones should be well investigated:
  Channel access method in multi-link
  Reliable transfer (Block Ack) over multi-link
In this contribution, considerations on multi-link are presented

## Slide 3: Entity for Multi-link Operation
In case of using multiple links for on TID:
  Tx STA queues the data in upper MAC
  Tx STA allocates data to links considering channel access process: use same SN
  Transmission procedure performed in Lower MAC and PHY
  Rx STA receives the PPDU in different links, extracts MPDU, and perform aggregation
  The aggregation includes the reordering of SN coming from different links

## Slide 4: The Options of Multi-link Transmission Procedure [4]
Independent transmission
  The transmission on multiple channel/link may proceeded different time
Simultaneous transmission
  The transmission on both channel occurs on same time

## Slide 5: Channel Access for Independent Transmission
For independent transmission, contention is performed independently
  Channel access is performed independently on each link
  Simultaneous Tx and Rx of multiple links is not preferred

## Slide 6: Block Ack Procedure in Independent Transmission
Depending on the capabilities of 802.11be devices, the BA cannot be received since link2 is still transmitting
  Link2 should wait while receiving BA

## Slide 7: Channel Access for Simultaneous Transmission
As in the legacy wide-band operation, the simultaneous multi-link channel access may be performed with one primary link
  Backoff procedure in one link, ED sensing in the other link(s)

## Slide 8: Head-of-line Blocking Delay in Simultaneous Transmission
Simultaneous transmission
  QoS data frames share sequence number (SN), one window size, and one reordering buffer over multi-link
  QoS data blocks which are simultaneously transmitted have to end at the same time
    Simultaneous Tx and Rx transmission shall not be performed

## Slide 9: Head-of-line Blocking Delay in Simultaneous Transmission (cont.)
HoL blocking delay
  QoS data frame which has SN from 6 would not go up to LLC until SN 5 frame is received.
    Reordering buffer in recipient would be wasted

## Slide 10: Conclusion
Multi-link operation can be classified into independent transmission and simultaneous transmission
Channel access for simultaneous transmission should be discussed
Reliable transfer with block ack mechanism in multi-link should be carefully considered

## Slide 11: Straw Poll 1
Do you agree with the following rule in multi-link?
  Simultaneous Tx and Rx transmission shall not be performed
Y/N/A

## Slide 12: Straw Poll 2
Do you agree with the following rule in multi-link?
  QoS data frames shall be properly assigned across multiple links for the receiver to reduce the Head-of-line blocking delay
Y/N/A

## Slide 13: Reference
[1] 18/1231r5 EHT draft proposed PAR
[2] 19/764r0 Multi-Link Aggregation: Gain Analysis
[3] 19/766r1 Enhanced Multi-band/Multi-channel Operation
[4] 19/0823r0 Multi-Link Operation: Design Discussion