## Slide 1: Combined HARQ and Rate Adaptation
Date: 2019-09-15
Authors:

## Slide 2: Motivation
Many HARQ presentations show different result
Some show combined results with rate adaptation [1, 2] with different capabilities
  Assume a MCS chosen based on known long term SNR (not instantaneous)
  MCS chosen with uniform instantaneous SNR feedback error within +/-5dB
What is the HARQ gain on a system level?
System-level simulations comprising
  Abstract channel & PHY model
  Model for HARQ combining
  EDCA, TXOP, A-MPDU, rate adaptation

## Slide 3: Channel & Phy Model
TGn channel model D
  80MHz @ 5GHz
  Pre-generated table of (correlated) channel realizations
For every transmission (preamble, header, A-MPDU segment)
  Take channel realization n from position xn = xn-1 + tn-1  n · v
  Velocity v of the environment
    No mobility  v = 0m/s  Channel does not change
    Mobility ~ v = 1m/s  Channel conditions change slowly, values are correlated
    Mobility ~ v = 3m/s  Channel conditions change unpredictably
  Calculate SINR from channel realization
L2S mapping for SINR to Block Error Probability
  Assumes LDPC codes

## Slide 4: HARQ Operation
t
STA 1
STA 2
BlockACK
BlockACK
HARQ Process 1
HARQ Process 2
HARQ Process 3
HARQ Process 1
HARQ Process 2
HARQ Process 3
RTS
CTS
Retransmission in next TXOP
Assume protocol mechanism exists to determine which MPDUs can be combined
Retransmissions can use remaining TXOP duration
Use Soft Combining
  Combine log-likelihood ratios
  Implemented by adding the effective SINRs of the transmissions
  Combine only MPDUs with the same MCS

## Slide 5: Evaluated HARQ Variants
Baseline: No HARQ
  4ms TXOPs
  Minstrel Rate Adaptation
    Retransmissions with lower MCS, depending on Minstrel retry chain
    Retransmissions can use remaining TXOP
Soft Combining + fast retransmissions
  Initial MCS selected by Minstrel
  Fast retransmissions
    Retransmission in TXOP do not increase the retry counter
    Do not change the MCS
  If no success in the TXOP
    Increase retry counter
    Lower MCS
SC + fast retransmissions + aggressive rate adaptation
  Initial MCS is selected based on Minstrel
  Keep MCS for all retransmissions

## Slide 6: Evaluation Scenario
One AP, one STA, Single link
  Downlink traffic from AP to STA
  Packet sizes distributed 80B ... 1480B
  Full buffer load
d = 1m ... 30m
AP
STA
d

## Slide 7: Results: No Mobility (v = 0m/s)
Static channel, constant SINR for a fixed distance
HARQ has no effect for good SINR
Significant gains only for bad SINR

## Slide 8: Results: Mobility ~ 1m/s
Channel varies from transmission to transmission
  Deep dips possible
Rate adaptation is
  Too optimistic  requires retransmission
  Too pessimistic  Inefficient channel usage
With HARQ
  Retransmission during TXOP is not counted
  Optimistic has less impact
Aggressive RA
  Even more opportunities for combining

## Slide 9: Results: Mobility ~ 3m/s
Similar gains

## Slide 10: Conclusions
Observe combined effects of
  HARQ
  Rate adaptation
  TXOP usage
  Time-varying channel
If rate adaptation is not able to follow the channel quality fluctuations, HARQ provides gains

## Slide 11: References
[1] Ron Porat, et. al., “HARQ Simulation Results,” IEEE 802.11-19/0798r0, May 2019
[2] Steve Shellhammer, et. al., “HARQ Simulation Results,” IEEE 802.11-19/1078r0, July 2019