## Slide 1: Views on Latency and Jitter Features in TGbe
Date: 2019-07-xx
Authors:

## Slide 2: Abstract
According to EHT PAR [1], the scope of TGbe includes at least one mode of operation capable of improved worst case latency and jitter.
The purposes of this presentation are to follow up on latency and jitter features presented in RTA TIG and EHT SG and to discuss key functions for each feature.
  The RTA report and recommendations [2][3] describes a summary of discussions presented in RTA TIG.
  In addition, features that have potential to reduce latency and jitter such as multi-band / channel operation are also discussed in EHT SG (TGbe).
  We should recall what functions had been discussed so far in RTA and EHT, and clarify issues that should be solved in TGbe.

## Slide 3: Use cases discussed in RTA [2]
Use cases |  | Intra BSS latency/ms | Jitter variance/ms | Packet loss | Data rate/ Mbps
Real-time gaming |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming |  | < 10 | < 2 | Near-lossless | <0.1 (Reverse link) >5Mbps (Forward link)
Real-time video |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
Robotics and industrial automation | Equipment control | < 1 ~ 10 | < 0.2~2 | Near-lossless | < 1
 | Human safety | < 1~ 10 | < 0.2 ~ 2 | Near-lossless | < 1
 | Haptic technology | <1~5 | <0.2~2 | Lossless | <1
 | Drone control | <100 | <10 | Lossless | <1 >100 with video
These use cases in IEEE 802.11be are important to expand Wi-Fi market.

## Slide 4: Technical features discussed in RTA and EHT (Summary)
Methods | Improvement for |  |  | Contributions
 | Latency | Jitter | Worst case latency | 
A. 802.1TSN approach (including time aware shaping) | ○ | ○ | ○ | 19/0373r0, 18/1947r4 18/1892r0, 18/1542r0, 802.1/0064r2, 18/1160r0
B. Priority tagging | ○ |  |  | 18/1761r1
C. Utilizing Trigger Frame | ○ | ○ | ○ | 18/1947r4, 18/1892r0
D. Multi-band / channel Operation | ○ |  |  | 19/0402r0, 19/0360r0, 18/1543r0
E. Admission control | ○ |  | ○ | 18/1892r0, 18/1160r0
F. Deterministic time scheduling (e.g. Token-passing) | ○ | ○ | ○ | 18/1889r0, 1918r0

## Slide 5: Technical features discussed in RTA and EHT (1)
A) 802.1 TSN approach (including time aware shaping) [4]-[9]
  Applying 802.1 Time-Sensitive Networking (TSN) over 802.11 is seemed to be the most straightforward approach to realize low latency networks in TGbe.
  MAC/PHY support should be required to meet functions considering bounded low latency and ultra high reliability.
  As described in [4], requirements should be separated between un-managed network and managed network.
  Key functions: detection mechanism of managed networks.
B) Priority tagging [10]
  There are four Access Categories in conventional EDCA and this classification is insufficient for fine control of real-time applications.
  Impacts on 802.11 PHY/MAC are relatively small compared to making new scheduling protocol.
  Key functions: mechanisms that ensure worst case latency in mixed environment of different priorities.

## Slide 6: Technical features discussed in RTA and EHT (2)
C) Utilizing Trigger Frame (TF) [5][6]
  Using 802.11ax trigger frames to make periodical timing resource for time-sensitive frames.
  If an AP periodically transmits TFs, STAs can stably transmit time-sensitive frames.
  Key functions: mechanisms that manage and protect periodical transmission in congested situation.
D) Multi-band / channel operation [11]-[13]
  These techniques are also prospective approaches to realize low latency in TGbe as well as TSN approach.
  These approaches can enhance reliability by using two or more different wireless media.
  Latency performance is improved due to extremely high speed transmission by utilizing multiple 6 GHz channels.
  Key functions: mechanisms that coexist with legacy standards especially when we use 2.4 GHz / 5 GHz channels.

## Slide 7: Technical features discussed in RTA and EHT (3)
E) Admission control [6][9]
  Admission control is a simple way to manage latency and worst case latency by controlling the number of STAs in a BSS.
  This approach should be applied to managed networks, or should ensure a certain mechanism that protects from interferences of transmissions of other BSSs.
  Key functions: detection mechanism of managed networks.
F) Deterministic time scheduling [14][15]
  TDMA/TDD-like approaches such as token-passing are effective to improve worst case latency.
  However, 802.11 has already defines optional TDMA/TDD-like scheduling functions such as PSMP or HCCA.
    Those methods are rarely used in practical.
  Key functions: mechanisms that soften impacts on existing protocol and coexist with CSMA/CA based on 802.11ax.

## Slide 8: Needs to extend existing functions
DCF (Distributed Coordinated Function) perspective
  Mechanisms that ensure worst case latency and coexist with legacy standards should be considered.
  Moreover, we should make consent on precise definition of "worst case latency"
    Should we guarantee certain value of worst case latency or make effort only to improve jitter characteristics?
Environmental perspective
  802.1 TSN approach, utilizing TF approach, admission control and time scheduling are effective in managed network.
  Mechanisms that can identify managed network should be required.

## Slide 9: Conclusions
We reviewed prospective approaches that are discussed in RTA TIG and EHT SG (TGbe) and their key functions that realize EHT PAR about worst case latency.
Their key functions that are needed for achieving EHT PAR about worst case latency should be realized.
  DCF perspective : mechanisms that ensure worst case latency and coexist with legacy standards.
  Environmental perspective : mechanisms that can identify managed network.

## Slide 10: References
[1] 802.11/18-1231r01 EHT draft proposed PAR
[2] 802.11/19-0065r6 RTA TIG summary and recommendations
[3] 802.11/19-0006r6 RTA report draft
[4] 802.11/19-0373r0 Time-Sensitive Applications Support in EHT
[5] 802.11/18-1947r4 Performance evaluation of Real Time Communication over Wi-Fi
[6] 802.11/18-1892r0 Time-Aware shaping (802.1Qbv) support in the 802.11 MAC
[7] 802.11/18-1542r0 Time-Aware Traffic Shaping over 802.11
[8] 802.1/19-0038r0 IEEE 802“Network Enhancements for the Next Decade”Industry Connections Activity(Nendica):Status Report
[9] 802.11/18-1160r Controlling latency in 802.11
[10] 802.11/18-1761r1 Packet Prioritization Issues
[11] 802.11/19-0402r1 Reducing Channel Access Delay
[12] 802.11/19-0360r0 MAC Architectures for EHT Multi-band Operation
[13] 802.11/18-1543r4 RTA- Dual link proposal
[14] 802.11/18-1889r1 Use cases and requirements potential wireless approaches for industrial automation applications
[15] 802.11/18-1918r0 Determinism for IoT considerations