## Slide 1: IEEE 802.11be: Extremely High Throughput (EHT) WLAN
Date: 2019-07-01
Authors:
Alfred Asterjadhi, et. al.

## Slide 2: Introduction
IEEE 802.11 has recently approved the creation of a new task group to work on a major amendment, 802.11be, for next generation wireless LAN [1, 2]
The presentation will cover need and scope of the 11be project, candidate feature sets and projected timeline
Alfred Asterjadhi, et. al.

## Slide 3: Needs for the Project
Amount of data traffic sent over WLAN continues to increase
  Propelled by ever increasing video traffic
    With throughput requirements that are constantly evolving due to the emergence of 4K and 8K video (e.g., uncompressed rate of 20Gbps)
Applications requiring high throughput and low latency are proliferating
  Such as virtual reality, augmented reality, gaming, remote office, cloud computing
    With stringent throughput & delay requirements (e.g., 1-10ms) to enhance user experience
  In addition users expect improved integration with time sensitive networks
    To support applications over heterogeneous Ethernet and Wireless LANs

## Slide 4: Scope of the project
Define modifications to both PHY and MAC layers that enable
  At least one mode of operation capable of supporting a maximum throughput of at least 30 Gbps, with carrier frequency operation between 1 GHz and 7.250 GHz
  At least one mode of operation of improved worst case latency and jitter
While ensuring backward compatibility and coexistence with
  Legacy IEEE802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands

## Slide 5: Candidate Features
Main candidate features that are under discussion
  320 MHz BW and more efficient utilization of non-contiguous spectrum
  Multi-band/multi-channel aggregation and operation
  16 spatial streams and MIMO protocol enhancements
  Multi-Access Point (AP) coordination
    E.g., coordinated frequency and/or spatial transmission
  Enhanced link adaptation and retransmission protocol (e.g., HARQ)
  Adaptation to regulatory rules specific to 6 GHz spectrum (if needed)

## Slide 6: Projected TGbe Timeline
PAR approved Mar 2019
First TG meeting May 2019
D0.1 Sept 2020
D1.0 Letter Ballot May 2021
D2.0 LB Mar 2022
D3.0 LB Nov 2022
Initial Sponsor Ballot (D4.0) May 2023
Final 802.11 WG approval Mar 2024
802 EC approval Mar 2024
RevCom and SASB approval May 2024
We are here

## Slide 7: References
Approved P802.11be PAR
  https://development.standards.ieee.org/P1102800033/par
Approved P802.11be CSD
  https://mentor.ieee.org/802-ec/dcn/19/ec-19-0063-00-ACSD-p802-11be.docx
Alfred Asterjadhi, et. al.