## Slide 1: Discussion on Multi-link Operations
Date: 2019-07-09
Authors:

## Slide 2
Abstract
In this contribution, we discuss some design choices that may simplify the data flow in multi-link operations.

## Slide 3: Introduction
Multi-band/multi-link operations have been identified as a candidate feature for 802.11be
Architectures enabling multi-band/multi-link operations for 802.11be have been discussed in [1] [2]
  Discussed support for multi-link schemes such as link switching, link aggregation, traffic steering, etc.
  Proposed the concept of Multi-link entity (MLE) and Multi-link Device (MLD)
  A common identifier for MAC-SAP or by DSM either on MLE level or MLD level
A number of design issues for multi-link operations have also been discussed in [3]
  Sequence number space, duplication detections, etc. for multi-link operations
In this contribution, we discuss the benefit of using a single ID to address an MLE or MLD for better data flow on different links in multi-link operations

## Slide 4: Data flow in multi-link operations (1/3)
DL data flow:
  Data frames from DS pass through “high” MAC-SAP in a MLD or MLE that contains APs
  The data are then distributed by the “high” MAC into frames to be sent over one or multiple links. Each of these frames is then assigned to an AP that will send it on a link it has established with a STA of the receiving MLE/MLD.
  Data frame(s) are transmitted over the air via the available links
  Data frame(s) are received by one or more STAs of a MLD or MLE that contains non-AP STAs
  Data frame(s) are passed to the “high” MAC, where the data frames are combined to form the original frame that is then available at the “high” MAC-SAP in the receiving MLD or MLE

## Slide 5: Data flow in multi-link operations (2/3)
UL data flow:
  Data pass through “high” MAC-SAP in a MLD or MLE that contains non-AP STAs
  The data are then distributed by the “high” MAC into frames to be sent over one or multiple links. which may be identified by a non-AP STA on each link. Each of these frames is then assigned to a STA that will send it on a link it has established with an AP of the receiving MLD/MLE
  Data frame(s) are transmitted over the air via the available links
  Data frames are received by one or more APs of a MLD or MLE that contains APs
  Data frame(s) are passed to the “high” MAC, where the data frames are combined to form the original frame that is then available at the “high” MAC-SAP in the receiving MLD or MLE
    /

## Slide 6: Data flow in multi-link operations (3/3)
UL and DL data flows are between the “high” MAC-SAPs of the MLEs/MLDs that contain APs and non-AP STAs
Hence, the “high” MAC-SAPs should be identified by IDs or MAC addresses
Therefore, it is beneficial to have these IDs or MAC addresses included in the MAC frames
  E.g., in one of the address fields in data frames

## Slide 7: Benefits using a single ID for multi-link data transmissions
A data frame can be clearly identified to be meant for higher layers if it contains the ID or MAC address of the target higher MAC SAP of the target MLD or MLE
Sequence numbers can be generated uniquely from the same sequence number space and it is easy to re-assemble fragments, packets and detect duplication
If dynamic link switching is desired, a packet can be transmitted over any link without having to regenerate MAC headers
It is easier to identify packets when multi-channel/multi-band aggregation is used to transmit a wide-bandwidth frame
Some of these benefits may depend on the particular design of multi-link operations defined in 802.11be

## Slide 8: Possible changes needed
APs and STAs belonging to a MLD and MLA may need to filter packets using their higher MAC-SAP ID or MAC addresses when receiving packets on the wireless medium
The ID and MAC addresses of the higher MAC-SAP of each MLE and MLD need to be indicated when multi-link operation is set up

## Slide 9: Conclusions
Multi-link devices such as MLD or MLE should be identified by the ID or MAC address of their “high” MAC SAPs
For multi-link data flows, it may be beneficial to include in the data frames a single ID or MAC address of the target “high” MAC-SAP of the target MLD and MLE

## Slide 10
References
[1] IEEE 11-19/0822r0, Extreme Efficient Multi-band Operation, May 2019
[2] IEEE 11-19/0823r0, Multi-link Aggregation, May 2019
[3] IEEE 11-19/0731r0, Multi-link Operation, May 2019