## Slide 1: Multi-Band Multi-Channel Concept in IEEE 802.11be – A Simple Study
Name | Affiliation | Address | Phone | Email
Sai Nandagopalan | Cypress Semiconductor Corp |  |  | snan@cypress.com
Date: 2019-07-15

## Slide 2: Why Multi Band Multi Channel (MBMC)?
New ways of operating in bands
Efficient use of spectrum
Leveraging underutilized spectrum
Increased data rates
Network load balancing
Dynamic fast switching between bands/channels

## Slide 3: Usage Models from Channels Perspective
The following are the usage models envisioned for MBMC operation
  Let us look at the typical spectrum below (just representative only)
The BSS may be formed in any single band or can be formed with multiple band aggregation
  There are pros and cons of the above

## Slide 4: Single Band Operation
Today’s 802.11a/b/n/ac/ax operate fully in only one band
There are two modes of operation today in Single Band
  Single band contiguous
    Ex: 20 MHz BSS or 40 MHz BSS or 80 MHz BSS or 160 MHz BSS
  Single band non-contiguous
    Ex: 80+80 MHz BSS
  Routers are available for above devices

## Slide 5: Multi Band Operation
Can form BSS across multiple bands
Two ways of Operation
  Concurrent asynchronous
  Concurrent synchronous
    In both cases, we can have APs and non AP STAs and depending on what device is capable we can see few deployment scenarios
Isn't FST already doing part of it?
  Is FST sufficient or not?

## Slide 6: Concurrent Asynchronous
Concurrent asynchronous devices have multiband concurrent operation
  Each band operates independently and simultaneously
    Dual band and triband concurrent routers
  Different non-AP STA devices can be connected to different APs in the collocated device
  May use BTM Request (802.11v) to transfer from one band to another band
  A concurrent asynchronous non AP STA may transfer one of its streams from one band to another to enhance user experience
    Delay, packet loss, jitter, load balancing etc
    FST protocol can be used

## Slide 7: Concurrent Synchronous
Concurrent synchronous devices have multiband concurrent operation
  All bands and operating channels are combined to present a single BSS
    Can consider today’s 80+80 MHz operation in one band as an example although this concept extends to multiple bands
  The maximum bandwidth 802.11be is touting is 320 MHz
  The operation of the concurrent synchronous device is similar to what we see as 160 MHz operation in a single BSS with 80+80 MHz
    Will have primary and secondary channels
  Non AP STA devices may operate on entire bands/channels as the AP to which they are associated or operate in one band/channels or partial multiple bands/channels
    Ex: 80 MHz STA associated with 160 MHz AP today

## Slide 8: Scenario 1
AP Asynchronous concurrent and non AP STA has support for multiple band/channel but can operate on only one band/channel at any instant
  Ex; AP operates on 20 MHz BSS 1 in 2.4 GHz, 80 MHz BSS 2 in 5 GHz and 80 MHz BSS in 6 GHz
  Ex: non AP STA has support for all three bands but can operate (connect) in only one band at a time
  Each band has unique MAC address
It is possible that the AP and/or non AP STA may decide to move all traffic or partial traffic from one band to another band to enhance user experience
This can be accomplished by FST or agile multiband [1]
  Ex: STA based FST and Stream based FST
Block ACKs are independent depending on transparent or non transparent
    IEEE Spec revmd 2.2 already covers it
Helps QoS and load balancing and efficient in power savings from non AP STA perspective. Fast switching is also achieved

## Slide 9: Scenario 1
Architecture of AP
Architecture of non AP STA
General STA architecture of STA from revmd 2.3 section 4
Multiband architecture of revmd 2.3 section 4.6 (non transparent FST)

## Slide 10: Scenario 2
AP is Asynchronous concurrent and non AP STA has support for multiple band/channel but can operate on those bands/channels independently and simultaneously at any instant
  Ex: non AP STA has support for 20 MHz in 2.4 GHz and 80 MHz in 5 GHz
  The association and authentication happens in both bands/channel simultaneously since non AP STA is capable
  Each band can have unique MAC addresses or same MAC address
It is possible that the AP and/or non AP STA may decide to move all traffic or partial traffic from one band to another band to enhance user experience
  This can be accomplished by FST or agile multiband
There is need for block ACK in case the communication happens on both channels simultaneously in a fashion scheduled by AP
  Although the author and few folks who designed FST claim that this can be achieved, the IEEE spec is not clear on this aspect wherein the same stream can be transmitted out of order in both the bands having one universal Block ACK agreement with a possible reordering mechanism
  In case BAs are independent in both bands, then there is a need for scheduler at upper layer on how to route traffic
Helps QoS, load balancing and fast switching
This will be power hungry from non AP STA perspective as it has to process all traffic in both channels simultaneously

## Slide 11: Scenario 2
Architecture of AP/non AP STA
Multiband architecture of revmd 2.3 section 4.6 (non transparent FST)

## Slide 12: Scenario 3
AP is Synchronous concurrent and non AP STA has support for multiple band/channel but can operate on only one band/channel at any instant
  The primary channel is decided by AP
  Any change of the STAs traffic from one channel to another channel can be done by Agile multiband or FST
  AP can have one unique MAC address across bands/channels or different MAC addresses and non AP STA may have one or multiple MAC addresses
New concepts for 11be
  There can be multiple primaries for different bands/channels
  Security can be done in one band for all bands
  The non AP STA can be parked anywhere (any channel/band)
    Need new rules for CCA if the STA is not parked on primary and how to asynchronously communicate from non AP STA
The above two sub-bullets warrant new protocol mechanisms
Helps QoS, load balancing and efficient spectrum utilization
Efficient from non AP STA perspective

## Slide 13: Scenario 3
Two possible architecture of AP
Multiband architecture of revmd 2.3 section 4.6, (transparent FST)
Multiband architecture of revmd 2.3 section 4.6 transparent FST as implemented in open source bonding driver of linux kernel 2.0 and above)

## Slide 14: Scenario 4
AP is Synchronous concurrent and non AP STA has support for multiple band/channel and can operate on all bands/channels simultaneously but independently at any instant
  The primary channel is decided by AP
  Any change of the STAs traffic from one channel to another channel can be done by Agile multiband or FST
  AP has one unique MAC address and non AP STA may have one or multiple MAC addresses
  Non contiguous OFDMA can be used to communicate with the STA and allocation can happen to STA at any band
New concepts
  There can be multiple primaries (the TGbe may decide against it) or the non AP STA may be concurrently connected to different APs
  The non AP STA can be parked anywhere (any channel/band)
    Need new rules for CCA if the STA is not parked on primary and how to asynchronously communicate from non AP STA
The above two sub-bullets warrant new protocol mechanisms
Helps QoS, load balancing and efficient spectrum utilization
Efficient from non AP STA perspective

## Slide 15: Scenario 5
AP is Synchronous concurrent and non AP STA has is similar to AP
Although this appears new, it is new at RF layer to mixed signal layer and once it reaches PHY, it is processed as a single stream
Efficient spectrum utilization, peak rate achievement and also very expensive
  Similar to operating STA in 160 MHz mode that is done today
If the AP were to pick channels in different bands efficiently, then once can reach high spectrum utilization
Power hungry from non AP STA perspectice

## Slide 16: What is there in revmd?
Revmd 2.3 says the following
  Architecture well defined and let us look at the architecture explanation
  The architecture already envisions multiband device with support for multiple bands/channels

## Slide 17: What is there in revmd?
Current draft
  Architecture well defined
  FST is approx. 9 years old
Security and control can be redesigned for new scenarios for 11be
Similarities with MLA (Document 823/19)
  No need to introduce MLO device concept as it is there in both the figures.
  MLO entitiy is already there (MLLE is same as in FST architecture)
  See next slide

## Slide 18: Similarities between 0823/19 and Current Architecture
MLO Entity already exists. If there is one MAC SAP it is transparent FST architecture
  BA, Security PN is maintained by multiband entity of FST
  This does not preclude us developing new feature with same architecture it TGbe determines that it is required
MLO device is nothing but non transparent FST where multiple MAC SAPs are exposed to higher layers
  Additionally MLO device forces upper layers to make scheduling decisions based in link conditions

## Slide 19: What is there in revmd?
Additionally, if TGbe wants to redesign FST there is a way as it does not preclude simultaneous operation (section 11)
  It is clear that FST can be kept alive in both bands at the same time
  It is also clear that the FST session is kept alive in old band even if the data moves in the new band
  The author does not advocate to use FST but only wants to point out that architecture exists in draft and we can create new features for multi-link by referencing to it

## Slide 20: Practical Implementation
Bonding driver exists in linux implementation since the inception of kernel 2.0 of FST in some practically available system and that will accomplish most of the scenarios outlined in MLA presentation (Figure courtesy: Carlos/Intel)
https://www.kernel.org/doc/Documentation/networking/bonding.txt
CFG80211
Bonding Driver
wlan0
11ac device
wpa_supplicant / hostapd
Network LIB
Network stack
NL80211
User Space
FST Manager
Kernel
Traffic Control (TC)
MAC80211
wlan1
11ad device
Data switch control
Data
Data
Data
control
control
Bonding driver: is an open source
driver used for bonding multiple
network interfaces
Allows exposing a single IP/MAC address towards network stack
We use existing driver as-is to implement FST data path
switching
FST Manager: implements data switching policy
Supplicant: Single instance manages both interfaces to control FST state machine

## Slide 21: Summary
Multiband architecture in revmd is sufficiently general and allows scope for any new innovation to support 11be multi-link or carrier aggregation capabilities
In case the group wants to use FST, then there is a need to modify the transparent FST to adapt it to the concept of (maybe having multiple MAC addresses although this concept is extended in bonding driver of linux kernel 2.0)
  Multiband management entity or bonding driver that is already present presents one MAC SAP to higher layers
Need to clearly spell that security and other control actions in one band will automatically apply in multiple bands
  OCT is there in specification and may need to be simplified
Additionally at higher layer, MPTCP exists and can aggregate links across technologies and is active in most of the cellular and laptop products
  Most smartphones manufactured after 2016 support it
Based on above points, new architecture as proposed in 0823/19 needs further study if those architecture concepts are really required and wants to group to defer any strawpolls

## Slide 22: References
[1] https://www.wi-fi.org/discover-wi-fi/wi-fi-agile-multiband