## Slide 1: Discussion on Functional Requirements
Date: 2019-07-09
Authors:

## Slide 2
Abstract
In this contribution, we discuss functional requirements for AP to advertise eBCS capabilities and/or services.

## Slide 3: Introduction (1/2)
802.11bc has agreed to have the following requirements regarding (eBCS) discovery [1]
  TGbc R3.5.1: 802.11bc amendment shall have a mechanism to facilitate discovery of 11bc-capable STAs.
  TGbc R3.5.2: 802.11bc amendment shall have a mechanism to facilitate the discovery of STAs consuming a particular broadcast service.
The requirements above seem to aim at non-AP STA side

## Slide 4: Introduction (2/2)
In addition, there are proposals to add the following requirements regarding (eBCS) discovery [2]
  TGbc R3.5.1: The 802.11bc amendment shall have a mechanism to facilitate discovery of 11bc-capable STAs.
    TGbc R3.5.1.1: The 802.11bc amendment shall describe the use of an extended capability bit to indicate eBCS capability.
  TGbc R3.5.2: The 802.11bc amendment shall have a mechanism to facilitate the discovery of STAs consuming a particular broadcast service.
    TGbc R3.5.2.1 The 802.11bc amendment shall describe a query/response mechanism for eBCS services.
    TGbc R3.5.2.2 The 802.11bc amendment shall be capable of indicating 0, 1, or multiple eBCS services within an eBCS response frame/message.
However, some of the eBCS AP related discovery seems to be missing

## Slide 5: The benefit for eBCS AP to indicate eBCS services in certain scenarios (1/2)
Stadium video distribution
  There may be a class of STAs that cannot transmit. In order to utilize eBCS service
    Option 1: all information of eBCS service and candidate eBCS APs must be loaded in firmware
    Option 2: eBCS may announce that they are capable of eBCS service and what types of eBCS services are provided
  Option 2 may provide more implementation and operation flexibility
Many other scenarios including ITS, multi-channel/multi-lingual/emergency broadcast, etc
  An eBCS AP announcing its eBCS services may speed up the process of set up eBCS service

## Slide 6: The benefit for eBCS AP to indicate eBCS services in certain scenarios (2/2)
UL Sensor Broadcast
  eBCS APs indicating that they provide UL Sensor Broadcast service may improve reliability of uplink broadcast

## Slide 7: Proposed Update to functional requirement document
TGbc R3.5.3: The 802.11bc amendment shall have a mechanism for eBCS APs to advertise their eBCS capabilities and eBCS services provided.

## Slide 8
References
[1] IEEE 11-19/151r3, 802.11bc Functional Requirements Document, June 2019
[2] IEEE 11-19/1001r1, Functional Requirements Document Proposed Update, July 2019