## Slide 1: 20MHz Channel Discussion Status
Date: 2019-07-17
Authors:
James Lepp, BlackBerry

## Slide 2: 20 MHz Contributions
4 contributions have been made during MAC ad-hoc meeting on Tuesday July 16
  11-19/1076 Liwen Chu (Marvell) medium access with 20 MHz BW
  11-19/1105 Hanseul Hong (Yonsei Univ) Study on 20 MHz Channel Access Schemes
  11-19/1156 Onn Haran (AutoTalks) 20 MHz channel usage options
  11-19/1103 Insun (LGE) 20 MHz channel access in 11bd: Follow-up
Consensus haven’t been reached

## Slide 3: Possible agreements
Common understanding that in the OCB context, using exact 11n parameters for backoff on the secondary channel, is unfair to the 10 MHz OCB traffic on that secondary channel (thus insufficient to meet the PAR).
  Group seems to agree that it is desired to match secondary channel detection with primary channel detection
Support for the idea that the group should consider a solution that avoids requiring two receivers in a 20 MHz 11bd STA.
  While this concept of “receivers” is an implementation detail, desire is to create write this standard in a way that minimizes this particular implementation complexity.
10 MHz legacy traffic needs to be accounted for, in both primary and secondary channel

## Slide 4: Unresolved
How to define primary and secondary channels during OCB operation
  In particular, some proposals don’t need to distinguish half the 20MHz as primary and half as secondary. Some proposals do.
What should be the detection sensitivity and timing of secondary channel and how to achieve that?
  There were different mechanisms presented, but no consensus yet on one preferred.
20MHz channel access scheme
  Allow 20 MHz only transmission scheme?
  Allow use of 20 MHz with 10MHz fallback (if secondary channel is busy)?
  Allow only one or both of the above two modes?

## Slide 5: Possible Straw Poll
Do you agree to add the following functional requirements to the 802.11bd FRD?
11bd 20 MHz channel access mechanism shall require one receiver only.
11bd 20 MHz channel access shall apply identical detection sensitivity on both 10 MHz channels
Y/N/A
(split in two if one is more agreeable than the other)