## Slide 1: Multi-Link Operation Management
Date: 2019-09-14
Authors:

## Slide 2: Recap: Multi-link logical entity (MLLE) architecture [1]
A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
AP
1
operating
on
2
.
4
GHz
AP
2
operating
on
5
GHz
AP
3
operating
on
6
GHz
Multi
-
link AP logical entity
Non
-
AP STA
1
Non
-
AP STA
2
Non
-
AP STA
3
Link
1
Link
2
Link
3
Multi
-
link non
-
AP logical entity

## Slide 3: Motivation
This contribution proposes how to manage multi-link for QoS, load-balancing and power saving.

## Slide 4: Motivation
Multi-link operation can improve the per-session peak throughput by exchanging frames on multiple links, in a non-congested environment.
Also, in a congested environment, it can improve the spectrum efficiency by more dynamically balancing the traffic load over multiple links.

## Slide 5: Motivation
In this congested scenario, the AP may need to dynamically determine for each non-AP STA one or more links on which frames can be exchanged or not.
Also, the non-AP STA needs to dynamically signal one or more links on which frames can be exchanged or not.
  The non-AP STA can signal that more links can be used for frame exchanges when it has more buffered traffic.
  Or, the non-AP STA can signal that one or more links can’t used for frame exchanges for the purpose of power saving and in-device resource management.

## Slide 6: Motivation
This contribution proposes a signaling to dynamically enable/disable link(s).
Supported multi-link
Enabled multi-link
[Follow existing PSM]
Disabled multi-link
[Can be turned off]

## Slide 7: Terminologies
Supported multi-link set: One or more links on which the multi-link operation is supported.
Enabled multi-link set: One or more links on which frames can be exchanged through the multi-link operation.
Disabled multi-link set: One or more links on which frames can’t be exchanged through the multi-link operation.

## Slide 8: Multi-link Operation Management (1/4)
An MLLE identifies which links support the multi-link operation during the multi-link operation setup phase.
The MLLE also exchanges the multi-link capabilities (e.g., the in-device coexistence interference level) during the multi-link operation setup phase.

## Slide 9: Multi-link Operation Management (2/4)
The AP MLLE determines and signals the enabled multi-link set for each TID/all TIDs to the non-AP MLLE.
  The enabled multi-link set of the non-AP MLLE shall be one or more links in the supported multi-link set of the non-AP MLLE but not in the disabled multi-link set most recently received from the non-AP MLLE.
A non-AP MLLE also may signal its preferred enabled multi-link set to the AP MLLE.

## Slide 10: Multi-link Operation Management (3/4)
The non-AP MLLE may determine one more links as the disabled multi-link set for the purpose of power saving and in-device resource management.
The non-AP MLLE may signal its disabled multi-link set to the AP MLLE.
  The disabled multi-link set shall be one or more but not all links in the supported multi-link set of the non-AP MLLE.

## Slide 11: Multi-link Operation Management (4/4)
The AP MLLE and the non-AP MLLE updates the enabled multi-link set whenever it transmits or receives a frame containing either the enabled multi-link set or the disabled multi-link set.
The AP MLLE and the non-AP MLLE can exchange frames using the MLO only on link(s) which are in the enabled multi-link set but not in the disabled multi-link set.

## Slide 12: Multi-link Operating Mode Example (1/2)
When the MLLE supports concurrent link operation
  A frame having the enabled multi-link set Info is sent by an AP MLLE.
  A frame having the disabled multi-link set Info is sent by a non-AP MLLE.
Link1
Link2
Link3
Link4
Association Request
Association Response
Data frame exchange
Frame having Enabled multi-link Info
Frame having Disabled multi-link Info
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Enabled multi-link
Enabled multi-link
Enabled multi-link
Contains Info on enabled link 1, 2, 3, 4
Contains Info on enabled link 1, 2
Contain Info on disabled link 1, 3, 4

## Slide 13: Multi-link Operating Mode Example (2/2)
When the MLLE does not support concurrent link operation
  A frame having the enabled multi-link set Info is sent by an AP MLLE.
  A frame having the disabled multi-link set Info is sent by a non-AP MLLE.
Link1
Link2
Link3
Link4
Association Request
Association Response
Data frame exchange
Frame having Enabled multi-link Info
Frame having Disabled multi-link Info
Data frame exchange
Enabled multi-link
Contain Info on enabled link 1
Contain the Info to disable link 1
Enabled multi-link
Contain Info on enabled link 2

## Slide 14: Conclusion
In this contribution, we propose the signaling mechanism for the enabled multi-link set and the disabled multi-link set.
  A non-AP MLLE can turn off the radio of its disabled multi-link set, for the purpose of power and other resource management.
  For the purpose of power saving and other resource management of the enabled multi-link set, existing per-link power management mechanisms can be utilized.

## Slide 15: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0773-03-00be-multi-link-operation-framework.pptx

## Slide 16: SP1
Do you support defining the following terminologies
  Supported multi-link set : One or more links on which the multi-link operation is supported.
  Enabled multi-link set : One or more links on which frames can be exchanged through the multi-link operation.
  Disabled multi-link set : One or more links on which frames can’t be exchanged through the multi-link operation.

## Slide 17: SP2
Do you support the following multi-link operation?
  An AP MLLE and a non-AP MLLE exchange their supported multi-link set.
  The AP MLLE signals the enabled multi-link set of the non-AP MLLE in the TBD format to the non-AP MLLE.
    The enabled multi-link set of the non-AP MLLE shall be one or more links in the supported multi-link set of the non-AP MLLE but not in the disabled multi-link set most recently received from the non-AP MLLE.
  The non-AP MLLE may signal its disabled multi-link set in the TBD format to the AP MLLE.
    The disabled multi-link set shall be one or more but not all links in the supported multi-link set of the non-AP MLLE.
  The AP MLLE and STA MLLE can exchange frames using the MLO only on link(s) which are in the enabled multi-link set but not in the disabled multi-link set.