## Slide 1: Multi-Link Operation Management
Date: 2019-11-13
Authors:

## Slide 2: Recap: Multi-link logical entity (MLLE) architecture [1]
A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
AP
1
operating
on
2
.
4
GHz
AP
2
operating
on
5
GHz
AP
3
operating
on
6
GHz
Multi
-
link AP logical entity
Non
-
AP STA
1
Non
-
AP STA
2
Non
-
AP STA
3
Link
1
Link
2
Link
3
Multi
-
link non
-
AP logical entity

## Slide 3: Motivation
This contribution proposes how to manage multi-link for QoS, load-balancing and power saving.

## Slide 4: Motivation
Multi-link operation can improve the per-session peak throughput by exchanging frames on multiple links, in a non-congested environment.
Also, in a congested environment, it can improve the spectrum efficiency by more dynamically balancing the traffic load over multiple links.
  The AP dynamically determines for each non-AP STA one or more links on which frames can be exchanged or not. As the AP informs those updates, the non-AP STA moves its operation links for the load balancing purpose.

## Slide 5: Motivation
The non-AP STA may also need to dynamically signal one or more links on which frames can be exchanged or not.
  The non-AP STA can signal that more links can be used for frame exchanges when it has more buffered traffic.
  Or, the non-AP STA can signal that one or more links can’t be used for frame exchanges for the purpose of power saving and in-device resource management.

## Slide 6: Motivation
This contribution proposes a signaling to dynamically enable/disable multiple link(s).
Supported multi-link set
Enabled multi-link set
[Follow existing PSM]
Disabled multi-link set
[Can be turned off]
Negotiated multi-link set

## Slide 7: Terminologies
Supported multi-link set: One or more links on which the multi-link operation is supported.
Negotiated multi-link set: One or more links on which the multi-link operation set up is negotiated.
Enabled multi-link set: One or more links on which frames can be exchanged through the multi-link operation.
Disabled multi-link set: One or more links on which frames can’t be exchanged through the multi-link operation.

## Slide 8: Multi-link Operation Management (1/3)
An MLLE identifies which links of the peer MLLE support the multi-link operation during the multi-link operation setup phase.
  The MLLE also exchanges the multi-link capabilities (e.g., the in-device coexistence interference level) during the multi-link operation setup phase.

## Slide 9: Multi-link Operation Management (2/3)
After the multi-link operation setup, an MLLE (an AP MLLE or a non-AP MLLE) may determine to change the enabled multi-link set associated with the peer MMLE for each TID/all TIDs.
  The enabled multi-link set of the non-AP MLLE shall be one or more links in the negotiated multi-link set of the non-AP MLLE.
In such case,
  The MLLE performs a negotiation in TBD format with the peer MLLE, to update the current enabled multi-link set.
    When the responding MLLE can’t accept this updated, it can reject the change of the enabled multi-link set.

## Slide 10: Multi-link Operation Management (3/3)
The AP MLLE and the non-AP MLLE can exchange frames using the MLO only on link(s) which are in the enabled multi-link set, subject to STA power states.
  For the purpose of power saving and other resource management,
    On the enabled multi-link set, the existing per-link power management mechanisms can be utilized.
    On the disabled multi-link set, the non-AP MLLE can turn off the radio.

## Slide 11: Multi-link Operating Example
After the multi-link setup, the enabled multi-link set can be updated, which can be initiated by any MLLE.
Link1
Link2
Link3
Link4
Multi-link Association Exchange
Data frame exchange
Multi-link Update Exchange
Multi-link Update Exchange
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Data frame exchange
Enabled multi-link
Enabled multi-link
Enabled multi-link
Contains Info on enabled link 1, 2, 3, 4
Contains Info on enabled link 1, 2
Contain Info on enabled link 1
Data frame exchange
Peer MLLME accepts this update.
Peer MLLE rejects this update.

## Slide 12: Conclusion
In this contribution, we propose the signaling mechanism for dynamically update the enabled multi-link set and the disabled multi-link set.

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0773-03-00be-multi-link-operation-framework.pptx

## Slide 14: SP1
Do you support the following multi-link operation?
  Define a TID-to-link mapping mechanism among the setup links of a multi-link logical device (MLD).
    TID-to-link mapping can have the same or different link-set for each TID unless a non-AP MLD indicates to be required the same link-set for all TIDs in the multi-link setup phase.
      NOTE: Such declaration method by the non-AP MLD is TBD (implicit or explicit).
    The TID to link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
      Format TBD
        Note: When the responding MLLE can not accept the update, it can reject the TID link mapping update.