## Slide 1: “Issue” survey results for IEEE 802.11 Coexistence Workshop in Vienna on 17 July 2019
6 August 2019
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: This report summarises the survey on coex issues discussed at the IEEE 802.11 Coexistence Workshop
  The IEEE 802.11 Coexistence Workshop was held from 1-10 pm on 17 July 2019 in Vienna, Austria
  After the workshop, a survey was conducted on various issues raised at the workshop, with results as shown in this report
    Note: all comments are included in the Appendices
  The results of this voluntary survey only represent the views of those that responded to the post workshop survey on coexistence issues:
    They may or may not represent the views of other attendees at the workshop (depending on whether the survey sample is random)
    They do not represent the views of the many stakeholders who did not attend the workshop (attendance were biased towards Wi-Fi stakeholders)
  Care should be taken in using these results to draw any conclusions about coexistence issues between Wi-Fi and NR-U/LAA

## Slide 3: The survey provided insight into many open coexistence issues
Workshop survey summary
  Q1: The vast majority of respondents prefer that their responses are anonymous
  Q2: Almost half of attendees responded to the issues survey
  Q3: There is a strong preference for independent 3GPP/IEEE 802.11 standards, with better collaboration
  Q4: A large majority want ETSI BRAN to have a role in coexistence, but there is disagreement on the role
  Q5: A large majority are in favour of the use of a common preamble in some form
  Q6: Almost half of survey respondents wanted a common preamble based on 802.11a in some form
  Q7: Banning short LBT for DRS gained the highest number of responses, but many opinions are unknown
  Q8: Preambles & thresholds are the most important coexistence issues, but others are important too
  Q9: Most intend to participate in IEEE 802.11 WG but many will contribute to ETSI BRAN & 3GPP RAN/RAN1

## Slide 4: Q1: The vast majority of respondents prefer that their responses are anonymous
Q1 Responses to this survey will be published anonymously, unless you consent to having your name and affiliation publicly associated with your answers. Do you consent?
  Given the high proportion who wanted anonymity, the survey collector (Andrew Myles) has decided to maintain anonymity for all
Chart: Respondents
| Yes | No
Responses | 10 | 56

## Slide 5: Q2: Almost half of attendees responded to the issues survey
Q2 What is your name and affiliation? This information will be used to validate your responses. It may also be publicly associated with your responses if you provide consent in Q1.
  66 responses were received (as of CoB on Friday, 2 August 2019)
  There were about 145 people in attendance at the workshop, representing a response rate of almost 50%
  The distribution of stakeholders with Wi-Fi & NR-U/LAA interests is roughly the same as the operational survey (difference of 8 people)
    NR-U/LAA interests: 39%
    Wi-Fi interests: 70%
    Other interests: 16%

## Slide 6: Q3: There is a strong preference for independent 3GPP/IEEE 802.11 standards, with better collaboration
Q3 During the IEEE 802.11 Coexistence Workshop a few speakers raised the question of how the IEEE 802.11 WG & 3GPP RAN should collaborate together in the future to promote good coexistence in the 6 GHz (and 5 GHz) band. How should the organisations work together?
Chart: 
| Work independently, collaboration similar to the past | Work independently, with better collaboration than in the past | Something else to promote good coexistence | Nothing, other forces will ensure coexistence | Nothing, there will only be one winner | Don't know | Prefer not to say
Responses | 0.21212 | 0.62121 | 0.090909 | 0 | 0.015152 | 0.015152 | 0.045455
n = 66

## Slide 7: Q3: The survey asked about various ways for IEEE 802.11 WG & 3GPP RAN to address coexistence
Q3 answer key
  Work independently, collaboration similar to the past
    The IEEE 802.11 WG & 3GPP RAN should specify their standards independently, with collaboration and coordination processes for issues related to coexistence between Wi-Fi & LAA/NR-U in 6 GHz following similar processes as in the past for 5 GHz (ie Liaison Statements, some common participation and the occasional workshop).
  Work independently, with better collaboration than in the past
    The IEEE 802.11 WG & 3GPP RAN should specify their standards independently, but they should also establish improved collaboration and coordination processes in the future with a goal of establishing true consensus across the organisations on issues related to coexistence between Wi-Fi & LAA/NR-U in 6 GHz.
  …

## Slide 8: Q3: The survey asked about various ways for IEEE 802.11 WG & 3GPP RAN to address coexistence
Q3 answer key
  ...
  Something else to promote good coexistence
    The IEEE 802.11 WG & 3GPP RAN should do something else to promote good coexistence between Wi-Fi & LAA/NR-U in 6 GHz.
  Nothing, other forces will ensure coexistence
    The IEEE 802.11 WG & 3GPP RAN should do nothing in particular to promote good coexistence between Wi-Fi & LAA/NR-U in 6 GHz because other forces will ensure it occurs anyway.
  Nothing, there will only be one winner
    The IEEE 802.11 WG & 3GPP RAN should do nothing in particular to promote good coexistence between Wi-Fi & LAA/NR-U in 6 GHz because good coexistence is not important - only one technology will succeed in the long term anyway.

## Slide 9: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3 survey & comment summary
  The survey responses indicate the vast majority (83%) want 3GPP RAN & IEEE 802.11 WG to develop their standards independently but also to collaborate on matters of common interest related to coexistence
  There is a general recognition that the current collaboration methods are not working that well, with 62% wanting better collaboration methods vs 21% wanting to use similar methods as the past
  The associated comments are diverse with no coherent theme; there is apparently not a clear and obvious way for 3GPP RAN & IEEE 802.11 WG to collaborate more effectively on coexistence issues
  A few comments highlighted the urgency of resolving any coexistence issues, noting it would need commitment from the leaderships and openness from the two communities to make concessions

## Slide 10: Q4: A large majority want ETSI BRAN to have a role in coexistence, but there is disagreement on the role
Q4 During the IEEE 802.11 Coexistence Workshop it was noted by at least one speaker that ETSI BRAN had taken the role of "referee" on coexistence issues in the 5 GHz band by specifying quite detailed adaptivity requirements in EN 301 893. While the scope of EN 301 893 is Europe, it has a global influence. What role should ETSI BRAN take in relation to coexistence issues in the 6 GHz band when specifying EN 303 687?
Chart: 
| Similar role, EN 301 893 as starting point | Similar role, “clean sheet” as starting point | Specify high level adaptivity requirements only | Don’t specify adaptivity requirements | Something else | Don't know | Prefer not to say
Responses | 0.33333 | 0.15152 | 0.24242 | 0.045455 | 0.045455 | 0.090909 | 0.090909

## Slide 11: Q4: The survey asked about various roles for ETSI BRAN in resolving coexistence issues
Q4 answer key
  Similar role, EN 301 893 as starting point
    ETSI BRAN should take a similar role in the 6 GHz band as it took in the 5 GHz band, using the detailed 5 GHz adaptivity requirements in EN 301 893 as a starting point when defining EN 303 687.
  Similar role, “clean sheet” as starting point
    ETSI BRAN should take a similar role in the 6 GHz band as it took in the 5 GHz band, defining detailed adaptivity requirements, but starting with a "clean sheet" when defining EN 303 687.
  …

## Slide 12: Q4: The survey asked about various roles for ETSI BRAN in resolving coexistence issues
Q4 answer key
  ...
  Specify high level adaptivity requirements only
    ETSI BRAN should specify only high level adaptivity requirements in EN 303 687, relying on other organisations (such as IEEE 802.11 WG, 3GPP RAN and the promoters of other technologies) to collaborate and coordinate on detailed mechanisms that achieve good coexistence between current and future technologies.
  Don’t specify adaptivity requirements
    ETSI BRAN should not specify any adaptivity requirements in EN 303 687, relying on other organisations (such as IEEE 802.11 WG, 3GPP RAN and the promoters of other technologies) to collaborate and coordinate on how to achieve good coexistence between current and future technologies.

## Slide 13: Q4: There is not consensus on the role (if any) that ETSI BRAN should take in promoting coexistence
Q4 survey & comment summary
  A large majority of respondents to the survey (72%) want BRAN to have a role in defining and enforcing “fair” coexistence
  About half (48%) want BRAN to define detailed requirements in 6 GHz , based on 5 GHz adaptivity (33%) or using a “clean sheet” (15%)
    Comments highlighted that BRAN had done a good job in the 5 GHz band and has a proven record as a “referee” for industry, driven by industry
  A significant number want ETSI BRAN to restrict itself to high level requirements (24%), or not set any rules at all (5% - leaving it to industry)
    Comments supporting these answers highlighted there is risk of innovation being blocked/delayed and there are philosophical objections to a European body (or indeed any non-industry body) setting detailed coexistence rules
  There is some recognition that if industry does not collaborate then regulators (in Europe?) will probably step in to enforce “fair” coexistence

## Slide 14: Q5: A large majority are in favour of the use of a common preamble in some form
Q5 Various presentations at the IEEE 802.11 Coexistence Workshop discussed the possibility of defining a common preamble between IEEE 802.11ax/be and NR-U/LAA in the 6 G Hz band. The use of a common preamble would allow symmetric access for both technologies using both preamble detection and energy detection, similar to what Wi-Fi does today. Other presentations proposed using energy detection-only as the basis of symmetric access. After hearing the arguments, what is your preference?
For the purposes of this question, if a preamble is used by a device then it is assumed the device will both transmit the preamble and respect the preamble on reception.
Note that the example thresholds in the answers are derived from the current 5 GHz rules, and are included for illustration purposes. They may be refined in the context of 6 GHz operation.

## Slide 15: Q5: A large majority are in favour of the use of a common preamble in some form
Chart: 
| Common mandatory preamble | Common optional preamble | No common preamble, but 802.11a preamble allowed | Energy detection only | Something else | Don't know | Prefer not to say
Responses | 0.39394 | 0.18182 | 0.060606 | 0.090909 | 0.10606 | 0.060606 | 0.10606
n = 66

## Slide 16: Q5: The survey asked about various options for the use (or not) of a common preamble
Q5 answer key
  Common mandatory preamble
    A common preamble should be specified, and should be mandatory to use. The use of a common preamble at a low threshold (eg -82 dBm) will allow the use of energy detection at a high threshold (eg -62 dBm)
  Common optional preamble
    A common preamble should be specified, but should be optional to use. The use of a common preamble at a lower threshold (eg -82 dBm) than an energy detection-only threshold (eg -72 dBm) will allow the use of energy detection at a higher threshold (eg -62 dBm).
  …

## Slide 17: Q5: The survey asked about various options for the use (or not) of a common preamble
Q5 answer key
  ...
  No common preamble, but 802.11a preamble allowed
    A common preamble should not be specified, but any implementation is free to use the 802.11 based preamble as the basis of coexistence. The use of the 802.11 preamble at a lower threshold (eg -82 dBm) than the energy detection-only threshold (eg -72 dBm) will allow the use of energy detection at a higher threshold (eg -62 dBm). Note that this is the status quo.
  Energy detection only
    Preambles should not be used to enable coexistence, energy detection-only should be used instead. In this case there will be a single energy detection threshold (eg -72 dBm)

## Slide 18: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5 survey & comment summary
  The survey results suggest a large majority (63%) are in the favour of using a common preamble in some form, with 39% wanting it mandatory
  The comments suggest a wide diversity of opinions
    Some advocated an 802.11a preamble, and some were adamantly against!
    Allegations were made that both 3GPP RAN & IEEE 802.11 WG are too inflexible to accept a compromise, having both determined their directions
    Concerns were expressed about complexity of a common preamble and the weakness of evidence supporting the use of a common preamble
    One suggestion was to give up, defining some spectrum for non LBT use
  On a more positive note, there are some ideas for progress
    Use the preamble detection mechanism suggested by AT&T
    Don’t specify a preamble but require detection of all systems at -82 dBm
    Form a joint collaboration group to resolve the preamble question

## Slide 19: Q6: Almost half of survey respondents wanted a common preamble based on 802.11a in some form
Q6 If a common preamble is defined for use by all technologies, what should it be based on?
Chart: 
| IEEE 802.11a preamble | IEEE 802.11a preamble, but with the possibility of "correlator-based physical carrier sensing" (see 3-11 by Ralf Bendlin from AT&T) | A new common preamble | Something else | Don't know | Prefer not to say
Responses | 0.25 | 0.1875 | 0.25 | 0.078125 | 0.10938 | 0.125
n = 64

## Slide 20: Q6: A majority of respondents are in favour of use of 802.11a preamble but there is not consensus
Q6 survey & comment summary
  Almost half of the survey respondents (44%) want a common preamble based on 802.11a in some form, whereas about one quarter want a new common preamble
  There was a lot of interest in the AT&T correlator proposal, subject to proper evaluation …
  … however, a number of comments highlighted the importance of the length field in any preamble
  Some asserted a need for Wi-Fi community to compromise on the preamble (to show flexibility?), noting there is no legacy in 6 GHz …
  … however, others expressed a preference for the 802.11a preamble, on basis it exists and can be easily implemented by NR-U devices

## Slide 21: Q7: Banning short LBT for DRS gained the highest number of responses, but many opinions are unknown
Q7 There has been lots of discussion over many months in the IEEE 802.11 WG, ETSI BRAN, 3GPP RAN/RAN1 and the IEEE 802.11 Coexistence Workshop about the impact on coexistence of the use of the short LBT access mechanism (aka Cat 2) for DRS (and possibly other purposes) by LAA/NR-U. Based on this discussion, what is your current view?
Chart: 
| Short LBT banned | Short LBT allowed | Something else | Don't know | Prefer not to say
Responses | 0.38462 | 0.24615 | 0.015385 | 0.21538 | 0.13846
n = 65

## Slide 22: Q7: The survey focused on two main options for the use of short LBT for DRS by NR-U
Q7 answer key
  Short LBT banned
    NR-U should not use short LBT for DRS access because it causes potential harm to other technologies, the benefit to NR-U is small and its use is contrary to the principle that all access in unlicensed spectrum should use the traditional back-off mechanism.
  Short LBT allowed
    NR-U should use short LBT for DRS access, as planned, because it causes no harm to other technologies and it enables NR-U systems to synchronize more easily. This synchronization may actually assist other technologies by making LAA/NR-U more efficient.

## Slide 23: Q7: There was no consensus on the use of short LBT for DRS by NR-U
Q7 survey & comment summary
  Banning no LBT gained a higher number of responses (38%) than not (25%) , but many opinions are unknown (36%)
  There were not a large number of comments, but they were diverse:
    No LBT is complexly unacceptable
    LBT is OK as long as regulations allow it
    LBT is OK as long as it is not used too often
  A number of comments asserted that 802.11 also uses short LBT for Beacons (based on an unconfirmed report in ETSI BRAN by R&S)
    Note: the R&S report will be discussed at an upcoming ETSI BRAN meeting

## Slide 24: Q8: Preambles & thresholds are the most important coexistence issues, but others are important too
Q8 The presentation from the Wireless Broadband Alliance (3-1) highlighted a variety of potential coexistence issues in both 5 GHz and 6 GHz operations. Which of these issues are important?
n = 65
Chart: 
| Use of 802.11 preambles or common preambles for coexistence | Energy Detection only vs. Preamble or Energy Detection vs. both | Multi-channel sharing mechanisms | Use of no/short LBT for control signaling | Blocking energy/reservation signals | Synchronous access proposals in U-NII-7 | Contention Window adjustment mechanisms with delayed acknowledgements | Something else | Don't know | None of these | Prefer not to say
Responses | 0.57143 | 0.55556 | 0.31746 | 0.38095 | 0.30159 | 0.1746 | 0.2381 | 0.063492 | 0.063492 | 0.031746 | 0.095238

## Slide 25: Q8: The concern in the workshop survey was similar to but greater than the equivalent WBA survey
n = 65
Chart: 
| Use of 802.11 preambles or common preambles for coexistence | Energy Detection only vs. Preamble or Energy Detection vs. both | Multi-channel sharing mechanisms | Use of no/short LBT for control signaling | Blocking energy/reservation signals | Synchronous access proposals in U-NII-7 | Contention Window adjustment mechanisms with delayed acknowledgements | Something else | Don't know | None of these | Prefer not to say
Post workshop survey | 0.57143 | 0.55556 | 0.31746 | 0.38095 | 0.30159 | 0.1746 | 0.2381 | 0.063492 | 0.063492 | 0.031746 | 0.095238
WBA survey | 0.5 | 0.36 | 0.36 | 0.22 | 0.1 | 0.08 | 0.04

## Slide 26: Q8: Preambles & thresholds are the most important coexistence issues, but others are important too
Q8 survey & comment summary
  The workshop survey indicates the use of preambles (57%) & thresholds (56%) are the most important coexistence issues
  However, there are many other coexistence related issues that are still important (between 20-40% are concerned) to many respondents
  Interestingly, the workshop survey results are similar to the equivalent WBA survey (although the workshop attendees are more concerned)
  The small number of comments on this question tended to take hard-line positions, both for and against these issues being important
    eg a couple of comments asserted none of the issues are important
  I suspect the comments are not representative of all views, but rather that people were getting tired answering the survey 

## Slide 27: Q9: Most intend to participate in IEEE 802.11 WG but many will contribute to ETSI BRAN & 3GPP RAN/RAN1
Q9: Thank you for your participation in this survey and the IEEE 802.11 Coexistence Workshop. In which forums are you planning to contribute to the further discussion of coexistence issues?
n = 64
Chart: 
| IEEE 802.11 WG | 3GPP RAN/RAN1 | ETSI BRAN | Nowhere | Other
Responses | 0.65625 | 0.3125 | 0.20312 | 0.078125 | 0.125

## Slide 28: Q9: Most intend to participate in IEEE 802.11 WG but many will contribute to ETSI BRAN & 3GPP RAN/RAN1
Q9 survey & comment summary
  Most survey respondents intend to participate in IEEE 802.11 WG (66%) on coexistence issues but many also plans to contribute to ETSI BRAN (20%) & 3GPP RAN/RAN1 (31%)
  The comments also suggested other fora will be used to discus coexistence issues:
    Wireless Broadband Alliance
    Wi-Fi Alliance
    Academia
    TCAM (EC’s Telecommunications Conformity Assessment and Market Surveillance Committee)
    3GPP RAN4

## Slide 29
Appendices

## Slide 30: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 1 of 7 pages
  The two organizations are submissions driven, it would be quite hard to impose any particular solution unless is proposed and supported by their members. Therefore the technical communications and individual networking between members in my opinion is the most effective way to generate solutions for spectrum sharing that will be accepted by both organizations.
  Regulatory bodies should also be actively involved.
  Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions.
    x 2 (with same affiliation)
  Good initial meeting. Only consensus seemed to be that there was some agreement that there is a problem to be solved. Should work on this soon, is it already too late for 802.11ax and 5G?

## Slide 31: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 2 of 7 pages
  Each side seems entrenched in its views and approach. Until or unless there is willingness to accept shared pain on both sides I don't think the status quo will change. Both sides have merits and drawbacks in their approach. It's probably a long road to work this one out. (No constructive suggestions unfortunately)
  Ideally a better way of collaboration should be defined. In the meantime, improved collaboration is required.
  The workshop is a step in the right direction, but there needs to be more stake-holder support.
  Organize additional workshops with stated goals of generating consensus on problem statement, channel access, AFC... A cross-organization Coexistence Assurance Document before specs are released. A position paper to FCC, ETSI, OFCOM, ... based on such a document.
  3GPP should not spend time and resources developing an alternative to 802.11 radio access, but should focus on fully integrating 802.11 radio access into their architecture.
  It would be always good to improve collaboration, but no option specifies how that should do and how it can work. So just choose the one mostly reflecting the current situation.

## Slide 32: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 3 of 7 pages
  The solutions that could be worked out by collaboration by 802.11 and 3GPP RAN will probably be significantly beneficial to both technologies, as any externally imposed solution by external entities (e.g. regulators, ETSI) is likely to be worse than an agreed solution.
  No fundamental progress will be possible without first establishing IPR rules and decision-making (e.g. voting) rules. Still, this might be a useful forum to educate 3GPP on the norms required to avoid a tragedy-of-the-commons scenario.
  Agreement between IEEE and 3GPP, then fix the decision in ETSI BRAN. Regulation alone will probably not solve the coexistence issue - If regulation should do so, the same discussions as currently in BRAN will be happen to influence regulators decision. Remaining problem: a third party could try to bypass such an IEEE/3GPP agreement

## Slide 33: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 4 of 7 pages
  The traditional collaboration and joint workshop doesn't seem to work very well since these workshops do not have any decision making power. In the past, my experience has been that after the workshop both IEEE and 3GPP go about their own business as is. In my view the responsibility for developing the coexistence between IEEE and 3GPP should be done by a joint task force between the two that has authority to make decision for both. This task force should be jointly chaired by 3GPP and IEEE.
  I wish I had a good answer for this.
  It would be nice to have the two organizations truly collaborate and come up with a coexistence solution that is future-proof in that as each standard evolves over time they can still coexist fairly. The goal should be that each can back-off to the other at the same level, preferably - 82dBm, which is a time-tested threshold value. In order to do so, each has to reliably recognize the other. This can be done via common preambles, but also by using known synchronization signals in each system.

## Slide 34: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 5 of 7 pages
  I think the IEEE Coexistence Workshop had the right sentiment, just execution and compressed schedule and poor quality control (Octoscope and Trinity College Dublin should have been eliminated by some form of review process) made it sub-optimal. More opportunities to get stakeholders co-located should be encouraged. An alternative would be to use ETSI BRAN for this, but the fear is that this will stifle innovation as draconian process gets imposed (Andy Gowans summed this up well).
  802.11 process would probably yield better coex solutions/influence if modelled after or moved in the direction of 3ggp way of working.

## Slide 35: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 6 of 7 pages
  The race to be the "first to market" in Greenfield (for unlicensed operations) spectrum in 6GHz can't be paused or stopped. Both 3GPP- and IEEE- technologies (as promoted by the vendor ecosystem) want to be there first. Seeing that 802.11ax implementations are already in the field (awaiting "6GHz band open for business" rulings), and that 3GPP Rel-16 timeline or content (of which NR-U is a feature set) is not changing, any effort to have "better" co-existence between IEEE- and 3GPP- technologies in unlicensed spectrum will involve the following:
    1. Commitment from respective leaderships to set out a hard deadline (within next 4 months) to force an outcome other than status-quo with the promise that specification update (if required) on both sides will be done in the desired timeframe
    2. Commitment from vendor eco-system to be open to constructive arguments If /1/ is realized, then it should be followed w/ another workshop (w/ limited allowed participation on a per company basis), in 30 days, with the singular aim of discussing details of the two approaches ("common preamble" vs "adjusting current ED thresholds") moderated in such a way as to force the bare-minimum which would satisfy field deployments. This workshop should prove to be indicative of whether further consensus is feasible.

## Slide 36: Q3: There was not a consensus on how to achieve good collaboration on coexistence issues
Q3: page 7 of 7 pages
  Are there any third party independent mediation services that can be employed in situations like this where a small team from each "side" could work together with neutral host? ETSI BRAN would be the backup plan.
  Good coexistence is keeping transmitters separate from each others receivers. ML and AI will extend what can be observed at transmitters. Today nobody has a handle on co-channel traffic five years from now. Any medium occupancy limits should be based on noise levels, not absolute limits. Where it is noisy transmitters should talk less.
  A common preamble must be agreed upon.
  Any coexistence of wireless technologies on the 6Ghz must have a coordinated approach between IEEE and 3GPP. WBA will consider having a strong role on this alignment by bringing the voice of the customer, the operators. Very important to identify clearly what are the use cases (scenarios) that can be impacted by the coexistence of these technologies. I am afraid many times people talk in general but in this cases is very important to talk on the specific scenarios,
  Coordination is needed to create a mutual success. A new process doesn't make sense. Both should strive to make applicable changes there were possible. Target: nobody loses, all win

## Slide 37: Q4: There is not consensus on the role (if any) that ETSI BRAN should take in promoting coexistence
Q4: page 1 of 4 pages
  In my opinion the regulators should allow (and recognize that) the engineers develop new technologies and generate innovative solutions. Therefore the regulators should be as general as possible in specifying (technology agnostic) rules for spectrum sharing
  Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions
    x 2 (with same affiliation)
  Seems like ETSI BRAN has a clear bias. It would be like the FCC specifying rules for the world. FCC seems like it does not want to be in that business and wants the industry to solve the issue, prefer to see ETSI BRAN do the same
  I'm far from an expert on the topic, but I don't see ETSI BRAN as an effective worldwide referee. They strike me as somewhat regionally biased, and not particularly agile. I'm more inclined to go with the wisdom of the OFCOM rep - get your acts together individually or you won't like it when regulators step in. Best would be to solve problems without needing a referee

## Slide 38: Q4: There is not consensus on the role (if any) that ETSI BRAN should take in promoting coexistence
Q4: page 2 of 4 pages
  Data from 5 GHz fields should be captured and analysed to help define the 6 GHz rules. No field data was presented at the workshop
  Without Wi-Fi incumbency, a clean slate is required while initially referencing 802.11 WG/3GPP
  3GPP does most of resolutions through consensus and submit the results to various standard bodies such as ETSI for regional endorsement. IEEE 802.11 and 3GPP should develop consensus through close collaboration and jointly submit to various regulatory/standard bodies requiring formalization in relevant specifications
  ETSI should stay very high level and regulate instead of imposing design
  This (no requirements) would be my preferred solution, but if this doesn't come to fruition, then I think ETSI BRAN should take on the "referee" role, using a "clean sheet" approach
  The citizenry's need for Wi-Fi in 6 GHz is the irresistible reality. The citizenry's need for small cell technology in 6 GHz or any other band, in unlicensed spectrum or any other licensing regime is de mininis as established by 5 years of market data. In general regulators should not hold back access to 6 GHz for leading technologies well adapted to unlicensed spectrum, with one caveat: regulators are advised to severely limit / exclude no-listen-before-TXOP because that encourages and allows designs that are too brittle for unlicensed spectrum

## Slide 39: Q4: There is not consensus on the role (if any) that ETSI BRAN should take in promoting coexistence
Q4: page 3 of 4 pages
  Too much details - prevent innovation - need a long to be agreed
  As I said the best solution is to have a separate joint task force to decide on the co-existence technology. ETSI BRAN is not the right body to do this since their rules ad views do not apply globally .. e.g. the US
  ETSI BRAN (or some other EU body) is required to define the regulations in the EU. Industry bodies could make recommendations to them. Using the existing EN as a starting point seems sensible given the desire to have a common WLAN standard applicable to both bands
  Adaptivity can be shown to not be serving the ISM band users well, contrary to what some presenters may think. Adaptivity needs a major overhaul for the 21st century. It is possible to be fixed, but we as a community first need to recognize that it is broken. To maybe borrow Dorothy Stanley's anecdote about Albert Einstein, think about the problem for 55 mins, or said by someone else, the first step to solving any problem is actually recognizing there is a problem

## Slide 40: Q4: There is not consensus on the role (if any) that ETSI BRAN should take in promoting coexistence
Q4: page 4 of 4 pages
  Unlike 5 GHz, 6 GHz spectrum range, limits of operations, and rules of operations are known to be different. Therefore, specifying adaptivity requirements in EN 303 687 (whether similar or different to 5 GHz is irrelevant) would serve limited benefit
  ETSI BRAN HS should support a wide variety of 5G applications (IOT, M2M, etc.) in 6 GHz, not just LAA. ML and AI will extend what can be observed at transmitters. Today nobody has a handle on co-channel traffic five years from now. Any medium occupancy limits should be based on noise levels, not absolute limits. Where it is noisy transmitters should talk less
  IEEE 802.11 AND 3GPP RAN (via individual members) should make absolutely sure that the work ETSI BRAN is doing is in the interest of BOTH SDOs for the Industry to set requirements on the use conditions. If it is not the interested parties to provide good Input in the end the Regulators might force something in the HS with both "communities" just losing
  ETSI has proven to be a good gatekeeper in the use of spectrum and can keep doing so, even when it is often cumbersome. However, don't invent the wheel again

## Slide 41: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 1 of 6 pages
  Although I choose the first one (common mandatory preamble), I am concerned about the fact that 3GPP and Wi-Fi are using different clock/sampling rate. To make the idea work may be too complex and costly
  I believe the workshop is intended to share the information and get clarified on doubts/questions by interacting with expert contributors to the standards. Workshop is neither a debate ground nor a place vote or straw poll in favor of any technology parameters (common preamble , ED/PD levels). Also, the simulation results and conclusions provided at workshop are varied and diversified. …
  … From the collaboration and coexistence point of view, I think if this kind of workshop leads to formation of an ad hoc group of experts from both IEEE 802 and 3GPP bodies to discus and come up with commonly agreed evaluation process and testing strategy to evaluate all proposals (common preamble. ED/PD levels etc.) to demonstrate effectiveness of proposals and finally select those parameter that would guarantee the coexistence both IEEE 802 and 3GPP technologies operating in unlicensed 5 GHz and 6 GHz. Of course, I also believe this is not going to be simple way forward but helps in building coordinated effort

## Slide 42: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 2 of 6 pages
  What "common preamble"? TGax never genuinely (or never at all) talked about common preamble in 6 GHz, instead voted for reusing 802.11a preamble. And WFA will soon have approved MRD for 11ax/ 6 GHz devices according to spec. Basically, "common preamble" topic is dead given TGax spec and WFA plan. It's long overdue for Coex SC and coex advocates within 802.11 WG to align their wording with what TGax, 802.11 WG, and WFA position ... Then the topic would be that 802.11/WFA take genuine steps and make changes in 11ax/6 GHz spec (such as processing of STF/LTF, PD/ED thresholds etc) so that LAA/NRU 6 GHz devices have some incentive to perform limited/full preamble processing
  From the discussions: Using a common preamble seems advisable, but given the difference in structure between IEEE and 3GPP protocols using the proposed IEEE preamble including a variable field doesn't seem like it will happen. 3GPP isn't going to adjust to accept the data field and act on it. Just power doesn't seem to work - either the level is to high and you miss users, or is so low you get false positives and can't claim an empty channel. Seems like the present -72 dBm is the best compromise if just doing power, and it isn't very good. The approach proposed by AT&T seems like a very sensible place to start - use the part of the preamble that is not dependant on data structure. Failing that you are favoring one system over another, given how different the approaches are

## Slide 43: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 3 of 6 pages
  Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions. Moreover, note that the ED threshold could be further discussed
  It should be found a common solution! Or the spectrum should be divided into an LBT-oriented and a synchronized area, which can be used by the respective other technology as soon as these access mechanisms are adhered to
  IEEE 802.11 based preamble should be adopted as common preamble
  Common preamble is just one way to facilitate fair co-existence, and more options (e.g. energy detection only) should also be further studied. Unfortunately, so far there is not much investigation of other options
  Need more insight for such an assessment

## Slide 44: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 4 of 6 pages
  Just to be clear when we say common preamble IT DOES NOT MEAN THE CURRENT IEEE preamble. The term common also implies that is jointly developed together. IEEE tends to believe that a common preamble usage implies 3GPP uses IEEE's preamble. That is not the right starting point and for the sake of compromise both 3GPP and IEEE should meet in the middle. So a NEW common preamble is designed that is used by both IEEE and 3GPP on top of any technology specific preamble or discovery signal they use
  I don't think that the common preamble is the only thing that shall be studied. Many presented results are contradictive, are obtained in corner or undefined scenarios, or with oversimplified model of operation. I would propose to start the work with defining common scenarios, clarification of the mode of operation, all parameters and studying the problems with testbed and simulation.

## Slide 45: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 5 of 6 pages
  Straight forward signal processing methods can be used to reliably detect the presence of Wi-Fi and 5G using the known synchronization signals (e.g. preambles) or signal structure (e.g. cyclic prefix) of each system. While a common preamble is an easy solution, it can also be constraining and lead to increased overhead. Each standard should simply specify a detection threshold (preferable - 82 dBm) at which it should back off to the other and leave the implementation to the device manufacturers. This is an approach that can be used for coexisting with other users of the spectrum as well.
  Successful coexistence relies on being able to detect other users of the medium, otherwise you end up transmitting over them. Therefore the detection method should be as sensitive as possible, which means using some form of correlation to give coding gain. Use of 802.11a preamble allows use of 802.11ax unchanged in 6GHz. The enhanced sensitivity should not be optional as without it you will disrupt other users to a greater extent. If you want a technology neutral solution, that has to be based on ED, which is inherently not as sensitive and will therefore give worse coexistence.

## Slide 46: Q5: Comments suggested a wider diversity of opinion on the common preamble than the survey results
Q5: page 6 of 6 pages
  Preamble-detect but not decode was presented by AT&T, with PD setting an ED threshold until energy below that threshold is detected, and the channel is assumed to be clear. I don't prefer that BRAN standardize AT&T proposal as it presumes 20 MHz channel operation for PD.
  Mandatory on both sides (IEEE & 3GPP). A simple approach like being proposed by AT&T might be a starting point. This entire topic needs further evaluation, but requires flexibility from both organisations

## Slide 47: Q6: A majority of respondents are in favour of use of 802.11a preamble but there is not consensus
Q6: page 1 of 4 pages
  No common preamble should be defined.
  Prefer the 802.11 preamble but would be willing to compromise if 3GPP would agree to using something
  From the discussions: Using a common preamble seems advisable, but given the difference in structure between IEEE and 3GPP protocols using the proposed IEEE preamble including a variable field doesn't seem like it will happen. 3GPP isn't going to adjust to accept the data field and act on it. Just power doesn't seem to work - either the level is to high and you miss users, or is so low you get false positives and can't claim an empty channel. Seems like the present -72 is the best compromise if just doing power, and it isn't very good. The approach proposed by AT&T seems like a very sensible place to start - use the part of the preamble that is not dependant on data structure. Failing that you are favoring one system over anther, given how different the approaches are.

## Slide 48: Q6: A majority of respondents are in favour of use of 802.11a preamble but there is not consensus
Q6: page 2 of 4 pages
  Need more data on this solution (AT&T proposal)
  No common preamble should be defined. Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions.
  This new proposal (from AT&T) may be promising but requires full technical evaluation for feasibility, complexity and performance.
  Option 2 (802.11a preamble) is a possibility but needs more study
  If a preamble is defined, it should be easily detected by all the RATs on the band.
  "Correlator - based physical carrier sensing" could be a viable option but I am not sufficiently familiar with the pros and cons of this concept.
  Wi-Fi 6 should forgo the legacy preamble (since there are no legacy systems in 6 GHz anyway) and work with 3GPP to design a new preamble that is acceptable to both standards.

## Slide 49: Q6: A majority of respondents are in favour of use of 802.11a preamble but there is not consensus
Q6: page 3 of 4 pages
  A common preamble should be a common signal not an information carrying channel. If it is an information carrying channel, the only information it should carry is the TXOP/COT length.
  There are two essential feature for coexistence provided by correlating STF/LTF and decoding the length field from the preamble. The correlation allows the start of a packet to be detected with full sensitivity but gives no indication of duration. The length field allows the duration of the transmission to be determined. Without the length field, you would have to rely on ED for the remainder of the packet, which is less sensitive. There are no suitable fields in the remainder of the packet which could be used for correlation based detection.
  A Wi-Fi radio is likely to be co-located with NR-U so re-use of existing preamble would be the most effective path.

## Slide 50: Q6: A majority of respondents are in favour of use of 802.11a preamble but there is not consensus
Q6: page 4 of 4 pages
  6GHz has no unlicensed incumbents. Therefore, it wouldn't be fair to ask 3GPP- ecosystem to implement preamble/sequence detection of 802.11a (L-STF/L-LTF and/or L-SIG). Similarly, it wouldn't be fair to ask IEEE- ecosystem to implement NR-SSBs/LTE-CRSs. However, both ecosystems could implement sensing and detection of a "new" sequence (X repetitions of Y-length OFDM symbol) say @ 60kHz SCS when operating in unlicensed bands @ say -82dBm (or lower). Whilst 1st wave of products will continue to be based on today's sensing mechanisms and thresholds, we'd rest assured that a future wave of products will conform to this 'new' common preamble.
  If not 11a preamble then no preamble.
  Some code in short training symbols, with 10 MHz and 20 MHz versions, low PAPR and simple to decode.
  This topic need to be more discussed among the end customer, the operators and have a strong view from them.
  Again, don't invent the wheel again

## Slide 51: Q7: There was no consensus on the use of short LBT for DRS by NR-U
Q7: page 1 of 2 pages
  Certain applications may benefit from short LBT, but the coverage of the application could be limited. Some kind of rules may need to be used.
  Note that it has also been observed (reported by Rhode & Schwartz) that there are existing Wi-Fi devices that make use of short (or no) LBT. Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions.
  However, such sort of access should occupy the channel no more than some very small threshold
  As long as regulation is not violated, didn't see any reason to limit such channel access scheme.
  That NRU is proposing short LBT for DRS is positive proof that NRU is not ready to operate in unlicensed spectrum. If a member of 802.11 proposed a technology to 802.11 that required short LBT, they would get virtually no affirmative votes, because the 802.11 group's experience makes them well aware of the short and long term pitfalls.

## Slide 52: Q7: There was no consensus on the use of short LBT for DRS by NR-U
Q7: page 2 of 2 pages
  BTW, some years ago LBT was introduced in EN 300 328 for the 2.4 GHz band. LBT of IEEE 802.11 is much shorter than LBT of IEEE 802.15.4, which is a penalty for 15.4. Advice by some Wi-Fi participants: Be faster!
  This, and other coexistence issues, need to be tested by the community on common test-beds, both hardware and software that can deliver reproducible results. The current evaluation methodology basically results in each side presenting results that bolster their case.
  Cat 2 LBT for DRS is similar to PIFS for beacons in 802.11. Only the duty cycle is higher (5% vs. 1-2%), so limiting the duty cycle further should be explored. There is some impact to other users, but this is acceptable if the duty cycle is small. This is a common approach in all forms of coex.

## Slide 53: Q8: Preambles & thresholds are the most important coexistence issues, but others are important too
Q8: page 1 of 1 pages
  Fair coexistence is important, but the aspects listed here do not cause significant problems in that respect
  Want both common preambles and a reasonable ED threshold. Should be mandatory for both sides
  All important, not knowledgeable enough to say which are critical
  These are all current complaints with 5GHz sharing. Starting from a clean slate should result in none of these issues if all vested stakeholders can agree to start again with fresh eyes for new ideas
  Not sure what 3, 6, 7 are so they may be important
  Fair coexistence is important, but the aspects listed here do not cause significant problems in that respect. Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions
  The crux of 6 GHz is how to mix using narrow channels with broad ones. 802.11 lacks carrier aggregation on the scale that 3GPP has. 11be tries to extend puncturing, but who knows how many simultaneous uplinks can be accommodated
  Once more important to have a strong feedback from operators

## Slide 54: Q9: Most intend to participate in IEEE 802.11 WG but many will contribute to ETSI BRAN & 3GPP RAN/RAN1
Q9: page 1 of 1 pages (those who selected “other”)
  Note that this survey has no official status and cannot be considered a representative indication of the views of the workshop participants. Further, as the workshop had no decision making authority, the responses to this survey also cannot be used to draw any conclusions or reach any decisions.
    x 2 (with same affiliation)
  Dissemination of the information to the ITU Members.
  3GPP RAN/RAN4
  TCAM
  As an academic, my interest lies in performing unbiased research in this area and presenting the findings in conferences and journal publications
  WFA and WBA
  Considering to develop a special program in WBA to help the industry to move forward and collaborate with all of the above organizations.