IEEE P802.11
Wireless LANs

| Proposed resolution to a few LB#240 CIDs on DMG/EDMG ranging |
| --- |
| Date: 2019-08-27 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Qi Wang | Apple, Inc. |  |  | qi_wang2@apple.com |
| Tianyu Wu | Apple, Inc. |  |  | tianyu@apple.com |
| SK Yong | Apple, Inc. |  |  | skyong@apple.com |

Introduction

Introduction

This submission contains proposals to resolve LB#240 CID- 1058, 2145 and 2146, all related to DMG/EDMG ranging.

| Comments: CID Page Clause Comment Proposed change Resolution 1058 21 8.3.4.4 Table 8-4 refers to LTF_SEQUENCE. What should be the value for DMG and EDMG which don't have LTF? Add text to specify the value for DMG and EDMG which don't have LTF Revised. Table 8-4 (Vector descriptions) lists the minimum parameter values required by the MAC or PHY in each of the parameter vectors. The “LTF_SEQUENCE” parameter only applies to PHY that performs the secured NTB ranging or TB ranging operation. In addition, “LTF_SEQUENCE” is not defined in the TRIGVECTOR. Therefore, it should not be part of Table 8-4. The resolution is to delete the “LTF_SEQUENCE” parameter and the associated text in Table 8-4 from the 11az spec. 2145 52 11.22.6.3.4 [Re-raising this comment from the comment collection, as it is not possible to determine from 18/1544r8 whether/how it was addressed. References are to the CC draft and hence may be wrong against D1.0.] "a DMGz/EDMGz Specific Parameters subelement" -- no such subelement is defined As it says in the comment (a few lines down it's an element -- make that consistent too) Revised. Agreed in principle. "a DMGz/EDMGz Specific Parameters subelement" no longer exists in 11az_D1.0 and 11az_D1.2 due to spec revisions since the comment collecting time. In 11az_D1.0 and 11az_D1.2, the term “The EDMGz Specific Parameters subelement” is used instead. 2146 52 11.22.6.3.4 [Re-raising this comment from the comment collection, as it is not possible to determine from 18/1544r8 whether/how it was addressed. References are to the CC draft and hence may be wrong against D1.0.] "a DMGz/EDMGz/ Specific Parameters subelement" -- spurious / Delete the last / Revised. Agreed in principle. "a DMGz/EDMGz Specific Parameters subelement" no longer exists in 11az_D1.0 and 11az_D1.2 due to spec revisions since the comment collecting time. In 11az_D1.0 and 11az_D1.2, the term “The EDMGz Specific Parameters subelement” is used instead. |  |
| --- | --- |

Proposed 11az spec modification:

Instruction to the editor: Delete the “LTF_SEQUENCE” parameter and the related text from Table 8-4.  The proposed modifications are in reference to the text in IEEE 802.11az_D1.2, and are indicated by the change marks as follows:

References:

1. IEEE Draft P802.11az_D1.2, Draft standard for information technology – telecommunications and information exchange between systems – local and metropolitan area networks – specific requirements – Part 11: Wireless LAN medium access control (MAC) and physical layer (PHY) specifications, Amendment 8: Enhancements for locationing

# Text boxes

Abstract

This submission contains proposals to resolve LB#240 CID-1058, 2145 and 2146, all related to DMG/EDMG ranging.