## Slide 1: 11bd Frame Format: Simulations
Date: 2019-09-15
Authors:

## Slide 2: Introduction
In previous meetings, preamble power boost and R-LSIG have been decided.
In this contribution, we will propose the preamble power boost level, and evaluate the auto-detection performance with RL-SIG.

## Slide 3: NGV Frame Format: Recap
LSTF+LLTF: power boost by x1 dB and x2 dB for BPSK modulation [1]
  Simulations to determine x1 and x2 value
R-LSIG added after L-SIG [2].
  RL-SIG provide better L-SIG decoding performance, ideally 3dB
  RL-SIG can also been used to auto-detect NGV PPDU format.
20MHz PPDU preamble will repeat 10MHz preamble.
NGV Portion
10MHz
LLTF
LSTF
L-SIG
RL-SIG

## Slide 4: Simulation Settings LTF Boost
10MHz PPDU: 11ac 20MHz DC2 + LDPC.
Pkt size: 300 bytes baseline.
Midamble
  Period – 10 symbols
  Format – Repeated 2x-Compressed (RC-LTF)
No CFO
Real carrier sensing and timing.
PER plots for LTF Boost
  LTF Boost = 0, 1, 2 ,3 dB
  STF Boost = 3 dB
  BPSK & BPSK DCM

## Slide 5: Rural LOS
L-LTF power boost doesn’t have much impact on the performance

## Slide 6: Highway LOS
L-LTF power boost doesn’t have much impact on the performance

## Slide 7: Urban Approaching LOS
L-LTF power boost doesn’t have much impact on the performance

## Slide 8: Highway NLOS
L-LTF power boost doesn’t have much impact on the performance

## Slide 9: Urban Crossing NLOS
L-LTF power boost doesn’t have much impact on the performance

## Slide 10: Simulation Settings Preamble Boost
10MHz PPDU: 11ac 20MHz DC2 + LDPC.
Pkt size: 300 bytes baseline.
Midamble
  Period – 10 symbols
  Format – Repeated 2x-Compressed (RC-LTF)
CFO: Uniform [-10 10]ppm on both Tx and Rx side.
Real carrier sensing and timing.
PER plots for Preamble Boost (STF Boost & LTF Boost)
  Preamble Boost = 0, 1, 2 ,3, 6 dB
  LTF Boost = STF Boost
  BPSK & BPSK DCM

## Slide 11: Rural LOS
L-STF power boost shows significant performance gain for BPSK-DCM
BPSK also shows some gain
3db power boost seems reasonable

## Slide 12: Highway LOS
L-STF power boost shows significant performance gain for BPSK-DCM
BPSK also shows some gain
3db power boost seems reasonable

## Slide 13: Urban Approaching LOS
L-STF power boost shows significant performance gain for BPSK-DCM
BPSK also shows some gain
3db power boost seems reasonable

## Slide 14: Highway NLOS
L-STF power boost shows significant performance gain for BPSK-DCM
BPSK also shows some gain
3db power boost seems reasonable

## Slide 15: Urban Crossing NLOS
L-STF power boost shows significant performance gain for BPSK-DCM
BPSK also shows some gain
3db power boost seems reasonable

## Slide 16: Simulation Settings Autodetection performance using RL-SIG
10MHz PPDU: 11ac 20MHz DC2 + LDPC.
Pkt size: 300 bytes baseline.
Midamble
  Period – 10 symbols
  Format – Repeated 2x-Compressed (RC-LTF)
CFO: Uniform [-10 10]ppm on both Tx and Rx side.
Ideal Timing
P_error plots
  Missed RL-SIG detection (repetition check)
  RL-SIG PER
  Data PER

## Slide 17: Rural LOS

## Slide 18: Highway LOS

## Slide 19: Urban Approaching LOS

## Slide 20: Highway NLOS

## Slide 21: Urban Crossing NLOS

## Slide 22: Discussions
Preamble power boost:
  L-STF power boost shows most gain up to 3dB.
  L-LTF power boost does not show much improvement.
  Better keep the same power from L-STF to L-LTF to maintain the same preamble detection behavior with existing scheme in 11p products.
  x1 = 3dB and x2 = 3dB is a good combination
RL-SIG autodetection:
  Performance is sufficiently good, so no extra preamble pattern is needed.

## Slide 23: Reference
[1] Bo Sun and etc., “802.11 NGV SG Proposed PAR”, IEEE 802.11-18/0861r9.
[2] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016r0.
[3] Dongguk Lim and etc., “Consideration on Features for 11bd”, 802.11-19/0009r0.

## Slide 24: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “11bd L-STF shall be boosted by 3dB when NGV data portion is modulated with BPSK.”
  “11bd L-LTF shall be boosted by 3dB when NGV data portion is modulated with BPSK.”
Y:
N:
A: