## Slide 1
Study on 20MHz Channel Access Schemes: follow-up
Date: 2019-09-17
Authors:

## Slide 2: Introduction
In SFD [1], the format of 20MHz 11bd PPDU is defined, and the channel access procedure for 20MHz transmission has been discussed [2], [3], [4]
  The access mechanism has to consider the fairness with the traffic in the secondary channel
The discussed mechanism includes:
  Whether to use the fallback operation
  Exact the channel access method
    May include 10MHz/20MHz sensing
    Considering the fairness issue
In this contribution, we further discuss the possible channel access methods and investigate the effects to traffics in secondary channel of each channel access method

## Slide 3: Recap: channel access methods for 20MHz
The baseline wide-band channel access
  Contention processed on the primary channel
  The CS for PIFS on the secondary channel
The channel access method based on baseline
As previously discussed, the fairness issue may occur
  The 20MHz enabled frame only senses for PIFS, when the traffic in secondary channel senses AIFS (+backoff when the busy channel detected)

## Slide 4: Consideration of enabling fallback options
The baseline approach with 10MHz fallback transmission may cause the strong adjacent channel [3]
  In legacy 10MHz PPDU transmission, adjacent channel interference may occur by statistically, because of no sensing in other channels
  Transmitting the 10MHz fallbacks after the busy indication of secondary channel may cause the adjacent channel interference with high probability, because it disregards the potential effects of adjacent channel interference
    May affect the signal quality of the 10MHz fallback PPDU and 10MHz PPDU in secondary channel
The 10MHz fallback procedure may cause severe congestion on the primary channel
  Because of more airtime (about 2 times) of 10MHz fallback PPDU in primary channel than 20MHz PPDU
The decision of using fallback mechanism should be carefully considered

## Slide 5: 20MHz channel access without fallback procedure from baseline
Basic AIFS: 20MHz channel access based on baseline wide-band channel access
  The channel sensing processed in one channel, and the AIFS CS in the other channel
  A new backoff procedure is initiated in case of channel busy indicated in the secondary channel during the AIFS period before the expiration of the backoff in the primary channel

## Slide 6: For backoff operation on secondary channel: receiver capability
The sensing and backoff procedure in both of primary and secondary channel may relieve the fairness issue
When one receiver/decoder is implemented in a STA, PD is not available for both of the channels
Suggested PD+ED sensing in primary channel and only ED in secondary channel.
  The carrier sensing operation is done in primary channel, as in the baseline
  Only ED operation is applied to the secondary channel

## Slide 7: Proposed 20MHz channel access without the fallback procedure
All backoff: the backoff procedure for both 10MHz band
  Using the single counter, the counter value is decreased at the end of each slot when:
    Carrier sensing result in primary channel indicates channel idle
    PHY CCA check in the secondary channel indicates channel idle

## Slide 8: The concept of EIFS: baseline
In the baseline, STA senses for EIFS before start/resuming the backoff in case of reception failure of the frame
  It provides the enough time for transmitter of STA to receive the ACK frame

## Slide 9: Decision of sensing period in secondary channel
The backoff procedure only with ED has not been defined
  If the AIFS sensing period is used in every busy indication caused by ED sensing, the following issue may occur:
    The severe hidden node problem will be occur in case of unicast frame transmission
    The fairness issue occurs for secondary channel in reception error of the frame
      11p devices sense during EIFS period
      20MHz channel access senses during AIFS period (because of no trial of decoding)
  Therefore, for busy indication in ED sensing, EIFS period ensures the fairness with the secondary channel

## Slide 10: Proposed 20MHz channel access without fallback procedure
All backoff: the backoff procedure for both 10MHz band
  For busy indication in primary channel, AIFS sensing before resuming the backoff
  For busy indication in secondary channel, EIFS sensing occurs because of unavailability of decoding frame

## Slide 11: Alternative 20MHz channel access with sensing of secondary channel
Modified AIFS channel access: Start AIFS for both channels & contention in primary channel, AIFS CS of secondary channel
  For AIFS sensing before channel access,
    Carrier sensing on primary channel (Preamble Detection + Energy Detection)
    PHY CCA check on secondary channel (ED only)

## Slide 12: Investigation on the effects to secondary channel
To investigate the fairness property and performance of each method, brief simulation is performed
  Assumes the perfect channel
  AC: BE assumed
  Packet length: (500) Bytes for normal packets on each 10MHz channel, (2000) Bytes for 20MHz-enabled packets
  Number of nodes: 10 legacy STA for contention performed channel, 200 legacy STA in secondary channel, 10 to 200 STAs in the other channel and 20MHz traffic
  Traffic model: 100ms of average inter-arrival time in each channel (legacy) + 20MHz enabled traffic
Only broadcast frame is transmitted: fairness effects of EIFS is not shown in the result

## Slide 13: Investigation on the effects to secondary channel
The four types of channel access methods without fallback operation is compared:
  Basic AIFS: 20MHz channel access based on baseline wide-band channel access
  Only backoff: primary channel sensing for AIFS, and senses both channels only in backoff period
  Modified AIFS: Start AIFS for both channels & contention in one channel, AIFS CS for the other channel at the end of backoff expiration
  All backoff: PD+ED for primary channel, ED for secondary channel for all backoff period
The two metrics are considered to be compared:
  Mean access delay of frames transmitted on secondary channel: for fairness comparison
  Mean access delay of 20MHz PPDU: for performance comparison

## Slide 14: Fairness Investigation results
The mean access delay for legacy devices in the channel that contention is not applied shows the effects to the secondary channel by the 20MHz transmission
Lower is better

## Slide 15: Throughput investigation result
The mean access delay of 20MHz PPDU has decreased because of the long duration of EIFS
  Most legacy traffic on secondary channel has priority than 20MHz PPDU
Lower is better

## Slide 16: Observation
For low traffic, the fairness problem is not shown well
  Because of low probability of interference
For high traffic, the effects to the mean access delay in secondary channel by 20MHz traffic is improved with modification
  For all 20MHz sensing and modified AIFS method
The EIFS sensing of secondary channel results in throughput degradation of 20MHz PPDU, because of low priority in backoff procedure
Investigation of EIFS protection from hidden node problem has not be considered
  Further investigation may be needed

## Slide 17: Decision of enabling fallback options
The fallback operation may not be permitted because of the described issues
  Adjacent channel interference
  Larger congestion level on primary channel
However, for flexibility, the enabling the fallback might be indicated from the upper layer, considering
  When it is decided, these information may help for right decision
    Effects of adjacent channel interference
      E.g. distance of STA using the secondary channel
    Channel capacity

## Slide 18: With fallback procedure: 20 MHz access of baseline
Basic AIFS: As in the baseline, if the channel busy indicated in secondary channel during AIFS immediately preceding to the expiration of backoff counter, STA uses only 10MHz primary channel
  For Busy indication during AIFS period in secondary channel, STA does not use the channel.

## Slide 19: With fallback procedure: 20 MHz access of proposed method
All backoff procedure: when fallback is enabled, when the channel busy is indicated for secondary channel by CCA result during the backoff procedure:
  ED+PD sensing performed in primary channel for remaining backoff counter
  10MHz PPDU transmission after expiration of backoff

## Slide 20: Conclusion
Allowing the 10MHz fallback transmission should be carefully considered, with the following possible problems
  Adjacent channel interference
  Congestion issue because of long airtime of packet with many fallbacks
If we allow only 20MHz transmission, the fairness issue occurs
  Need adjustment mechanism for fairness guarantee
  The ED sensing in secondary channel may alleviate the fairness issue, but EIFS sensing may cause long access delay of 20MHz PPDU
Alternative options may be possible for 10MHz fallback transmission enabled, by the decision of upper layer
  Basic AIFS: alleviates the fairness problem for AIFS sensing on the secondary channel
  All backoff: only uses 10MHz primary channel for the busy indication for secondary channel
  Hard to compare the fairness effects, because of different congestion level with fallback operation

## Slide 21: Straw poll 1
Do you agree with the followings:
  Channel access for 20MHz is based on the sensing and backoff procedure in both 10 MHz primary and secondary channels.

## Slide 22: Straw poll 2
Do you agree with the followings:
  STA shall sense the primary 10MHz channel using preamble detection and energy detection and sense the secondary 10MHz channel using energy detection with one receiver and decoder.

## Slide 23: Straw poll 3
Do you agree to add the followings to SFD:
  Channel access for 20MHz shall use a single counter, and the counter value is decreased at the end of each slot when:
    Carrier sensing result in the primary channel indicates channel idle
    PHY CCA check in the secondary channel indicates channel idle

## Slide 24: Straw poll 4
Do you agree to add the followings to SFD:
  When channel busy is indicated in the secondary channel and the duration of channel use is not known (e.g. NAV, packet detection), channel state shall be determined to be idle for a TBD IFS (e.g., AIFS, EIFS) sensing period before it resumes the backoff procedure.
  Y/N/A=17/0/6

## Slide 25: Straw poll 5
When 10MHz fallback transmission is enabled by the upper layer and the channel busy is indicated for the secondary channel during the backoff procedure:
  Channel sensing is performed in the primary channel for the remaining backoff counter
  10MHz PPDU transmission after the expiration of backoff
  Y/N/A=4/0/17

## Slide 26: Reference
[1] IEEE 802.11-19/497r2, 802.11bd Specification Framework Document, Bahar Sadeghi (Intel)
[2] IEEE 802.11-19/366r5, 20MHz Channel Access in 11 bd, Insun Jang (LG electronics)
[3] IEEE 802.11-19/715r1, 20MHz channel usage, Onn Haran (Autotalks)
[4] IEEE 802.11-19/807r1, Consideration on 20MHz channel access in 11bd, Yongsu Gwak (KNUT)

## Slide 27: backup

## Slide 28: Results for equal traffic: 100ms mean interval
Mean access delay in legacy STAs for equal traffic in both channel
  100 STAs in primary, 100 STAs in secondary

## Slide 29: Results for equal traffic: 100ms mean interval
Mean access delay for 20MHz PPDU for equal traffic in both channel
  100 STAs in primary, 100 STAs in secondary

## Slide 30: Results for equal traffic: 50ms mean interval
Mean access delay in legacy STAs for equal traffic in both channel
  100 STAs in primary, 100 STAs in secondary

## Slide 31: Results for equal traffic: 50ms mean interval
Mean access delay for 20MHz PPDU for equal traffic in both channel
  100 STAs in primary, 100 STAs in secondary

## Slide 32: Fairness Investigation results: including low traffic
When it is applied for low traffic, fairness issue is not shown well
  Because of low traffic in all channel