## Slide 1: Further discussion for 11be preamble
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Nov. 2019

## Slide 2: Introduction
The discussion on 11be preamble was underway in previous meeting and we received the following comment when we presented 1486r1 in September meeting.
  False/Miss Detection probability for proposed preamble
To address this comment, we investigate the performance of False/Miss detection error of proposed 11be preamble in this contribution.

## Slide 3: Recap: 11be preamble
11be preamble
  Includes the RL-SIG which is equal with L-SIG.
  Includes the length field set to as mod3 = 0.
    By using the length field, 11ax and 11be can be distinguished.
  Includes the fixed information (ex., PHY identifier) for identification of 11be and future generation.
    The symbol(s) including this information locates right after RL-SIG.
    The PHY identifier is transmitted by using the common control field of EHT PPDU (ex., EHT-SIG)
L-SIG
EHT-SIG1
L-STF
L-LTF
RL-SIG
…
EHT-SIG2
Length mod 3 = 0
PHY identifier

## Slide 4: Transmission of PHY identifier (1/2)
To indicate the PPDU version (e.g., 11be and future generation) as early as possible, PHY identifier can be included in the front symbol(s) of EHT-SIG field.
  As described in [1], the EHT-SIG field can be composed of two fields, for example, EHT-SIG1* and EHT-SIG2*.
  EHT-SIG1 field includes the PHY identifier.
The EHT-SIG1 field can be composed of following two options.
  Option 1 : configured with one OFDM symbol
    It is possible to detect the PPDU format, quickly.
    Due to a lack of room for other information, we cannot transmit the various information with the PHY identifier, simultaneously.
      Except for the PHY identifier, CRC and tail bit, it may use the 9 or 13 bits
* : This is just one example and can be called by another name.

## Slide 5: Transmission of PHY identifier(2/2)
  Option 2 : configured with two OFDM symbols.
    Not only the PHY identifier but also other information, for example, TXOP, BSS color, etc., can be transmitted.
      By using the various information, we can perform the power saving.
    Due to the decoding of two symbols, the detection of PPDU format is relatively later than option 1.
  For the transmission of more information in EHT-SIG1, in both options, we can consider the short CRC bit such as 4 bit CRC which is applied to the 11ax HE-SIGA field.
  In the next slides, we investigate the false/miss detection error probability of proposed 11be preamble according to each option.

## Slide 6: Simulation parameters
BW : 20MHz
Ant_config = 1 Tx / 1Rx
Channel impairment : No ( ideal timing and No CFO)
Channel : TGnD NLoS
Tx Frame format : 11be, 11ax, 11ac, 11n, 11ba
Information bits for PHY identifier : 3bit
CRC
  4 bit (x4 +x+1)
  8 bit (x8+x2 +x+1)

## Slide 7: False/miss error probability - length field
The validity check of length field.
  For the detection of 11be, only two steps (i.e., the repetition check and content check(i.e., length mod3 =0) ) are considered.
  In this result, the performance of miss-detection is bounded at PER of combined L-SIG.
  We confirmed that it provides enough low error rate of false detection by using the length field.

## Slide 8: False/miss error probability - PHY identifier
Furthermore, the PHY identifier including the PPDU information will further help reducing false detection error after the content check.
  Option 1
  In the aspect of the false error triggering, CRC8 offers lower error probability, but CRC4 also provides the reliable performance.(i.e., false error is lower than 10^-3)

## Slide 9: False/miss error probability -PHY identifier
  Option 2
    It shows the similar trend with option 1.
    CRC4 with more information bits can provide the lower false error probability than 10^-3.

## Slide 10: Conclusion
The RL-SIG including the length field which set to the value as mod3 =0 provides the reliable performance of false detection error.
In addition, we can potentially further reduce the false detection error if we include the PHY identifier
  It gives a false error probability lower than 10^-3.
For the early indication of the PHY identifier, we can consider the EHT-Sig field composed of two fields, for example, EHT-SIG1 and EHT-SIG2.
  EHT-SIG1 can be configured with one or two OFDM symbols.
  Both options offer the low false error probability.

## Slide 11: SP1
Do you agree to incorporate the following text into the 11be SFD?
  The LENGTH field value in L-SIG set to mod3 = 0.
  Y34/N13/A1

## Slide 12: SP2
Do you agree to add the following text into the 11be SFD?
  11be shall define a field which indicates standard version (e.g., 11be and future standards) in a SIG field of 11be preamble.
  The contents of the SIG field is TBD.
  The location and size of the SIG field is TBD.
  Y48/N0/A2

## Slide 13: SP3
Do you agree to add the following text into the 11be SFD?
  The common SIG field can be composed of two signal fields encoded separately in 11be depending on PPDU format.
    This field does not include the user specific information.
    Each field includes the CRC and Tail bits
    The naming of both SIG1 and SIG2 is TBD.
  The first field of the SIG field includes the information which indicates standard version.
L-SIG
SIG1
L-STF
L-LTF
…
…
SIG2
SIG field

## Slide 14: Motion 1
Move to add the following to the spec-framework document
  PHY version identifier field shall be one of the universal fields in the EHT preamble
    Purpose is to simplify auto-detection for future 802.11 generations, i.e, value of this field is used to identify the exact PHY version (be/bf/bg.. etc) starting with 802.11be
    Size and exact location of this field is TBD

## Slide 15: Reference
[1] IEEE 802.11-19/1486r1, Further discussion for 11be preamble
[2] IEEE 802.11-19/1021r1, Preamble Design Harmonization
[3] IEEE 802.11-19/1099r1, Preamble structure in 11be
[4] IEEE 802.11-19/1142r0, Discussion on the preamble for 11be
[5] IEEE 802.11-19/1214r0, Preamble Design Consideration for 802.11be
[6] IEEE 802.11-19/1085r0, high-level-eht-preamble-structure
[7] IEEE802.11-15/0579r2, 802.11ax Preamble Design and Auto-detection

## Slide 16: Appendix

## Slide 17: Preamble Auto-Detection for legacy
Preamble for legacy

## Slide 18: RL-SIG
Assuming RL-SIG is included in 11be PPDU, 11be devices can progress the auto-detection which has been adopted in 11ax.
Auto-detection with RL-SIG
  First step : Repetition check
    As introduced in [6], multiple ways in frequency domain can be considered
  Second step : L-SIG contents check
    Parity check = OK
    Rate check = 6Mbps
    Length field (mod 3) = ?
  By MRC of L-SIG and RL-SIG, enable range extension.
Repetition check
MRC & Contents check
Legacy detection
(11n/11ac/11a)
Received PPDU
N
N
Y
11ax or 11be

## Slide 19: SP2
Do you agree that the preamble of 11be PPDU includes repeated L-SIG after L-SIG?
Y:39/N:11/A:30