## Slide 1: Non-OFDMA Tone Plan for 320MHz
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contribution [1], tone plans for 320MHz were proposed
  OFDMA tone plan: repeat the 11ax 80MHz tone plan
  Non-OFDMA tone plan: define a new RU for the contiguous bandwidth
By defining a new RU, better peak rate can be achieved
However, there are some concerns on hardware complexity due to non-consistent non-OFDMA tone plans between non-contiguous and contiguous bandwidth cases
In this contribution, a non-OFDMA tone plan which not only guarantees consistency but also improves peak rate is proposed

## Slide 3: Non-OFDMA Tone Plan (1/2)
In [1], to further increase the peak rate, the non-OFDMA tone plan below was proposed for the contiguous 320MHz bandwidth
  4068-tone RU with 16 pilots can achieve an additional 1.294Gbps (3.37%) increase in peak rate compared to 4x996-tone RU assuming MCS11, 0.8us GI and 16 SS
However, we need a different tone plan for the non-contiguous 160+160MHz bandwidth, and these two different designs can cause a hardware complexity increase
  For 160+160MHz, additional null tones at DC and edges in each 160MHz segment are required, and thus, a different tone plan needs to be defined
4068 or 4066 or …
DC: 5 or 7 or …
12 left guard
11 right guard

## Slide 4: Non-OFDMA Tone Plan (2/2)
For simplicity, a consistent non-OFDMA tone plan is proposed
  Contiguous 320MHz
  Non-contiguous 160+160MHz
  2x2020-tone RU can achieve an additional increase in peak rate compared to 4x996-tone RU
    Note that we can get further gain by decreasing the number of pilots
    Additional 1.020Gbps (2.65%) can be achieved if the number of pilots is 2x8
    In Appendix A, the residual CFO impact is shown according to the number of pilots
  Assuming 0.4us GI, 2x2020-tone RU can support more than 40Gbps (40.161Gbps) even with the same number of pilots as in 4x996-tone RU (64 pilots)
    From the market viewpoint, it could be attractive to provide more than 40Gbps by Wi-Fi
  The number of guard and DC tones need to be further studied
    12 / 11 guard tones in each 160MHz segment may be sufficient since it can meet the 11ax TX mask for 160MHz as shown in Appendix B
    5 nulls at DC in each 160MHz segment may be sufficient with DC offset calibration
Null: 5 or 7 or …
12 left guard
2x2020 or 2*2018 or …
Null: 5 or 7 or …
23 DC
11 right guard
DC: 5 or 7 or …
12 left guard
11 right guard
DC: 5 or 7 or …
12 left guard
11 right guard
2x2020 or 2x2018 or …

## Slide 5: Summary
We have proposed the non-OFDMA tone plan in 320MHz bandwidth
  It is consistent between 160+160MHz and 320MHz
  It has better peak rate than 4x996-tone RU

## Slide 6: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
  2xTBD-tone RU is used for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
    2xTBD-tone RU consists of two TBD-tone RUs
    Each TBD-tone RU composes each 160MHz segment in conjunction with null tones at center and edges
    Each 160MHz segment has no null tones except for center and edges
    The number of null tones for center and edges in each 160MHz segment are TBD
Y/N/A:

## Slide 7: Straw Poll #2
Do you agree to add the following to the TGbe SFD?
  12 and 11 null tones are used at the left and right edges in each 160MHz segment for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
Y/N/A:

## Slide 8: Straw Poll #3
Do you agree to add the following to the TGbe SFD?
  5 null tones are used at the center in each 160MHz segment for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
Y/N/A:

## Slide 9: Straw Poll #4
Do you agree to add the following to the TGbe SFD?
  2x2020-tone RU is used for the Non-OFDMA tone plan of 320/160+160 MHz PPDU as shown in slide 4
    2x2020-tone RU consists of two 2020-tone RUs
Y/N/A:

## Slide 10: References
[1] 802.11-19/1066r0 Tone Plan Discussion
[2] 802.11-00/294r0 Suggested PA Model for 802.11 HRb

## Slide 11: Appendix A
Residual CFO impact according to the number of pilot tones
  PER comparison between cases w/o CFO and w/ CFO
  CFO is randomly applied within ±20ppm which is first compensated in L-STF and L-LTF and its residual phase is tracked by using pilots
5GHz band
320MHz using 2x2020-tone RU
P8, P16, P32, P64: 8, 16, 32, 64 pilots in 2x2020-tone RU
SISO
MCS0
2000 bytes
TGnD channel
LDPC coding

## Slide 12: Appendix B
PSD for each 160MHz segment when using 2020-tone RU with 12/11 guard tones and 5 DC tones
  RAPP model is applied with p=3 and 4dB average input power backoff from 1dB compression point [2]