## Slide 1: Non-OFDMA Tone Plan for 320MHz
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contribution [1], tone plans for 320MHz were proposed
  OFDMA tone plan: repeat the 11ax 80MHz tone plan
  Non-OFDMA tone plan: define a new RU for the contiguous bandwidth
By defining a new RU, better peak rate can be achieved
However, there are some concerns on hardware complexity due to non-consistent non-OFDMA tone plans between non-contiguous and contiguous bandwidth cases
In this contribution, a non-OFDMA tone plan which not only guarantees consistency but also improves peak rate is proposed

## Slide 3: Non-OFDMA Tone Plan (1/2)
In [1], to further increase the peak rate, the non-OFDMA tone plan below was proposed for the contiguous 320MHz bandwidth
  4068-tone RU with 16 pilots can achieve an additional 1.294Gbps (3.37%) increase in peak rate compared to 4x996-tone RU assuming MCS11, 0.8us GI and 16 SS
However, we need a different tone plan for the non-contiguous 160+160MHz bandwidth, and these two different designs can cause a hardware complexity increase
  For 160+160MHz, additional null tones at DC and edges in each 160MHz segment are required, and thus, a different tone plan needs to be defined
4068 or 4066 or …
DC: 5 or 7 or …
12 left guard
11 right guard

## Slide 4: Non-OFDMA Tone Plan (2/2)
For simplicity, a consistent non-OFDMA tone plan is proposed
  Contiguous 320MHz
  Non-contiguous 160+160MHz
  2x2020-tone RU can achieve an additional increase in peak rate compared to 4x996-tone RU
    Note that we can get further gain by decreasing the number of pilots
    Additional 1.020Gbps (2.65%) can be achieved if the number of pilots is 2x8
    In Appendix A, the residual CFO impact is shown according to the number of pilots
  Assuming 0.4us GI, 2x2020-tone RU can support more than 40Gbps (40.161Gbps) even with the same number of pilots as in 4x996-tone RU (64 pilots)
    From the market viewpoint, it could be attractive to provide more than 40Gbps by Wi-Fi
  The number of guard and DC tones need to be further studied
    12 / 11 guard tones in each 160MHz segment may be sufficient since it can meet the 11ax TX mask for 160MHz as shown in Appendix B
    5 nulls at DC in each 160MHz segment may be sufficient with DC offset calibration
Null: 5 or 7 or …
12 left guard
2x2020 or 2*2018 or …
Null: 5 or 7 or …
23 DC
11 right guard
DC: 5 or 7 or …
12 left guard
11 right guard
DC: 5 or 7 or …
12 left guard
11 right guard
2x2020 or 2x2018 or …

## Slide 5: Summary
We have proposed the non-OFDMA tone plan in 320MHz bandwidth
  It is consistent between 160+160MHz and 320MHz
  It has better peak rate than 4x996-tone RU

## Slide 6: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
  A 160MHz tone plan is duplicated for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
    The 160MHz tone plan is TBD
Y/N/A:

## Slide 7: Straw Poll #2
Do you agree to add the following to the TGbe SFD?
  12 and 11 null tones are used at the left and right edges in each 160MHz segment for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
Y/N/A:

## Slide 8: Straw Poll #3
Do you agree to add the following to the TGbe SFD?
  5 null tones are used at the center in each 160MHz segment for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
Y/N/A:

## Slide 9: Straw Poll #4
Do you agree to add the following to the TGbe SFD?
  2x2020-tone RU is used for the Non-OFDMA tone plan of 320/160+160 MHz PPDU as shown in slide 4
    2x2020-tone RU consists of two 2020-tone RUs
Y/N/A:

## Slide 10: References
[1] 802.11-19/1066r0 Tone Plan Discussion
[2] 802.11-00/294r0 Suggested PA Model for 802.11 HRb

## Slide 11: Appendix A
Residual CFO impact according to the number of pilot tones
  PER comparison between cases w/o CFO and w/ CFO
  CFO is randomly applied within ±20ppm which is first compensated in L-STF and L-LTF and its residual phase is tracked by using pilots
5GHz band
320MHz using 2x2020-tone RU
P8, P16, P32, P64: 8, 16, 32, 64 pilots in 2x2020-tone RU
SISO
MCS0
2000 bytes
TGnD channel
LDPC coding

## Slide 12: Appendix B
PSD for each 160MHz segment when using 2020-tone RU with 12/11 guard tones and 5 DC tones
  RAPP model is applied with p=3 and 4dB average input power backoff from 1dB compression point [2]