## Slide 1: Fair Sub-Channels Access
Date: 2019-09-16
Authors:
Yossi Shaul, Autotalks

## Slide 2: Background
It was agreed to support 20MHZ operation for 11bd
11bd main advantage is co-channel coexistence with 11p
Open issue: channel access rules for 20MHZ channel assuming both 11p/11bd devices

## Slide 3: Motivation
Both 10MHz sub-channels may carry equally important legacy services
Existing WiFi operation decodes NAV in a single sub-channel
  By default, one (which one? arbitrary?) sub-channel has better protection than the other
Fair 20MHz channel access is achieved by decoding L-SIG length field in both sub-channels, without preferring one sub-channel over the other
  Implementation would require two receivers, which is undesired due to cost and complexity
  Without NAV / L-SIG length field, legacy sub-channel would have less transmission opportunities and higher hidden node collision probability
A concept of lightly-modified single-radio decoder capable of decoding L-SIG length field in both sub-channels is proposed

## Slide 4: 20MHz 11bd PPDU
  From SFD: “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.”
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG
11bd PPDU

## Slide 5: Block Diagram of 20MHz Receiver with single NAV decoding
RF
A/D
Synchronization
Cyclic shift removal
FFT
Symbol -> Data processing
NAV state machine
Equalization
Primary ch. subcarriers
Sample packet reception flow
  Baseline receiver performs preamble detection and NAV calculation on the primary channel
  Remaining of 20MHz PPDU is decoded at entire band
  Decoding of 10MHz PPDU is unnecessary if received packet belongs to a different service, as when 20MHz transmission doesn’t fallback to 10MHz

## Slide 6: Block Diagram of 20MHz Receiver with dual L-SIG packet length decoding
RF
A/D
Synchronization
Upper 10MHz
Cyclic shift removal
FFT
Symbol -> Data processing
Synchronization
Lower 10MHz
Packet length
Equalization
Lower ch. subcarriers
Upper ch. subcarriers
Upper + lower subcarriers
Sample packet reception flow
  Preamble is searched in both upper and lower sub-channels
  Packet length is extracted from L-SIG using the sub-channels that contained the preamble (sum of both sub-channels can be used when found in both)
  Receiver continues to monitor the other sub-channel after receiving L-SIG (10MHz packet isn’t decoded)
    Buffer stores L-SIG samples if sub-channel preamble was received while L-SIG of other sub-channel is decoded
L-SIG buffer

## Slide 7: Packet Flow Example
20MHz
Header
Header
Successful reception
Body
L-SIG packet length decoded
Body
L-SIG decoded (given dynamic range)
Body
Body
L-SIG buffer enables decoding of both sub-channels
Header
Header
Header
Header
Processed sub-channel
State
Upper + lower
All (upper and lower)
Lower
Upper
Lower
10MHz header
20MHz reception
Scan
10MHz header
10MHz header
10MHz header
Scan + CCA L
Scan + CCA L+U
Scan + CCA L
Scan
Scan
Received packets
Scan + CCA U
Upper
Scan + CCA L+U
Scan + CCA U

## Slide 8: Straw Poll
Do you agree to add the following text into Section 3 of SFD?
802.11bd 20MHz shall be capable to decode both 10MHz sub-channels L-SIG and to extract legacy length field
Y:
N:
A:
September 2019
Yossi Shaul, Autotalks