IEEE P802.11
Wireless LANs

| Proposed resolution to LB240 CID-1058 |
| --- |
| Date: 2019-08-27 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Qi Wang | Apple, Inc. |  |  | qi_wang2@apple.com |
| Tianyu Wu | Apple, Inc. |  |  | tianyu@apple.com |

Introduction

Introduction

This submission contains proposals to resolve LB#240 CID- 1058.

| Comments: CID Page Clause Comment Proposed change Resolution 1058 21 8.3.4.4 Table 8-4 refers to LTF_SEQUENCE. What should be the value for DMG and EDMG which don't have LTF? Add text to specify the value for DMG and EDMG which don't have LTF Revised. Incorporate the text change in 1504r0. The LTFVECTOR applies only to TB ranging and Non-TB ranging which do not operate in the 60GHz band. Therefore, the LTFVECTOR is not used by DMG/EDMG ranging, there is no need to define how it is set by DMG/EDMG STAs. |  |
| --- | --- |

Proposed 11az spec modification:

Instruction to the editor:  Add a new row in Table 8-3 of REVmd_D2.2 for the “LTF_ SEQUENCE” parameter and the related text. Delete the “LTF_SEQUENCE” parameter and the related text from Table 8-4 in 11az_D1.3.  The proposed modifications are in reference to the text in 802.11az_D1.3 and REVmd_D2.2, and are indicated by the change marks as follows:

8.3.4.3 PHY SAP service primitives parameters

Table 8-3 (PHY SAP service primitive parameters) shows the parameters used by one or more of the PHY SAP service primitives.

Table 8-3—PHY SAP service primitive parameters

| Parameter | Associated primitive | Value |
| --- | --- | --- |
| LTFVECTOR | PHY-RXLTFSEQUENCE.request | Indicate the Secure LTF Counter (#2289) to make the randomized LTF sequence used in the Non-TB sounding NDP PPDU and TB sounding NDP PPDU. The Secure LTF Counter (#2289) is defined in 9.4.2.280 (Secure LTF Parameters). |

References:

1. IEEE Draft P802.11az_D1.3, Draft standard for information technology – telecommunications and information exchange between systems – local and metropolitan area networks – specific requirements – Part 11: Wireless LAN medium access control (MAC) and physical layer (PHY) specifications, Amendment 8: Enhancements for locationing

# Text boxes

Abstract

This submission contains proposals to resolve LB#240 CID-1058.